# King Fahd University of Petroleum & Minerals

Civil Engineering Department

# CE317

# Computer Methods in CE

# Lecture 4(

# Taylor Series-Cont.

# Use of Taylor series to approximate differential operators:

There are three ways to numerically approximate the first order derivative of a function:

- 1st order forward finite difference:

Consider the 1st order Taylor series:

which yields:

which can be written as

(1)

where h is called the interval or step size.

- 1st order backward finite difference:

If we write the 1st order Taylor series backward, we get:

or:

(2)

- 1st order centered finite difference:

The formula can be obtained by adding the sides of (1) + (2) to get:

(3)

# Example:

# Use the forward, the backward and the centered difference approximations to estimate the first derivative of f(x)=e2x+1 at x=2 using a step size h=0.2.

Approximation for the second order derivatives can be derived using the following procedure:

Recall the 2nd order Taylor series:

which can be written as

or:

(4)

using (3) in (4), we can express f’’i in terms of fi-1 , fi and fi+1:

which is the second order centered finite difference. Similar procedure can be used to obtain the second order backward and forward finite differences.

Example:

Given the following data for the deflection y(x) of a beam of length L = 1m and EI = 1 N.m2, estimate the numerical value for the bending moment at the middle of the beam.

| X (mm) | 0 | 100. | 200. | 300. | 400. | 500. | 600. | 700. | 800. | 900. | 1000. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Y(x) (mm) | 0. | -2.6 | -4.9 | -5.7 | -7.9 | -8.3 | -7.7 | -5.5 | -4.8 | -2.5 | 0. |

# Footnotes

( Important: This handout is only a summery of the lecture. The student is expected to take detailed notes during the class and refer to the textbook for more examples and discussion.