Lecture No. 9 & 10

Subject:  Three Dimensional  Force Systems

Objectives of Lecture:

- To explain the equations of equilibrium of three dimensional force systems

- To explain the procedure for solving problems on equilibrium of three dimensional force systems

### Equations of Equilibrium of Three Dimensional Force Systems

For the three dimensional force system, as shown in Fig.9.1, the equations of equilibrium may be written as:

∑Fx = 0 		and		∑Fy = 0		∑Fz = 0

#### Where

∑Fx = Algebric sum of all forces along x axis

∑Fy = Algebric sum of all forces along y axis

∑Fz = Algebric sum of all forces along z axis

Procedure for Solving Problems on Equilibrium of Three Dimensional Force Systems

#### Free-Body Diagram

- Establish the x, y, z axes in any suitable orientation

- Label all the known and unknown force magnitudes and directions on the diagram

- The sense of a force having an unknown magnitude can be assumed

#### Equations of Equilibrium

#### Use  the scalar equations of equilibrium

∑Fx = 0, ∑Fy = 0, ∑Fz = 0, in case where it is easy to resolve each force into its x, y, z components

- If the three-dimensional geometry appears difficult, then first express each force as a Cartesian vector, substitute these vectors into ∑F = 0, and then set i,j,k components=0

- For a spring in the system, apply F = k s

- If the solution yields a negative result, this indicates the force, assumed in the beginning, is the reverse

Numerical Examples

- Try the solved examples from Book

(Examples 3 –5 to 3 –8, page 100 to 103)

- Unsolved Examples

3-41

Determine the magnitude of F1 required to keep the concurrent force system, as shown in Fig.9.2, in equilibrium.

Fig.9-2

3-42

Determine the magnitudes of F1, F2, and F3 for the equilibrium of the particle, as shown in Fig.9-3.

## Fig.9-3

3-46

If cable AB, as shown in Fig.9.4, is subjected to a tension of 700 N, determine the tension in cables AC and AD and the magnitude of the vertical force F.

## Fig.9-4

## 3-47

Determine the stretch in each of the two springs required to hold the 20-kg crate in the equilibrium position, as shown in Fig.9-5. Each spring has an unstretched length of 2m and a stiffness of k = 300N/m.

## Fig.9-5

## 3-49

Determine the force in each cable, as shown in Fig.9-6, needed to support the 500 lb cylinder.

# Fig.9-6

## 3-55

Determine the force acting along the axis of each of the three struts, as shown in Fig.9-7, needed to support the 500 kg block.

## Fig.9-7

## 3-62

A small peg P rests on a spring that is contained inside the smooth pipe, as shown in Fig.9-8. When the spring is compressed so that s= 0.15m, the spring exerts an upward force of 60 N on the peg. Determine the point of attachment A(x,y,0) of cord PA so that the tension in cords PB and PC equals 30N and 50N, respectively

##### Fig.9-8