Lecture No. 21 & 22

Subject:  Equilibrium of a Rigid Body (Three Dimensions)

Objectives of Lecture:

- To show how to solve rigid body (three dimensional) problems using the F.B.D. and the equations of equilibrium

21-22.1 Support Reactions of a Rigid Body in Three Dimensions

21-22.2 Equations of Equilibrium for a Rigid Body in Three Dimensions

- Vector Equations of Equilibrium

ΣF = 0, Eq. 1 ΣMO = 0, Eq. 2

Where

ΣF =vector sum of all the external forces acting on the body

ΣMO=vector sum of the couple moments and the moments of all the forces about any point O

(b)	     Scalar Equations of Equilibrium

ΣF = ΣFX i+ ΣFy j+ ΣFz k= 0

ΣFX = 0, Eq. 1 ΣFY = 0, Eq. 2 ΣFZ = 0, Eq. 3

ΣMO = ΣMX i+ ΣMy j+ ΣMz k =0

ΣMX = 0, Eq. 4 ΣMY = 0, Eq. 5 ΣMZ = 0, Eq. 6

ΣFX , ΣFY ,ΣFZ

= Algebraic sum of the external force components acting in the X, Y, and Z directions

ΣMX , ΣMY ,ΣMZ

= Algebraic sum of the moment

components about the X,Y, and Z

axes

Procedure for Analysis

- Establish the x, y,z coordinate axes in any suitable orientation

- Draw the F.B.D. of the body, showing the reactions and external forces and couple moments

- For unknown reactions or forces, assume some senses

- Apply either the vector or the scalar equilibrium equations to the free body diagrams

- Solve the equilibrium equations to get the values of unknowns

- Reverse the sense of that unknown which is found to be with negative magnitude

Numerical Examples

- Try the solved examples from Book

(Examples 5–15 to 5 –19, page 242 to 246)

- Unsolved Examples

| 5-65 Determine the x, y, z components of reaction at the ball supports B and C and the ball-and-socket A (not shown) for the uniformly loaded plate |  |
| --- | --- |

| 5-66 Determine the x, y, z components of reaction acting on the ball-and-socket at A, the reaction at the roller B, and the tension in the cord CD required for equilibrium of the plate. |  |
| --- | --- |

| 5-83 The boom is supported by a ball-and-socket joint at A and a guy wire at B. If the 5-KN loads lie in a plane, which is parallel to the x-y plane, determine the x, y, z components of reaction at A and the tension in the cable at B. |  |
| --- | --- |

| 5-85 Rod AB is supported by a ball-and-socket joint at A and a cable at B. Determine the x, y, z components of reaction at these supports if the rod is subjected to a 50-lb vertical force as shown |  |
| --- | --- |

| 5-87 Member AB is supported at B by a cable and at A by a smooth fixed square rod, which fits loosely through the square hole of the collar. If F = {20i –40j–75k}lb, determine the x, y, z components of reaction at A and the tension in the cable. |  |
| --- | --- |

| 5-90 The pole is subjected to the two forces shown. Determine the components of reaction at A assuming it to be a ball-and-socket joint. Also, compute the tension in each of the guy wires, BC and ED. |  |
| --- | --- |