# CE317 : Computer Methods in Civil Engineering

Lecture 16(:Curve Fitting- Interpolation

Interpolation is another type of curve fitting. How is different from least squares?

Suppose we have some accurate data, say:

| x | f(x) |
| --- | --- |
| 2 | 22 |
| 4 | 80 |
| 6 | 140 |
| 8 | 140 |
| 10 | 60 |

If we want to determine the value f (5.25), we can linearly interpolate between the two data points {4,80} and {6,140}:

How about if we want to obtain f ( 7)? Is linear interpolating ok? Why?

So we need to do a higher order interpolation, say quadratic (2nd order polynomial) interpolation. 2nd order interpolation requires 3 points. One possibility is to use the data points {4,80},{6,140} and {8,140}. The other possibility is to use the data points {6,140},{8,140} and {10,60}. How are you going to interpolate through each 3 data points?

Procedure to fit a 2nd order polynomial through 3 data points

### Using {4,80},{6,140} and {8,140}

### Using {6,140},{8,140} and {10,60}

### Lagrange Interpolating Polynomials

Let us now explain a general procedure for generating 1st and higher order interpolating polynomials. Let us start with the 1st order interpolating polynomial:

| x | f (x) |
| --- | --- |
| x0 | f (x0) |
| x1 | f (x1) |

The above polynomial is known as the 1st order Lagrange interpolating polynomial. The same procedure can be followed for the 2nd order Lagrange interpolating polynomial:

| x | f (x) |
| --- | --- |
| x0 | f (x0) |
| x1 | f (x1) |
| x2 | f (x2) |

It can be shown that for the 3rd  order polynomials we have:

and so on for higher order polynomials.

# Example

Given the data:

| x | 1 | 2 | 3 | 5 | 6 |
| --- | --- | --- | --- | --- | --- |
| f(x) | 4.75 | 4 | 5.25 | 19.75 | 36 |

Calculate f(4) using 1st, 2nd, and 3rd order Lagrange interpolating polynomials

## Solution

- 1st order Lagrange interpolating polynomial:

2nd  order Lagrange interpolating polynomial:

3rd  order Lagrange interpolating polynomial:

# Footnotes

( Important: This handout is only a summery of the lecture. The student should take detailed notes during the class and refer to the textbook for more examples and discussion.