بسم الله الرحمن الرحيم

King Fahd University of Petroleum & Minerals

### DEPARTMENT OF CIVIL ENGINEERING

Second Semester 2001-2002 (012)

ENGINEERING MECHANICS - STATICS

## CE 201

##### First Major Exam

#### Date: March 04, 2002		         7:30 p.m.	  	       Time allowed: 1 ½ hours

Name: ……………………………          Number: …………………      e-mail: ...……..…………

Circle the Section: 02; 03.

Summary of Performance

| Problem | Full Mark | Score |
| --- | --- | --- |
| 1 | 1.1 | 10 |  |
|  | 1.2 | 10 |  |
|  | 1.3 | 10 |  |
| 2 | 20 |  |
| 3 | 30 |  |
| 4 | 20 |  |
| Total | 100 |  |

# Instructor:  Dr. Saeid A. Alghamdi

Remarks: ………………………………………………………………………………………………………………………………………………………………………………………………………………

Problem 1:

  - Draw clear separate FBDs of the ball, the pulley and the crate for the assembly shown in Fig. 1.1 assuming the crate has a mass of 40 kg.

Hint: Assume the force between ball and surface is normal to the surface, and the pulley has a vertical and a horizontal force at its center but its weight is negligible.

Fig. 1.1:

1.2 A flowerpot is supported by two cables as shown in Fig. 1.2. If the tension in cable AC is 60 lbs, determine the weight of the flowerpot.

Fig. 1.2:

1.3 A body is subjected to two forces as shown in Fig. 1.3. Determine the resultant vector R if the angle between the directions of  F1 and F2  is 600.

Fig. 1.3:

Problem 2:

The frame shown in Fig. 2 carries a force of 500 lbs at joint A. If it is known that FAC is 300 lbs, determine the force FAB  and the angle 

Hint: use the parallelogram construction to resolve F along AC and AB.

Fig. 2:

Problem 3:

A scale is constructed using a 10-kg mass A, a 2-kg pan P, and the pulley C and cord BCA arrangements shown in Fig. 3. If the cable BCA has a length of 2.0 m, and s = 0.80 m, determine the mass MD.

Hint: total mass at the pan is Mpan  + MD.

Fig. 3:

Problem 4:

A steel cylinder is supported by a boom OA and a cable AB as shown in Fig. 4. If the force in the cable is 80 N, use the vectors’ dot product definition to:

a) determine the angle between AB and AO;

b) determine the component of FAB  along boom AO.

Note: end A is in the xy plane.

Fig. 4:

# Text boxes

pulley

crate

ball

F1 = 40 kN

F2 = 100 kN

FBD at B

FAB