بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

STRUCTURAL MECHANICS I

CE 203- 032

## QUIZ NO. 3 - Take home

Axial deformations; Thermal Stresses; Generalized Hooke’s Law.

Tuesday, April 06, 2004

- A steel cubic piece is placed inside a rigid enclosure as shown below in Fig. P-1. The temperature is increased by 300 C. Compute the resulting stresses if the cube is free to expand only in the z- direction. Assume E=200 GPa, v= 0.30; x /0C.

- The steel bar ABC has original diameter cm and is sbjected to two axial forces as shown  in Fig. P-2.

- Plot the normal stress ditribution MPa.

- Compute the relative movement of c/s at B with respect to the c/s at C: B/C.

- Compute the final length of the bar if E=200 GPa.

- Determine the new minimum diameter of the bar if  v = 0.30.

# Text boxes

2 m

1 m

z-axis

Fig. P-1:

400 kN

200 kN

A

B

C

Fig. P-2: