Structural Mechanics I

CE  203

Summary of lectures 9-11: Axial Deformations (Mechanical & Thermal)

Axial Deformation:  it may be elongation (+ve) or contractions (-ve), and is always accompanied by

lateral deformations (-ve or +ve). Axial deformation is designated as a and lateral deformation is designated as  l. The deformations are mechanical and/or thermal.

Mechanical Displacements and Deformations: Displacements (u+du) and (u) will give axial deformation d(lthe difference du. The axial strain du/dx0.

uf  = u0 + ∫xdx=∫x)/[A(x).E(x)] dx

= uo + NL/AE.

is valid for a uniform bar segment with all values constant.

Otherwise,  lmech =uf  - u0 = Ni Li/Ai Ei.

# Thermal Deformations: lther= lwhereis a coefficient of thermal expansion for a given material.

Total Deformations: ltot = lmech + lther.=NsLs/AsEs + ls

# Axial Deformations: Combined Mechanical/Thermal Problems

The solution is based on using a FBD and the method of superposition (linear addition) such that for:

- Statically determinate problems:

  - Use the equations of statics equilibrium to determine the normal force Ns in each segment.

  - The equation of deformation is written such that: TOTAL axial deformation at a point = mechanical deformation + thermal deformation.

- Statically in-determinate problems:

  - Write the equations of statics equilibrium to determine the normal forces. The equations are not enough to determine the unknowns.

  - Assume a FINAL position of deformation that does NOT violate the conditions of the problem supports and geometry.

  - Write the equation of deformation in terms of the normal forces and based on the initial and final position assumed. The equation is called the “ compatibility Equation”.

  - Solve the equations from steps 1 and 3 simultaneously to obtain all Ns, all reactions and all deformations.

- Typical Problem With Mechanical and Thermal Effects: Due to temperature rise T and applied load P. If supports are rigid: l tot = l mech + l ther = 0.  The bar will be studied using two uniform segments of lengths L1, and L2.

Equilibrium equation:  AX + BX = 100 kN   … (1)

Compatibility equation:

l tot = l mech + l ther = 0

(N1L1/A1E1)+ (N2L2/A2E2)

+ l1+l2=0.

… (2)

Solve equations 1 and 2 simultaneously...

The following examples illustrate the procedure of solving statically determinate or indeterminate problems of axially loaded bars with or without thermal effects.

Note

Note: Here the problem does not have applied forces P, but after the gap closes there will N forces caused by rigid support reactions. Therefore Ns = NA = Bx = - 

# Text boxes

A

L2

L1

u

u+du

dx0

P

T =Tf – T0 > 0

B

Ax

Bx

P=100 kN

N1=Ax

N2= -Bx

N1=Ax

Ax

N2

Bx

Properties Table

## Gap

Determine T that leads to sa ksi if right support can move only gmm

A

B

Bx

Ax

steel

aluminum