Structural Mechanics I

CE  203-KFUPM-021

Summary of lecture 21                                                Torsion of Solid Non-circular Shafts

Angular Deformations: The study of kinematics (geometry) of deformations leads to the relationships between angle of twist x) and shear strain (x).

The main difference between the deformations of circular shafts and non-circular shafts is the presence of axial deformations in non-circular shafts. The axial displacement function u(x) leads to axial strains x) and the function is termed Warping Function.

The warping effects on non-circular shafts are clarified by the deformed shape shown in Fig. 1 shown below for a shaft under pure torsion.

The relationships between Tint to shear stress  and angle of twist per unit length ddx  for non-circular shafts are obtained from the mathematical theory of elasticity through the solution for  a stress function using differential equations.

The following notes will summarize the final results obtained from the theory of elasticity for the solution of the torsion problem for non-circular section.

Fig. 1:  Warping of a shaft with square cross section.

# Text boxes

andare functions of  cross section aspect ratio b/a