بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

STRUCTURAL MECHANICS I

CE 203-02 031

## QUIZ NO.4 - Take home

Analysis of Torsion stresses and deformations in Shafts

Pick-up date: 11/10/2003 12:16:27 AM

Due date: Class time Novemebr 12, 2003.

Note: There is a bonus for honest and tidy work!

ِA hollow tubular (circular) steel shaft of meam diameter do and thickness t =10 mm drives a wind turbine that is producing a power of 7 kW at an angular speed of 5000 rev./minute with full 100% effciency (i.e no power is lost). If it is known that the allowable shear stress is all = 50 MPa, determine:

- the required do using the exact theory of torsion;

- the relative angular deformation if the shaft is 40 cm long with G = 80 GPa (using the approximate theory of torsion).

# Text boxes

Name: ______________________

ID. No.:

_____________________

This is my own independent work:

Signature:  ___________________

Score:      /40

do