بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

STRUCTURAL MECHANICS I

CE 203 -031

## QUIZ NO. 7 & 8 (Take-home BUT independent work is expected)

Compound stresses and stress transformations			 		Monday, January 5, 2004

- Consider the beam shown in the Figure below. It is subjected to axial force in addition to the actions of shear forces and bending moments (obtained from the SFD and BMD: see the previous quiz!).

- Draw the plane state of compound stresses at x = 4 m from left support (at point on the centroid of the cross section).

- Use the state of stress in part 2 (above) to draw Mohr's circle and obtain the principal shear stresses with associated normal stress  and show them on a properly oriented element..

# Text boxes

50 kN

Cross section

50 cm x 200 cm

25kN/m

6 m

4 m

20 kN

100kN