بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

STRUCTURAL MECHANICS I

CE 203 -042

## QUIZZ NO. 9 (Take-home BUT independent)

Compound Stresses and Stress Transformations 		                                         Due Date: January 3, 2005

Study the following cantilever bar with the cross section of 10 cm x 20 cm where the force F is written as a vector:

- Compute all internal reactions on the fixed end and show them in the right directions as required for equilibrium.

- Compute the maximum normal and shear stresses on the c/s at the fixed end, and show them on the stress cube.

- Use Mohr's circle to determine the principal shear stresses for point A and show them on a properly oriented element.

# Text boxes

A

z

10 cm

y

Fixed end

z

y

x

4 m

F = 30 i – 40 j + 12 k  (kN)

Applied at the center of the c/s at the right end.