The following notes summarize the key issues introduced in lectures 37-40. The issues stressed in these lectures are devoted to the analysis of problems involving static dry friction force on a dry surface.

- The friction force created on a rough surface is denoted Ff. The magnitude of this force depends on the conditions of equilibrium as shown in Fig. 1 below.

Fig. 1: Values of Ff.

- In static problems Ff can NOT be more than s N. The vale of Ff might be less than the limiting value.

The solution steps of problems involving static dry friction are:

- Draw the FBDs.

- Write the equations of equilibrium in the simplest form possible including Ff. If the motion is impending (i.e. the body is on the verge of motion) set Ff = Fs = s N.

- Utilize relationships of geometry if available.

- Identify the unknowns and solve the resulting equations for the unknowns. Here you must be careful with solution steps.

The following two examples will summarize the key steps indicated above.

# Text boxes

Ff

W

N

P

Ff

s N

Static equilibrium

Dynamic equilibrium

sin 