بسم الله الرحمن الرحيم

DEPARTMENT OF CIVIL ENGINEERING

ENGINEERING MECHANICS: STATICS

CE 201-012

## QUIZ NO. 2 – Sections 02 & 03

Position Vector; Dot Product; Force along a Line     Wednesday, Feb. 13, ‘02

- Use the figure shown below to explain the physical meaning of the dot product of force F1 and vector u12. (F1 . u12 = ……)

- If a force F= 20 i + 30 j – 40 k  (kN): 1) plot the force vector and the line on a right hand coordinate system; 2) find the component of F along line that joins two points given by two locations (1,1,-1) m,  and (0,0,1) m.

# Text boxes

t

2

1

u12

F1