Safety Assessment in the Built Environment of Saudi Arabia

by Osama Jannadi 1 and Sadi Assaf 2

Abstract: This paper assesses the safety procedures on a construction job site in Saudi Arabia. Safety on the construction site was assessed by conducting a survey of projects during construction. A standardized checklist was used to conduct the survey. This checklist included those items which are perceived to be important from the safety point of view.  These are fire prevention, scaffold/mobile tower, cartridge operated tools, trenching & excavation, housekeeping, sandblasting, power tool machine & equipment, heavy equipment, gas/electric welding, construction formwork, health & welfare, transportation, cranes & lifting devices, compressed gas, air compressors, site safety administration, temporary electricity supplies, and special items.  The sites for the study were selected randomly from the Eastern province of Saudi Arabia. The sites were differentiated into large and small projects based on the size, dollar volume and number of workmen employed on the job-site. This was done to test whether the level of safety on a construction site was a function of the size of a project. The results of the study indicated that safety levels varied between the large and small projects. Small projects averaged low safety assessment scores in fire prevention, health and welfare, and safety administration, while safety assessment scores in large project were consistently high in all different divisions.  A Spearman Rho rank correlation of the different divisions was computed and a test of hypothesis was conducted.  It was found that both large and small projects generally agree on the ranks of the divisions although they have different safety standards.

____________________________________________________________________

1 Assoc. Prof. And Chairman, Dept. of Construction Engrg and Mgmt, College of Environmental Design, Box # 1978, King Fahd University of Petroleum & Minerals, Dhahran 31261, Saudi Arabia, E-Mail: jannadi@dpc.kfupm.edu.sa

2 Assoc. Prof., Dept. of Construction Engrg and Mgmt, College of Environmental Design,

Box # 680, King Fahd University of Petroleum & Minerals, Dhahran 31261, Saudi Arabia

Introduction

Safety on the jobsite is an important aspect of the overall safety in construction.  Construction sites are in a constant state of change, dictating frequent inspections. The construction field is one of the most hazardous industrial fields (Grimaldi and Simonds, 1984). The practice of safety in construction in the United States is regulated by governmental agencies such as the Occupational Safety and Health Administration (OSHA), which provides strict rules and regulations to enforce safety and health standards on jobsites. However, the practice of safety in Saudi Arabia is not regulated by any government agency as is the case in the United States (Fullman, 1984). The prevention of accidents is, therefore, an area of responsibility of the top management of the organization.  Some construction companies realize the importance of reducing their accident rates not only for humanitarian reasons, but also because of the many financial benefits which flow from the safe conduct of the work.  Other companies do not have a strong belief in safety. This has serious repercussions when any unfortunate incidents occur. Good management should always insist that every engineer, supervisor, and laborer must be familiar with all basic safety aspects and practices that guard those around the sites from accidents and injuries.

The responsibility for safety on any construction project should be shared between all the parties involved in the project, namely, the owner, the designer or the architect, and the contractor. The owner as part of his safety responsibilities must ensure that the designer designs a safe project. He must also ensure that the contractor has a safety program. The owner should include the safety program as an element of the bidding technicalities. The architect or the designer contributes towards ensuring the safety of the project by properly designing the temporary work and the permanent work from the safety point of view. The temporary works must be designed so that they provide a safe means of access to and about the construction work. The permanent work must be designed so that it is stable and safe for the users. Contractors should provide a safe environment for workers by meeting all safety requirements during construction processes, beginning with site preparation and ending with completion of the work.

The safety performance of the company should be measured so that unsafe conditions and unsafe practices can be identified. There are several methods of measuring the safety performance on a job site.  One way is by conducting a safety audit. A comprehensive audit is basically a revision of all aspects of the company's safety program. A properly conducted safety audit will determine the strengths and weaknesses of the current safety program. Any problem areas that might adversely affect the success of the program will be identified (Kavianian and Wentz, 1990).  Another way of measuring safety performance is by applying the concept of profiling which consists of the development of a corporate safety performance standard in a number of categories that are considered to be important.  Companies are then compared to this standard and a profile is made showing this comparison (Fletcher, 1972). The injury frequency rate which is the number of lost-time injuries per million man hours of exposure can also be used to measure safety performance.   Jannadi and Al-Sudairi (1995) measured safety performance in Saudi Arabia using the injury frequency rate, and concluded that safety performance is best in the larger construction firms.  Safety performance can also be measured by using a standard checklist that covers all aspects of the work (Saudi Aramco, 1988).

Safety management is an approach aiming to remove or minimize the forces which cause losses by injuring the workers, or by damaging equipment and facilities. There are two models which study the causation of accidents. These are the behavioral and the situational models (Raouf and Dhillon, 1994). The behavioral models consider humans as the major factor, responsible for accidents, whereas situational models consider the interactions between humans, environment, and the situation for studying the accident process. The causes of accidents are divided into two categories, immediate causes and contributing causes. The contributing causes of accidents include the physical condition of the workers and the management policies. The immediate causes of accidents include unsafe acts and unsafe conditions. Unsafe conditions are physical conditions, which if left uncorrected, are likely to cause an accident. Therefore, to improve safety on the work site, such conditions must be detected before an accident occurs. Unsafe conditions are detected on a work site by performing periodic safety inspections. These are usually conducted by the site safety personnel. Check lists are used to conduct such inspections. One such checklist is used to conduct this survey. This checklist tries to assess the safety of the site by considering only the unsafe conditions on the work site.

Objective of the paper

The objective of this paper is to assess the level of safety practiced at different construction projects in Saudi Arabia. A survey of different construction sites was conducted, to determine whether safety levels differ according to the size of the project.  A standard checklist was used to assess the safety practices of the different firms.

Research Methodology

A survey of 14 randomly selected projects was conducted to assess safety practices in Saudi Arabia. The sites were located in the Eastern province of Saudi Arabia. A standard checklist developed by the Saudi Arabian Oil Company (Saudi Aramco) for evaluation of safety was used in this survey (Saudi Aramco, 1988).

The projects for the survey were selected at random, based on the fact that they were under construction at the time of the survey. The survey included two types of projects: i) large construction projects with estimated construction costs of over SR 50 millions (1 US $ = 3.75 SR); and ii) small construction projects with estimated construction costs of less than SR 5 million. There were 7 large projects and 7 small projects in all. The large projects included several office and commercial buildings. The small construction sites consisted mainly of  residential buildings and housing.

The checklist used for the survey is  shown in Table 1. This checklist includes those items which are perceived to be important from the safety point of view on the construction site. The checklist consists of 18 divisions and 96 items distributed among the different divisions. These are fire prevention, scaffold/mobile tower, cartridge operated tools, trenching excavation, housekeeping, sandblasting, power tool machine & equipment, heavy equipment, gas/electric welding, construction formwork, health & welfare, transportation, cranes & lifting devices, compressed gas, air compressors, site safety administration, temporary electric, and special items. This checklist was developed by the Saudi Aramco.  Saudi Aramco is an oil company considered to be one of the biggest in the world, with oil production averaging 8 million barrels per day. Saudi Aramco is a safety oriented oil company that applies both quantitative and qualitative risk evaluation techniques to its operating facilities. Safety is monitored by conducting various safety inspections and reviews. In 1994, the numbers of both the planned quarterly safety inspections and the unscheduled inspections of the operating facilities and construction sites were 4,897 and 13,940 respectively.  Also safety is actively promoted within Saudi Aramco through a wide range of publications, films and other media. Over 2.2 million safety awareness items were produced in 1994 (Saudi Aramco, 1995). The above checklist is used by Saudi Aramco to assess the safety on the construction projects undertaken by them.

The data was collected by a student of the authors. All sites were personally visited by the surveyor and the evaluations were made with the help of the project superintendent at the respective sites.

Table 1.  Safety checklist

Divisions

Yes / No

Divisions

Yes / No

| (1) Fire Prevention |  | (2) Housekeeping |  |
| --- | --- | --- | --- |

Adequate Fire Extinguisher

Proper type Extinguisher

Adequate Water Barrels /Buckets

Properly located

Emergency tel. # posted

Fire  Watches

Open Flame Operations

Storage of Flammable /combustibles

Average Score

*

Site Access Roads

Security Fences/Gates

Site Access Signs

Trash Container

Daily Clean-up

Materials Stacking

Aisleways

Old Timber Denailed

Overall Condition

| Average Score |
| --- |
|  | (3) Scaffold/Mobile Tower |
| (4) Sandblasting |

Planking

Wheel Locks

Using Proper Wheel/Condition

Scaffold Access

Proper Couplers

Good ties/Outriggers

Plumb and Level

Condition of frame members

Average Score

Operator's Hood (Air Supply)

Air Filter (to hood)

Hoses  properly grounded

Operator's protective clothing

Remote area/warning signs

| Average Score |
| --- |
|  | (5) Cartridge Operated Tools |
| (6) Power Tools / Machine and Equipment |

Penetration to safe zone

Control/Storage of cartridges

Proper maintenance of tools

Certified operator

Operator Protective Equipment

Average Score

Properly guarded

Tool Rest

Operator's Protective Equipment

Damaged hand tools

| Average Score |
| --- |
|  | (7) Excavation |
| (8) Heavy Equipment |

Shoving /Trench Box

Sloping

Barriers/Warning Signs/Lights

Access/Egress

Average Score

Roll Over Protection

Back-up Alarms

Licensed Operators

| Average Score |
| --- |
|  | (9) Concrete Formwork |
| (10) Gas/Electric Welding |

Timber Adequate Strength

Protective Clothing & Equipt.

Firm Footing for Support

Side Slope Bracing

Average Score

Proper Acetylene Press

Acetylene on/off Wrench

Operator's Protective Equip.

Average Score

Divisions

Yes / No

Divisions

Yes / No

(11) Health and Welfare

(12) Compressed Gas

Medical Facilities/Supplies

Designated Smoking Areas

Washing Facilities

Drinking Water and Cups

Toilet Facilities/Sanitation

Ventilation

Average Score

Cylinder Secured

Proper Storage

Protective Caps in place

Proper Handling

Proper Color Coding

| Average Score |
| --- |
|  | (13) Transportation |
| (14) Air Compressors |

Buses/Pickup Trucks/Other

Vehicles

Use of Seat Belts

Licensed Operators

Proper Maintenance

Average Score

Inspection for Press Relief

Valve Operational

Inspection for Air Press

Gauges

Proper Hose & Connection

Coupling Safety Wired

Guards

| Average Score |
| --- |
|  | (15) Cranes & Lifting Devices |
| (16) Safety Administration |

Current  Inspection Sticker

Saudi Arab Licensed Operator

Load Radius Indicator

Safety Latches (Hooks)

Maintenance of Wire Ropes

Maintenance of Slings & Chain

Safe Load Chart (Arabic/Eng.)

Two Blocks

Proper Use of Outriggers

Signal man/Rigger

Average Score

Accidents Report

Safety Coordinator

Fire/Safety Inspection Log

Site Safety Program

Work Permits Requirements

on Site

Safety Inspection Reports

Fire Aid, Accident, Fatalities

| Average Score |
| --- |
|  | (17) Temporary Electric |
| (18) Special Items |

Correct Voltage

GFI (used)

Circuit 3 Wire Ground

Inspection for Recapt/Plugs

Service Panel Fused

Warning Signs

Hold Tags and Lock Out

Average Score

Average Score

Limitations

Safety on the construction sites is divided into two aspects. They are the physical aspects and the behavioral aspect. The physical aspects of safety on the construction sites covers the unsafe work conditions. The behavioral aspects of safety cover the unsafe acts or behavior on the part of the workers on the site. This paper concentrates only on the physical conditions on the site. The behavioral aspects are not covered. Hence the checklist used for this survey covers only those dimensions of safety which come under the domain of physical conditions.

Data Analysis

Each item within a division was evaluated as "yes" or "no" depending on its existence in the jobsite.  Each "yes" was given a score of 100 and each "no" was given a score of zero.  The division score was calculated by the following equation:

The division score was calculated by multiplying the number of "yes" by 100 and the total sum divided by the number of applicable items.  Items not applicable for a particular project were ignored and not used in the calculation.  Each project was scored by obtaining the average of the applicable division scores within that project.

Projects were assessed based on the following scale:

0%-59% as poor

60%-69% as fair

70%-79% as good

80%-89% as very good

90%-100% as excellent.

Also the average of division scores was calculated for both small and large projects and ranked according to their safety score as shown in Table 5.

Results

Tables 2 and 3 show the safety levels in large and small projects respectively. The safety level in large projects is high and this could be due to the fact that most of the projects surveyed were constructed by large internationally known firms which apply their own safety code and practices.  In addition, most of these construction companies have a safety administration department as part of their organizations.

Safety assessment scores in small projects varied widely.  The maximum was 71.78% (good) and the minimum 34.43% (poor). These differences could be due to not implementing the Saudi Safety Code and the lack of set rules and regulations for contractors to follow.  All safety measures taken were at the initiative of the contractor.

Table (2):   Safety levels in large projects

| Project # | Safety Score | Rating |
| --- | --- | --- |
| 1 | 89.4 | very good |
| 2 | 87.1 | very good |
| 3 | 74.7 | good |
| 4 | 78.3 | good |
| 5 | 82.4 | very good |
| 6 | 82.6 | very good |
| 7 | 96.8 | excellent |

Table (3):   Safety levels in small projects

| Project # | Safety Score | Rating |
| --- | --- | --- |
| 8 | 51.9 | poor |
| 9 | 65.3 | fair |
| 10 | 71.8 | good |
| 11 | 42.9 | poor |
| 12 | 66.0 | fair |
| 13 | 54.3 | poor |
| 14 | 34.4 | poor |

The variance, the standard deviation, and the average safety scores of large and small projects were calculated and the results are presented in Table 4.  It is clear that the safety level in large projects is higher than the safety level in small projects. This finding is in agreement with earlier research done by Jannadi and Al-Sudairi, (1995). Also the safety level among small projects varies more, with some projects showing good scores and others having a dismal performance. The large projects, however, show a consistent level of safety.

Table 4. The average safety score, the variance, and the standard deviation of the large and small projects

|  | Variance | Standard Deviation | Average Safety Score |
| --- | --- | --- | --- |
| Large Projects | 52.45 | 7.24 | 84.55 |
| Small Projects | 908.4 | 30.14 | 65.21 |

Table 5 shows the divisions’ average scores and their ranks for large and small projects.  It can be concluded that the following divisions had low safety levels in small projects:

a.	Fire Prevention

b.	Health & Welfare

c.	Safety Administration

Table 5. Divisions’ safety average scores and ranks for large and small projects

| Large Projects | Small Projects |
| --- | --- |

Division

| # | Division | Average Score | Rank | Average Score | Rank |
| --- | --- | --- | --- | --- | --- |
| 1 | Fire Prevention | 71.43 | 17 | 0 | 16 |
| 2 | Scaffold/Mobile Tower | 93.5 | 2 | 73.1 | 9 |
| 3 | Cartridge Operated Tools | 83.3 | 10 | 86.7 | 5 |
| 4 | Trenching Excavation | 83.3 | 10 | 71.4 | 10 |
| 5 | House Keeping | 87.4 | 6 | 28.5 | 13 |
| 6 | Sandblasting | 81.7 | 12 | 94.4 | 3 |
| 7 | Power Tools Machine | 85.7 | 7 | 79.2 | 7 |
| 8 | Heavy Equipment | 90.5 | 4 | 100 | 1 |
| 9 | Gas/Electric Welding | 100 | 1 | 100 | 1 |
| 10 | Concrete Formwork | 92.9 | 3 | 83.3 | 6 |
| 11 | Health & Welfare | 75.7 | 15 | 25.2 | 14 |
| 12 | Transportation | 75 | 16 | 78.6 | 8 |
| 13 | Cranes & Lifting Devices | 80.7 | 13 | N/A | N/A |
| 14 | Compressed Gas | 88.6 | 5 | 90 | 4 |
| 15 | Air Compressor | 85.7 | 7 | 60 | 11 |
| 16 | Safety Administration | 76.2 | 14 | 20.6 | 15 |
| 17 | Temporary Electric Supply | 85.7 | 7 | 52.3 | 12 |

A Spearman Rho rank correlation coefficient, rs, of the different divisions was computed, with division number 13 ignored since it is not applicable to small projects.  The coefficient gives a numerical index of the relation between the ranks of the divisions.

6 ( D2

Spearman rank correlation coefficient, rs  = 1   -    __________

N(N2-1)

where	D = 	Difference between ranks for the same division

N = 	Number of divisions (in this case 16) (Dominowski, 1980)

6 (D2		                 6 * (317)

rs  =   1 -    __________    =   1 -  ________________      =       0.534

N(N2-1)   	            16 * {(16)2-1)}

Test of Hypothesis

A critical value of rs is needed to test the alternative hypothesis that large and small projects generally agree on the important ranking of the divisions against the null hypothesis which says that there is no association between the rank.  Using the table of critical value of Spearman's rank correlation coefficient, (Mendenhall, 1993) the critical value of rs with a = 0.05 and N = 16 is 0.425.

Since the calculated value of rs is larger than the critical value, then the null hypothesis will be rejected at the a = 0.05 level of significance. It appears that there is some agreement between the two ranks in both small and large projects.

Conclusion

This paper assesses construction safety on the job site.  It concludes that safety level in construction sites varies with the project size. Large projects constructed by large international firms have much better safety records than smaller ones. This indicates the need for implementing a safety code in Saudi Arabia to monitor and enforce safety requirements at work sites.  Also the results indicate that large projects have little variation in safety levels, while small projects have a wide variation in their safety performance.  In addition to this, small projects have very low safety assessment scores in fire prevention, health and welfare, and safety administration. A Spearman Rho rank correlation of the safety scores of the different divisions has been computed and a test of hypothesis conducted.  It is found that both large and small projects generally agree on the safety rankings of the divisions.

Acknowledgment

The writers would like to thank Mr. Al-Juaid for collecting the data for this research and the King Fahd University of Petroleum & Minerals for providing various facilities for conducting this study.

References

1. Dominowski, R. L. (1980). “Research Methods.” Prentice-Hall, Inc., Englewood Cliffs, New Jersey.

2. Fletcher, J.  (1972). “The Industrial Environment.“  Willowdale, Ontario: National Profile Ltd.

3. Fullman, P. E. (1984). “Construction Safety, Security, and Loss Prevention.” John Wiley & Sons, Inc., New York.

Grimaldi, U. V., and Simonds, R. H. (1984). “Safety Management.”  Richard, D. Irwin, Inc., Illinois.

Jannadi, M. O., and Al-Sudairi, A.(1995). “Safety Management in the Construction Industry in Saudi Arabia.” Building Research and Information, Vol. 23, No. 1, pp60-63.

6. Kavianian, H. R. and Wentz, C. A.  (1990). “Occupational and Environmental Safety Engineering and Management.“ Van Nostrand Reinhold, New York.

7. Mendenhall, W. (1993). “Introduction to Probability and Statistics.” Duxbury Press, Boston.

8. Saudi Aramco. (1988). “Saudi Aramco Construction Safety Manual.” Third Edition, Saudi Arabia.

Saudi Aramco. (1995). “Saudi Aramco 1994 Loss Control Report.” Al-Mutawa Press Co., Dammam, Saudi Arabia.

10. Raouf, A. and Dhillon, B.S. (1994), "Safety Assessment - A Quantitative Approach”.           Lewis Publishers. pp 11-14.