COE 202, Term 162

Digital Logic Design

Assignment# 1 Solution

Due date: Saturday, March 18, 2017

# Consider the combinational circuit given below which has three inputs C1, C0, and X, three outputs C1+, C0+ and Y:

## Write a Verilog model to model the combinational circuit using either primitive gates or assign statement.

module Cell3XM1 (output C1P, C0P, Y, input C1, C0, X);

assign Y = X ~^  C0;

assign C0P = C1 ^ (~X &  C0);

assign C1P = X | (C1 &  C0);

endmodule

## Write a test bench to test the correctness of your Verilog model by applying all the input patterns to the circuit. Apply consecutive inputs patterns after a delay of 100ps. Verify the correct functionality of your circuit by deriving the truth table and comparing it with what you got from simulations.

module Cell3XM1_Test();

reg C1, C0, X;

wire C1P, C0P, Y;

Cell3XM1 M1 (C1P, C0P, Y, C1, C0, X);

initial begin

C1=0; C0=0; X=0;

#100 C1=0; C0=0; X=1;

#100 C1=0; C0=1; X=0;

#100 C1=0; C0=1; X=1;

#100 C1=1; C0=0; X=0;

#100 C1=1; C0=0; X=1;

#100 C1=1; C0=1; X=0;

#100 C1=1; C0=1; X=1;

end

endmodule

The expected truth table is as follows:

| C1 | C0 | X | C1P | C0P | Y |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 |
| 1 | 0 | 0 | 0 | 1 | 1 |
| 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 1 | 1 |

The simulation waveform given below matches the expected values shown in the truth table.

## Write a Verilog model that instantiates four copies of this circuit and connects C1 and C0 of the first instance to 00, C1+ and C0+ of the first instance to C1 and C0 of the 2nd instance, C1+ and C0+ of the 2nd instance to C1 and C0 of the 3rd instance, and C1+ and C0+ of the 3rd instance to C1 and C0 of the 4th instance.

module D3XM1 (output Cout1, Cout0, output [3:0] Y, input [3:0] X);

wire  [2:0] C1P, C0P;

Cell3XM1 M1 (C1P[0], C0P[0], Y[0], 0, 0, X[0]);

Cell3XM1 M2 (C1P[1], C0P[1], Y[1], C1P[0], C0P[0], X[1]);

Cell3XM1 M3 (C1P[2], C0P[2], Y[2], C1P[1], C0P[1], X[2]);

Cell3XM1 M4 (Cout1, Cout0, Y[3], C1P[2], C0P[2], X[3]);

endmodule

## Write a test bench that tests the 4-bit circuit modeled in (iii) that applies the following input patterns to your circuit (X3X2X1X0)={0001, 0010, 0011, 0100, 0101} and observes the obtained outputs Y3Y2Y1Y0. Can you guess the functionality of the 4-bit circuit?

module D3XM1_Test();

reg [3:0] X;

wire Cout1, Cout0;

wire [3:0] Y;

D3XM1 M1 (Cout1, Cout0, Y, X);

initial begin

X=4'b0001;

#100 X=4'b0010;

#100 X=4'b0011;

#100 X=4'b0100;

#100 X=4'b0101;

end

endmodule

# The simulations results are shown below and it can be deduced from simulations that the circuit is computing the function Y=3*X-1.