COE 202, Term 142

Digital Logic Design

Assignment# 2 Solution

Due date: Tuesday, March 31

# It is required to design a combinational circuit that computes the equation Y=3*X, where X is a 4-bit unsigned number.

## Determine the number of outputs needed for your circuit.

Since the maximum input value is 15, the maximum output value is 3*15=45. Thus, we need 6 outputs.

## Derive the truth table of your circuit.

| X3 | X2 | X1 | X0 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |
| 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 |
| 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 |
| 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |
| 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |

## Derive minimized equations for your circuit using K-Map method.

Y5 = X3 X2 + X3 X1 X0

Y4 = X3' X2 X1 + X3 X2' X1' + X3 X2' X0'

Y3 = X3' X2' X1 X0 + X3' X2 X1' + X3 X2 X1 + X3 X2' X1' + X3 X1 X0'

OR

Y3 = X3' X2' X1 X0 + X3' X2 X1' + X3 X2 X1 + X3 X2' X1' + X3 X2' X0'

Y2 = X2 X1' + X2 X0 + X2' X1 X0'

Y1 = X1' X0 + X1 X0'

Y0 = X0

## Write a Verilog model for modeling your design by using an assign statement for each output.

module Times3 (output [5:0] Y, input [3:0] X);

assign Y[5] = X[3] && X[2] || X[3] && X[1] && X[0];

assign Y[4] = !X[3] && X[2] && X[1] || X[3] && !X[2] && !X[1] || X[3] && !X[2] && !X[0];

assign Y[3] = !X[3] && !X[2] && X[1] && X[0] || !X[3] && X[2] && !X[1] || X[3] && X[2] && X[1] || X[3] && !X[2] && !X[1] || X[3] && X[1] && !X[0];

assign Y[2] = X[2] && !X[1] || X[2] && X[0] || !X[2] && X[1] && !X[0];

assign Y[1] = !X[1] && X[0] || X[1] && !X[0];

assign Y[0] = X[0];

endmodule;

## Write a Verilog test bench to test the correctness of your design for the following input values: X=1, X=3, X=5, X=10 and X=15.

module t_Times3();

wire 	[5:0] Y;

reg 	[3:0] X;

Times3 M1 (Y, X);

initial begin

X=4'b0001;

#10	X=4'b0011;

#10	X=4'b0101;

#10	X=4'b1010;

#10	X=4'b1111;

end

endmodule;