COE 202, Term 162

Digital Logic Design

Assignment# 2 Solution

Due date: Sunday, April 9

# It is required to design an iterative combinational circuit that computes the equation Z=2*X-Y, where X and Y are n-bit unsigned numbers.

## Determine the number of inputs and outputs needed for your 1-bit cell.

This circuit requires the following 3 pieces of information, which can be encoded using 2 signals:

- No carry or borrow (C=0, B=0)

- Carry = 1 (C=1, B=0)

- Borrow = 1 (C=0, B=1)

## Derive the truth table of your 1-bit cell.

| Bin | Cin | X | Y | Bout | Cout | Z |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 | 0 | 1 |
| 0 | 0 | 1 | 0 | 0 | 1 | 0 |
| 0 | 0 | 1 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 0 | 1 | 1 |
| 0 | 1 | 1 | 1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 1 | 0 | 1 |
| 1 | 0 | 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 1 | 0 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 | 0 | 0 | 0 |
| 1 | 1 | 0 | 0 | X | X | X |
| 1 | 1 | 0 | 1 | X | X | X |
| 1 | 1 | 1 | 0 | X | X | X |
| 1 | 1 | 1 | 1 | X | X | X |

## Derive minimized equations for your 1-bit using K-Map method.

Z = Bin' Cin' Y + Cin Y' + Bin Y' = Bin' Cin' Y + Y' (Cin + Bin) = Y ( (Cin + Bin)

Cout = Cin X + Bin' X Y'

Bout = Bin X' + Cin' X' Y

## Write a Verilog model for modeling your 1-bit cell by using an assign statement for each output.

module Cell2XMY (output Bout, Cout, Z, input Bin, Cin, X, Y);

assign Z = Y ^  (Cin | Bin);

assign Cout = Cin & X |  ~Bin & X & ~Y;

assign Bout =  Bin & ~X | ~Cin & ~X & Y;

endmodule

## Write a Verilog model for modeling a 4-bit circuit based on the 1-bit model you have.

module D2XMY (output Bout, Cout, output [3:0] Z, input [3:0] X, Y);

wire  [2:0] C, B;

Cell2XMY M1 (B[0], C[0], Z[0], 1'b0, 1'b0, X[0], Y[0]);

Cell2XMY M2 (B[1], C[1], Z[1], B[0], C[0], X[1], Y[1]);

Cell2XMY M3 (B[2], C[2], Z[2], B[1], C[1], X[2], Y[2]);

Cell2XMY M4 (Bout, Cout, Z[3], B[2], C[2], X[3], Y[3]);

endmodule

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=1,Y=1},  {X=3, Y=2}, {X=5, Y=1}, {X=4, Y=5}, and {X=15, Y=15}.

module D2XMY_Test();

reg [3:0] X, Y;

wire Bout, Cout;

wire [3:0] Z;

D2XMY M1 (Bout, Cout, Z, X, Y);

initial begin

X=4'b0001; Y=4'b0001;

#100 X=4'b0011; Y=4'b0010;

#100 X=4'b0101; Y=4'b0001;

#100 X=4'b0100; Y=4'b0101;

#100 X=4'b1111; Y=4'b1111;

end

endmodule

# The simulations results are shown below and it is clear that the circuit is implementing the function Z=2*X-Y correctly.

# Text boxes

Y

X

Cin

Cout

Bin

Bout

Z