COE 202, Term 142

Digital Logic Design

Assignment# 3 Solution

Due date: Thursday, April 16

# It is required to design a circuit that receives two 4-bit unsigned numbers A=A3A2A1A0, B=B3B2B1B0 and produces 6-bit output C= C5C4C3C2C1C0. The circuit implements the following functions based on the values of the three selection inputs: S1, S1 and S0.

| S2 S1 S0 | Function |
| --- | --- |
| 0 0 0 | C = A + B |
| 0 0 1 | C = A - B |
| 0 1 0 | C = A + 1 |
| 0 1 1 | C = A - 1 |
| 1 0 0 | C = 2A+B |
| 1 0 1 | C = 2A-B |
| 1 1 0 | C = A+2B |
| 1 1 1 | C = A-2B |

# Show the block diagram design of your circuit using MSI components like Adder, Multiplexor, as needed. Use only one adder in your solution.

# Model your design in Verilog by modeling each component separately i.e. adder, MUX, etc. and then instantiating these components to model your circuit.

We show below the Verilog models of the various components needed in the solution:

2x1 MUX:

module mux2x1 #(parameter n=6) (input [n-1:0] a, b, input select,  output [n-1:0]  y);

assign y = (select ? a : b);

endmodule

4x1 MUX:

module mux4x1 #(parameter n=6) (input [n-1:0] a, b, c, d, input [1:0] select,  output reg [n-1:0] y);

always@(select or a or b or c or d) begin

case (select)

2'b00: y=d;

2'b01: y=c;

2'b10: y=b;

2'b11: y=a;

endcase

end

endmodule

Adder:

module adder #(parameter n = 6)

(output [n-1:0] sum, input [n-1:0] a, b, input cin);

assign  sum = a + b + cin;

endmodule

Next we show the Verilog model for the whole ALU:

module ALU #(parameter n=4) (output [n+1:0] C, input [n-1:0] A, B, input [2:0] S);

wire [n+1:0] X, Y, Z, zero;

assign zero = 0;

assign cin = !S[1] & S[0] | S[2] & S[0] | !S[2] & S[1] & !S[0];

mux2x1 M1 ({A[n-1], A,1'b0},{A[n-1],A[n-1],A}, S[2] & !S[1], X);

mux2x1 M2 ({B[n-1],B,1'b0},zero, S[2], Y);

mux4x1 M3 (~Y, Y, ~{B[n-1],B[n-1],B}, {B[n-1],B[n-1],B}, S[1:0], Z);

adder  M4 (C, X, Z, cin);

endmodule

# Write a Verilog test bench to test your design and verify its correctness by simulation. Show snapshots of your simulation to demonstrate its correctness. For each function, test at least 2 input combinations of your choice to demonstrate correct functionality.

module t_ALU();

wire 	[5:0] C;

reg 	[3:0] A,  B;

reg   [2:0] S;

ALU  M1 (C, A, B, S);

initial begin

A=4'b0100; B=4'b0111; S=3'b000;

#10	S=3'b001;

#10	S=3'b010;

#10	S=3'b011;

#10	S=3'b100;

#10	S=3'b101;

#10	S=3'b110;

#10	S=3'b111;

#10 A=4'b1111; B=4'b0011; S=3'b000;

#10	S=3'b001;

#10	S=3'b010;

#10	S=3'b011;

#10	S=3'b100;

#10	S=3'b101;

#10	S=3'b110;

#10	S=3'b111;

end

endmodule

The simulation snapshot is given below which demonstrates that the ALU is working properly: