COE 202, Term 162

Digital Logic Design

Assignment# 3 Solution

Due date: Thursday, April 27

# It is required to design a circuit that receives two 4-bit signed numbers in 2's complement representation A=A3A2A1A0, B=B3B2B1B0 and produces a 6-bit output C= C5C4C3C2C1C0. The circuit implements the following functions based on the values of the two selection inputs: S1 and S0.

| S1 S0 | Function |
| --- | --- |
| 0 0 | C = A + B |
| 0 1 | C = A - B |
| 1 0 | C = 2A + 1 |
| 1 1 | C = 2A - 1 |

# Show the block diagram design of your circuit using MSI components like Adder, Multiplexor, as needed. Use only one adder in your solution.

# Model your design in Verilog by modeling each component separately i.e. adder, MUX, etc. and then instantiating these components to model your circuit.

module adder #(parameter width = 6)

(output cout, output [width-1:0] sum,

input [width-1:0] a, b, input cin);

assign {cout, sum} = a + b + cin;

endmodule

module mux2x1 #(parameter width = 6)

(output [width-1:0] c,

input [width-1:0] a, b, input select);

assign c = (select ? a : b);

endmodule

module mux4x1 #(parameter width = 6)

(output reg [width-1:0] y,

input [width-1:0] a, b, c, d, input s1, s0);

always @(a, b, c, d, s1, s0) begin

case ({s1, s0})

2'b 00 : y = d;

2'b 01 : y = c;

2'b 10 : y = b;

2'b 11 : y = a;

endcase

end

endmodule

module ALU

(output cout, output [5:0] c,

input [3:0] a, b, input s1, s0);

wire [5:0] T1, T2;

mux2x1 M1 (T1, {a[3], a, 1'b0}, {a[3],a[3],a}, s1);

mux4x1 M2 (T2, 6'b111110, 6'b1, ~{b[3],b[3],b}, {b[3],b[3],b}, s1, s0);

adder M3 (cout, c, T1, T2, s0);

endmodule

# Write a Verilog test bench to test your design and verify its correctness by simulation. Show snapshots of your simulation to demonstrate its correctness. For each function, test at least 2 input combinations of your choice to demonstrate correct functionality.

module ALU_Test();

reg [3:0] A, B;

reg s1, s0;

wire Cout;

wire [5:0] C;

ALU  M1 (Cout, C, A, B, s1, s0);

initial begin

s1=0; s0=0; A=4'b0101; B=4'b0111;

#100 A=4'b0100; B=4'b1111;

#100 A=4'b0111; B=4'b0111;

#100 A=4'b1000; B=4'b1000;

#100 s1=0; s0=1; A=4'b0110; B=4'b0011;

#100 A=4'b1110; B=4'b1111;

#100 A=4'b1000; B=4'b0111;

#100 s1=1; s0=0; A=4'b0010;

#100 A=4'b1111;

#100 A=4'b0111;

#100 A=4'b1000;

#100 s1=1; s0=1; A=4'b0111;

#100 A=4'b1111;

#100 A=4'b1000;

end

endmodule

The test bench has been simulated and can be seen from the simulation waveform given below, the ALU is functioning correctly.