COE 202, Term 141

Digital Logic Design

Assignment# 4

Due date: Sunday, Dec. 21

# It is required to design a synchronous  sequential circuit that receives a serial input X and produces a serial output Z that computes the equation Z=3*X-2.  Assume that the inserted input values of X will be such that Z will always be positive. Assume the existence of an asynchrnous reset input to reset the machine to a reset state. The following are a set of some input and output streams:

Example:

| Input | X | 1 0 1 0 0 |
| --- | --- | --- |
| Output | Z | 1 0 1 1 0 |
| Input | X | 1 1 1 0 0 |
| Output | Z | 1 1 0 0 1 |

# Derive the state diagram of the circuit assuming a Mealy model.

# Implement your design using D flip flops with minimal number of flip flops and combinational logic.

# Model your design in logic works.

# Test your design and verify its correctness by simulation. Show snapshots of your simulation to demonstrate its correctness

This assignment can be solved based on a group of two students. Include snapshots of simulation output to illustrate the correctness of your circuit. Submit your solution as a word document along with the circuit in one zipped file.