King Fahd University of Petroleum and Minerals

College of Computer Science and Engineering

Computer Engineering Department

COE 202: Digital Logic Design (3-0-3)

Term 102 (Spring 2011)

Major Exam 1

Thursday March 17, 2011

Time: 90 minutes, Total Pages: 9

Name:________________________________ ID:______________ Section: _______

Notes:

- Do not open the exam book until instructed

- Calculators are not allowed (basic, advanced, cell phones, etc.)

- Answer all questions

- All steps must be shown

- Any assumptions made must be clearly stated

| Question | Maximum Points | Your Points |
| --- | --- | --- |
| 1 | 25 |  |
| 2 | 20 |  |
| 3 | 10 |  |
| 4 | 20 |  |
| Total | 75 |  |

Question 1.											(25  points)

Fill in the Spaces: (Show all work needed to obtain your answer)

a. The expressions

b. For the logic function F(W, X, Y, Z), minterm m5 = . _____________(True/False)

c. Counting the number of hours in one day in BCD requires a minimum of ________(how many) bits.

d. The Boolean function one literal as _______.

e. is represented in the canonical shorthand form as .                                                                         The complement

f. Assume some computer hardware that performs integer arithmetic in 5 bits. The largest decimal number that can be added to 12 without causing an incorrect result is ________.

g. The decimal value of the largest 3-bit binary fraction is __________.

h. One factor that may limit gate fan out is   _______________________________________________.

i. The largest 2-digit octal number has the decimal value_________.

j. Using gates having propagation delay of 5 ns each, the input-to-output delay for a logic circuit that directly implements the logic function XYZ + WV will be ________ ns.

k. To implement the function as a product of maxterms, we need

_________ (how many) OR gates, each having __________(how many) inputs.

l. To represent any integer greater than 1, the binary system requires the largest number of digits among all number systems __________(True/False)

m. The Hi-Z logic state becomes relevant when connecting: _______(select one)

i) Inputs of logic gates together

ii) An output of a logic gate to inputs of other logic gates

iii) Outputs of logic gates together

Question 2.											(20 Points)

- Using up to 4-bit fractional accuracy, convert (103.4375)10 to: (8 Points)

- Binary

- Octal

- Hexadecimal

- Find the result of the following operations:				(9 Points)

- (37.4)16 + (59.7)16

- (37.4)8 + (59.7)16

- (101)2 × (110)2

- (111100)2 – (100011)2

- Determine the radix r for the following case: (6A)r = (86)14		(3 Points)

Question 3.											(10  Points)

# Prove the identity of each of the following Boolean functions using algebraic manipulation. Start with the left-hand side expression and derive from it the right-hand side expression.

Question 4.											(20  Points)

- For the circuit shown, the propagation delay (in nano-seconds) for each gate is listed in the table below.       										(5 Points)

| Gate | Propagation Delay (in Nano-Seconds) |
| --- | --- |
| G1 | 1 ns |
| G2 | 1.5 ns |
| G3 | 4 ns |
| G4 | 2.5 ns |
| G5 | 2 ns |

- What is the Boolean expression of the output function F

- What is the worst case path delay for this circuit

# Express the following function in the sum of minterms form {((mi)} and the product of Maxterms form {𝚷 (Mi)}							(6 Points)

# For the Boolean function F(A, B, C, D)     (5 Points)

# Write the corresponding algebraic Boolean expression  (without simplification)

# What is the product of Maxterms form of  F  {𝚷 (Mi)}?

# Write the corresponding product of Maxterms Boolean expression  (without simplification)

# Using Boolean Algebra, put the sum of minterms function F(x, y, z) into its simplest form; where F(x, y, z)= x’ y’ z’  +  x y’ z + x’ y z’ + x’ y’z  			(4 Points)

# Footnotes

Nano = 10-9