March  25, 2006

COMPUTER ENGINEERING DEPARTMENT

COE 202

FUNDAMENTALS OF COMPUTER ENGINEERING

Major Exam I

Second Semester  (052)

Time: 7:30-9:30 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 25 |  |
| Q2 | 18 |  |
| Q3 | 12 |  |
| Q4 | 20 |  |
| Q5 | 25 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [25 Points]

# (Q1) Indicate whether the following is true or false, and if it is false correct it:

## (1) (True, False)	The hexadecimal number (421)16 is equal to the octal number (841)8.

## (True, False)	The binary number (1110.0111)2 is equal to (14.875)10 , (E.7)16 and (16.7)8.

## (True, False)	The 16`s complement of the hexadecimal number (B120)16 is (4EE0)16 while the 15`s complement is (4ED0)16.

## (True, False)	Assuming 6-bit representation of numbers, the binary number 111010 is equal to +58 in sign-magnitude representation, -5 in 1`s complement representation, and -4 in 2`s complement representation.

## (True, False)	The decimal number 2048 can be represented as an unsigned number in 11 bits.

## (True, False)	Assuming 5-bit 1`s complement representation of numbers, then 11011+01001 is equal to 00101.

## (True, False)	Assuming 6-bit 2’s complement representation, the range of numbers that can be represented is -63 to +63.

## (True, False)		Assuming 8-bit 2`s complement representation of numbers, then E6+9A produces overflow i.e. it produces incorrect result.

## (True, False)	The result of the following addition operation (AA)16 + (13)16  is  (123)16.

## (True, False)	The result of the following unsigned multiplication operation (A15)16 * (8)16  is  (50A8)16.

# [18 Points]

# (Q2) Prove the identity of each of the following Boolean functions using algebraic manipulation. Start with the left-hand side expression and derive from it the right-hand side expression. Clearly indicate the postulates and theorems used.

## (a + b)(a` + c)(b + c) = a`b + ac

## { [b` + (a + c)` + a`(c`+d)][d` + b`c`] }` = b (a + c) + d (b + c)

[12 Points]

# (Q3) Given the function F(A, B, C)= A + B` C

## (i) Determine the minterms of the function F and express it as an algebraic sum of   minterms.

## Determine the maxterms of the function F and express it as an algebraic product of maxterms.

[20 Points]

# (Q4) Consider the function F(A, B, C) = M(3, 5).

## (i)  Simplify the function into a minimal sum-of-products expression.

## (ii) Simplify the function into a minimal product-of-sums expression.

## Implement the function using only 2-input NAND gates and Inverters, with minimal number of gates. Draw the circuit diagram for your implementation.

## Implement the function using only 2-input NOR gates and Inverters, with minimal number of gates. Draw the circuit diagram for your implementation.

[25 Points]

# (Q5) Simplify the following Boolean functions F together with the don`t care conditions d, into minimal sum-of-products expressions. Identify all the prime implicants and the essential prime implicants.

## (i) F(A, B, C, D)=m(0, 6, 7, 9, 11, 13, 15), d(A, B, C, D)=m(2, 5, 8, 10)

## F(A, B, C, D, E) =m(0, 1, 2, 3, 4, 6, 10, 11, 14, 17, 18, 21, 22, 25, 26, 27, 29, 30)

# Text boxes

0

1

0

0

1

1

1

1

1

A=0

11

BC

DE

01

00

10

11

01

00

10

1

0

0

1

1

0

0

1

1

1

0

1

0

1

0

1

0

1

0

1

0

1

0

A=1

10

11

01

00

10

11

01

00

DE

BC

X

1

1

X

0

1

1

0

1

1

X

0

X

0

0

1

10

11

01

00

10

11

01

00

CD

AB