May 6, 2006

COMPUTER ENGINEERING DEPARTMENT

COE 202

FUNDAMENTALS OF COMPUTER ENGINEERING

Major Exam II

Second Semester  (052)

Time: 8:00-10:00 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 20 |  |
| Q3 | 20 |  |
| Q4 | 20 |  |
| Q5 | 20 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

# [20 Points]

# (Q1) Consider the Boolean function F(A, B, C, D)=m(0, 3, 13, 14).

## (i) Implement the function F using only 4x1 multiplexers and inverters.

## (ii) Implement the function F using only 2x4 decoders, and 2-input 	OR gates. Assume that the decoders have enable input.

# [20 Points]

(Q2)  It is required to design a 4-bit comparator that compares two 4-bit numbers A=A3A2A1A0 and B=B3B2B1B0, and produces two outputs GT and LT. If A>B, then the output signal GT is set to 1 and LT is set to 0. If A<B, then the output signal LT is set to 1, and GT is set to 0. Otherwise both signals will be set to 0, which indicates that the two numbers are equal (i.e. A=B). The 4-bit comparator circuit can be designed in a modular way as shown below:

## (i) Obtain the truth table for the 1-bit comparator bit-slice, where Ai and Bi are the 	two bits to be compared, GTi+1 and LTi+1 are the inputs from the outputs of the 	previous stage and GTi and LTi are the outputs of the current stage. Note that GTi and 	LTi  signals propagate from the most significant bit to the least significant bit.

## (ii) Show a minimized gate-level design for the 1-bit comparator bit-slice.

[20 Points]

# (Q3) It is required to design a circuit that has two 4-bit inputs A=A3A2A1A0 and B=B3B2B1B0 and one 6-bit output C= C5C4C3C2C1C0. The circuit implements the following eight functions based on the values of the three selection inputs S2, S1 and S0.

| S2 S1 S0 | Function |
| --- | --- |
| 0 0 0 | C=A + B |
| 0 0 1 | C=A - B |
| 0 1 0 | C=A+1 |
| 0 1 1 | C=A-1 |
| 1 0 0 | C=B |
| 1 0 1 | C=-B |
| 1 1 0 | C=2B |
| 1 1 1 | C=3B |

# Assume that you can use MSI components like Adder, Multiplexor, Decoder in your design as needed. Note that you only need to show the used components as blocks showing only their inputs and outputs without showing their detailed implementations.

[20 Points]

# (Q4) Given the D-latch and the rising edge-triggered D-flip flop shown below:

## (i) Complete the timing diagram given below:

## (ii) Show an implementation of the D-latch using only NAND gates and inverters.

## (iii) Show an implementation of the rising-edge triggered D-flip flop using D-latches and inverters.

[20 Points]

# (Q5) A sequential circuit has two JK flip-flops A and B, input X and one output Z. The flip-flop input equations and output function are:

# JA = B X 	KA = B 		Z = A X   B`

# JB = X  	KB = X`

## (i)  Draw the logic diagram of the circuit.

## (ii)  Obtain the state table of the circuit.

## (iii) Obtain the state diagram of the circuit.

## (iv) Is the circuit a Mealy or Moore model?

## (v) Is the input sequence {0, 0} a synchronizing sequence for the circuit? If the answer is yes, what will be the state reached after synchronization.

# Text boxes

GT0

LT1

GT1

LT

GT

B0

A0

LT1

GT1

LT2

LT3

0

GT4

GT3

LT4

GT2

LT2

GT2

LT3

GT3

LT0

0

B1

A1

B2

A2

B3

A3

QF

QL

D

CLK