COE 202, Term 162

Digital Logic Design

HW# 3

# For the Boolean function E and F, as given in the following truth table:

| X | Y | Z | E | F |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 0 |
| 0 | 0 | 1 | 1 | 0 |
| 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 1 |
| 1 | 1 | 1 | 0 | 1 |

## List the minterms and the maxterms of each function.

## List the minterms of E’ and F’.

## List the minterms of E + F and E . F.

## Express E and F in sum-of-minterms algebraic form.

## Simplify E and F to expressions with a minimum number of literals.

# Simplify the following Boolean functions F together with the don`t care conditions d. Find all prime implicants and essential prime implicants, and apply the selection rule.

## F(A, B, C)=m(3, 5, 6), d(A,B,C)=m(0, 7)

## F(A, B, C, D)=m(4, 6, 7, 8, 12, 15), d(A, B, C, D)=m(2, 3, 5, 10, 11, 14)

## F(A, B, C, D) = )=M(1, 3, 5, 6, 7, 9, 10, 11, 14)

# Simplify the following Boolean functions F together with the don`t care conditions d in (1) sum-of-products and (2) product-of-sums form:

## F(W, X, Y, Z)=m(0, 1, 2, 3, 7, 8, 10), d(W, X, Y, Z)=m(5, 6, 11, 15)

## F(A, B, C, D)=m(3, 4, 13, 15), d(A, B, C, D)=m(1, 2, 5, 6, 8, 10, 12, 14)

## F(A, B, C, D, E, F)=m(6, 9, 13, 18, 19, 25, 27, 29, 41, 45, 57, 61)

# The following Boolean expression: BE + B`DE` is a simplified version of the expression: A`BE + BCDE + BC`D`E + A`B`DE` + B`C`DE`. Are there any don`t care conditions? If so, what are they?

# Simplify each of the following expressions, and implement them with (1) NAND gates, (2) NOR gates. Assume that both true and complement versions of the input variables are available.

## WX` + WXZ + W`Y`Z` + W`XY` + WXZ`

## XZ + XYZ` + WX`Y`

# Implement the following Boolean function with XOR and AND gates:

# AB`C`D + A`BC`D + AB`CD` + A`BCD`

# Convert the AND/OR/NOT logic diagram shown below to (a) a NAND logic diagram, and (b) a NOR logic diagram.

# Derive the exclusive-OR/exclusive–NOR circuits for three-bit parity generator and a four-bit parity checker, using an even parity bit.

# A NAND gate with seven inputs is required. For each of the following cases, minimize the number of gates used in the multiple-level result:

## Design the 7-input NAND gate using 2-input NAND gates and NOT gates.

## Design the 7-input NAND gate using 2-input NAND gates, 2-input NOR gates, and NOT gates.