## Slide 1: Functions and Functional Blocks
COE 202
Digital Logic Design
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Outline
Enabling function
Decoders
Implementing Functions using Decoders
Encoders
Multiplexers
Implementing Functions using Multiplexers
DeMultiplexers
Design Examples using MSI Functional Blocks

## Slide 3: Functions and Functional Blocks
Will consider functions that are useful in designing other combinational and sequential circuits
Such circuits can be implemented using a set of functional blocks
In the past, many functional blocks were implemented as separate SSI (small scale integration), MSI, and LSI integrated circuits (ICs)
Today, they are often used as parts in a design library for use within larger VLSI circuits
10s 100s 1000s millions gates/chip
SS  MS  LS  VLS
(Small Scale) (Medium Scale) (Large Scale) (Very Large Scale)

## Slide 4: Enabling Function
Enable: Allow an input signal to pass through to an output
Disable: block an input signal from passing through to an output, replacing it with a fixed state (1, 0, or HiZ)
Disable: EN = 0 in both cases
When disabled, output = 0
When disabled, output = 1

## Slide 5: Decoders
A decoder is a circuit that decodes an input code. Given a binary code of n-bits, a decoder will tell which code is this out of the 2n possible codes.
A decoder may have enable line
  In general, output i equals 1 if and only if the input binary code has a value of i.
  Thus, each output line equals 1 at only one input combination but is equal to 0 at all other combinations.
  Thus, the decoder generates all of the 2n minterms of n input variables.

## Slide 6: 2-to-4 Decoder
A 2-to-4 decoder contains two inputs denoted by A1 and A0 and four outputs denoted by D0, D1, D2, and D3.
For each input combination, one output line is activated, that is, the output line corresponding to the input combination becomes 1, while other lines remain inactive.
For example, an input of 00 at the input will activate line D0. 01 at the input will activate line D1, and so on.

## Slide 7: 2-to-4 Decoder
Notice that, each output of the decoder is actually a minterm resulting from a certain combination of the inputs, that is:
( minterm m0)
( minterm m1)
( minterm m2)
( minterm m3)

## Slide 8: 2-to-4 Decoder with Enable
Attach m output-enabling gates opened by the EN input
  Note use of X’s to denote both 0 and 1 at the inputs
  Combination containing two X’s represent four input binary combinations

## Slide 9: 3-to-8 Decoder
In a three to eight decoder, there are three inputs and eight outputs, A0 is the least significant variable, while A2 is the most significant variable.
Each output represents one minterm
  For example, for input combination A2A1A0 = 001, output line D1 equals 1 while all other output lines equal 0’s
  It should be noted that at any given instance of time, one and only one output line can be activated.

## Slide 10: 3-to-8 Decoder Implementation
Notice that each output line
is the minterm corresponding to
the input code, i.e. D5 is m5

## Slide 11: Hierarchical 2-to-4 Decoder Design

## Slide 12: Hierarchical 3-to-8 Decoder Design

## Slide 13: Decoder Expansion
Example: 3-to-8 from two 2-to-4 with EN
  Using two 2-to-4 decoders
  & one 1-to-2 decoder

## Slide 14: Implementing Functions using Decoders
Implementing functions of n inputs and m requires:
  Specification:
   As a Truth Table (has n input columns and m output columns) or m sum of minterms (SOm) expressions
  Implementation requires:
   One n-to-2n-line decoder
   m OR gates, one for each output
  Procedure:
   From the truth table: For each ‘1’ in the truth table of an output, connect the corresponding Di of the decoder to the OR of that output
   From the m minterm expressions: Connect the decoder Di’s corresponding to the minterms of each output to the OR of that output

## Slide 15: Implementing Functions using Decoders
Example:1-bit adder (Full Adder)
LSB
We need:
2 SOm expressions
3-to-23 Decoder
2 OR gates of appropriate # of inputs
Larger # of 1’s require larger ORs. If so, Consider expressing F and using a NOR instead!

## Slide 16: Encoders
An encoder performs the inverse operation of a decoder.
It has 2n inputs, and n output lines.
Only one input can be logic 1 at any given time (active input). All other inputs must be 0’s.
Output lines generate the binary code corresponding to the active input.

## Slide 17: Octal-to-Binary Encoder
Only 8 rows are
relevant, out of the 2^8 = 256 rows
Assuming
only 1 (and at least 1)
Input line being
active at a time

## Slide 18: Octal-to-Binary Encoder
Note that not all input combinations are valid.
Valid combinations are those which have exactly one input equal to logic 1 while all other inputs are logic 0’s.
Since, the number of inputs = 8, K-maps cannot be used to derive the output Boolean expressions. The encoder implementation, however, can be directly derived from the truth table:
  Since A0 = 1 if the input octal digit is 1 or 3 or 5 or 7, then we can write: A0 = E1 + E3 + E5+ E7
  Likewise, A1 = E2 + E3 + E6+ E7, and similarly
  A2 = E4 + E5 + E6+ E7
  Thus, the encoder can be implemented using three 4- input OR gates.

## Slide 19: Major Limitation of Encoders
Exactly one input must be active at any given time.
If the number of active inputs is less than one or more than one, the output will be incorrect.
For example, if E3 = E6 = 1, the output of the encoder A2A1A0 = 111, which implies incorrect output.
Two Problems to Resolve:
  1. If two or more inputs are active at the same time, what should the output be?
  2. An output of all 0's is generated in 2 cases:
    when all inputs are 0
    when E0 is equal to 1.
    How can this ambiguity be resolved?

## Slide 20: Major Limitation of Encoders
Solution To Problem 1:
  Use a Priority Encoder which produces the output corresponding to the input with higher priority.
  Inputs are assigned priorities according to their subscript value; e.g. higher subscript inputs are assigned higher priority.
  In the previous example, if E3 = E6 = 1, the output corresponding to E6 will be produced (A2A1A0 = 110) since E6 has higher priority than E3.
Solution To Problem 2:
  Provide one more output signal V to indicate validity of input data.
  V = 0 if none of the inputs equals 1, otherwise it is 1

## Slide 21: 4-to-2 Priority Encoders
Sixteen input combinations.
Three output variables A1, A0, and V.
V is needed to take care of situation when all inputs are equal to zero.

## Slide 22: 4-to-2 Priority Encoders

## Slide 23: Multiplexers: 2n-to-1
A multiplexer (MUX) selects information from one of 2n input line and directs it toward a single output line.
A typical multiplexer has:
  2n information inputs (I(2n – 1), … I0) (to select from)
  1 Output Y (to select to)
  n select control (address) inputs (Sn - 1, … S0) (to select with)
Implemented using decoders
MUX selection circuits can be duplicated m times (with the same selection controls in parallel) to provide m-wide data widths

## Slide 24: 2-to-1 MUX
The single selection variable S
has two values:
  S = 0 selects input I0
  S = 1 selects input I1
3-input K-map optimization gives
the output equation:
The circuit:
Can be seen As:
1-to-2 decoder
+ Enabling
+ Selection
Truth Table
2n Minterms
2n I Inputs

## Slide 25: 4-to-1 MUX
Using 2-to-4 decoder +4 2-input AND + 4-input OR for Enabling/Selection
X
2-to-4
Size of the Select
Inputs = Log2 (4)
# of the
ANDs

## Slide 26: 4-to-1 MUX
A 4-to-1 MUX can be implemented using three 2-to-1 MUXs.
F = s1’s0’ I0 + s1’s0 I1 + s1s0’ I2 + s1s0 I3
= s1’ (s0’ I0 + s0 I1)+ s1 (s0’ I2 + s0 I3)
2x1
MUX
I0
I1
S0
2x1
MUX
I2
I3
S0
2x1
MUX
S1
F

## Slide 27: Quad 2-to-1 MUX
Given two 4-bit numbers A and B, design a multiplexer that selects one of these 2 numbers based on some select signal S. Obviously, the output (Y) is a 4-bit number.
The 4-bit output number Y is defined as follows:
  Y = A IF S=0, otherwise Y = B
The circuit is implemented using four 2x1 Muxes, where the output of each of the Muxes gives one of the outputs (Yi).

## Slide 28: Quad 2-to-1 MUX
2x1
MUX
A0
B0
S
Y0
2x1
MUX
A1
B1
S
Y1
2x1
MUX
A2
B2
S
Y2
2x1
MUX
A3
B3
S
Y3

## Slide 29: 16-to-1 MUX

## Slide 30: Implementing Functions using Multiplexers

## Slide 31: Implementing Functions using Multiplexers
Implementing a function of n inputs and m outputs (n to m) requires:
  Truth table, or m Sum-of-minterms expressions
  m-wide 2n-to-1 multiplexer
Design:
  In the order they appear in the truth table:
    Apply the function inputs to the multiplexer select inputs Sn -1, … , S0
    Label the outputs of the multiplexer with the output variables
  Value-fix the information inputs to the multiplexer using the values from the truth table. For don’t cares, use either 0 or 1.

## Slide 32: Implementing Functions using Multiplexers
Example: 1-bit adder

## Slide 33: Implementing Functions using Multiplexers
Example: 1-bit adder, a more efficient approach

## Slide 34: Implementing Functions using Multiplexers
Example: F (A,B,C,D) = m(1,3,4,11,12,13,14,15)
16 rows in truth table
 16-to-1 MUX
(conventional
approach)
But using the efficient
approach … will use
only an 8-to-1 MUX
+ 1 inverter

## Slide 35: Implementing Functions using Multiplexers
Example: F (A,B,C) = m(1,2,6,7)

## Slide 36: Shannon's Expansion
The cofactor of f(x1,x2,…,xi,…,xn) with respect to variable xi is fxi = f(x1,x2,…,xi=1,…,xn)
The cofactor of f(x1,x2,…,xi,…,xn) with respect to variable xi’ is fxi’ = f(x1,x2,…,xi=0,…,xn)
Theorem: Shannon's Expansion
Any function can be expressed as sum of products (product of sums) of n literals, minterms (maxterms), by recursive expansion.

## Slide 37: Shannon's Expansion
Example: f = ab + ac + bc
  fa = b + c
  fa’ = bc
  F = a fa + a’ fa’ = a (b + c) + a’ (bc)
Using Shanon’s Expansion we can implement any function using any sizes of multiplexers
2x1 MUX: f = a [ b (1) + b’ (c) ] + a’ [ b (c) + b’ (0) ]
  Three 2x1 Muxs
4x1 MUX: f = a b (1) + a b’ (c) + a’ b ( c) + a’ b’ (0)

## Slide 38: Demultiplexer
Multiplexer
Demultiplexer
MUX
De
MUX
Many-to-One
One-to-Many

A decoder with Enable is
Referred to as:
Decoder/Demultiplexer
DeMUX
A device that moves data arriving on a single input (E) to one of m outputs (Ds)
Determined by the value of log2 address inputs (As)

## Slide 39: Decoder with Enable = DeMultiplexer
Alternatively, can be viewed as distributing the value of the signal EN to 1 of 4 outputs
In this case, called a Demultiplexer
Decoder is disabled
No 1’s
Normal
Decoder
Operation
Data Input
Address
Outputs

## Slide 40: Design Examples using MSI Functional Blocks
1. Adding Three 4-bit numbers
2. Adding two 16-bit numbers using 4-bit adders
3. Building 4-to-16 Decoders using 2-to-4 Decoders with Enable
4. Selecting the larger of two 4-bit numbers
5. BCD to Excess-3 Code Converter using a decoder and straight binary encoder

## Slide 41: Adding Three 4-bit Numbers
Problem: Add three 4-bit numbers (X, Y, Z) using standard MSI combinational components
Solution:
Let the numbers be X3X2X1X0, Y3Y2Y1Y0, Z3Z2Z1Z0
X3X2X1X0
+ Y3Y2Y1Y0
-------------------
C4 S3S2S1S0
S3S2S1S0
+ Z3Z2Z1Z0
-------------------
D4 F3F2F1F0
Note: C4 and D4 are generated in position 4. They must be added to generate the most significant bits of the result

## Slide 42: Adding Three 4-bit Numbers
64
59 +
123
89 +
212
1

## Slide 43: Adding Two 16-bit Numbers using 4-bit Adders
Solution:
Four 4-bit adder blocks are connected in cascade, with carries rippling in between

## Slide 44: Design a 4-to-16 Decoder Using 2-to-4 Decoders with Enable
Problem: Design a 4x16 Decoder using 2x4 Decoders
Solution:
Each group combination holds a unique value for A3A2
  One Decoder can be therefore used with inputs: A3A2
  Four more decoders are needed for representing each individual color combination
A3 | A2 | A1 | A0 | Active Output
0 | 0 | 0 | 0 | D0
0 | 0 | 0 | 1 | D1
0 | 0 | 1 | 0 | D2
0 | 0 | 1 | 1 | D3
0 | 1 | 0 | 0 | D4
0 | 1 | 0 | 1 | D5
0 | 1 | 1 | 0 | D6
0 | 1 | 1 | 1 | D7
1 | 0 | 0 | 0 | D8
1 | 0 | 0 | 1 | D9
1 | 0 | 1 | 0 | D10
1 | 0 | 1 | 1 | D11
1 | 1 | 0 | 0 | D12
1 | 1 | 0 | 1 | D13
1 | 1 | 1 | 0 | D14
1 | 1 | 1 | 1 | D15
A3A2 = 00
A3A2 = 01
A3A2 = 10
A3A2 = 11
Common to all 4
3-to-4 decoders
Select 1 of the 4
2-to-4 decoders

## Slide 45: Design a 4-to-16 Decoder Using 2-to-4 Decoders with Enable
2x4 Decoder
D0 D1 D2 D3
A0 A1
2x4 Decoder
D4 D5 D6 D7
A0 A1
2x4 Decoder
D8 D9 D10 D11
A0 A1
2x4 Decoder
D12 D13 D14 D15
A0 A1
2x4 Decoder
A2 A3
E
D0 D1 D2 D3
E
Enable for the
full 4-to16 decoder

## Slide 46: Hardware that Compares Two Unsigned 4-bit Numbers and Passes the Larger of the Two
Solution: We will use a magnitude comparator and a Quad 2-to-1 MUX. How?

## Slide 47: BCD to Excess-3 Code Converter using a Decoder and Straight Binary Encoder
Index
0
1
2
3
4
5
6
7
8
9
BCD: 0 - 9
Excess-3: 3 - 12
Excess-3
BCD