Name: KEY									Id#

COE 202, Term 052

Fundamentals of Computer Engineering

Quiz# 1

Date: Monday, Feb. 27

# Q1. Represent the following numbers in binary and hexadecimal. Use as many bits as needed, and approximate the fraction to 4 binary digits:

## (200.6)10

= (C8.9)16

=(11001000.1001)2

## (54.5)8

=(101100.101)2

= (2C.A)16

# Q2. Assume that an 8-bit register contains the following number 10111000. Determine the content of the register assuming that it represents:

## an unsigned number.

= 128+32+16+8=184

OR = 255 – (64+7) = 255 -71 = 184

## a 2’s complement signed number.

2’s complement of 10111000 = 01001000 = 64+8=72

  - 10111000 represents -72

# Q3. Perform the following operations assuming that numbers are represented using 8-bits assuming r’s complement representation, and determine if there is an overflow or not:

## (11101110)2 + (11110111)2

11101110

+ 		11110111

__________

11100101		Cout = 1

There is no overflow since we are adding two negative numbers and we got a negative number. Also Cin ( Cout = 0.

ii. (4C)16 -  (D0)16

= (4C)16 + 16’s complement of  (D0)16

= (4C)16 + (30)16 =  (7C)16

There is no overflow since we are adding two positive numbers and we got a positive number.

# Q4.  Determine, in binary and decimal, the smallest (negative) number and the largest (positive) number that can be stored using the 2`s complement notation, assuming 10-bit representation.

|  | Binary | Decinal |
| --- | --- | --- |
| Smallest (negative) | 10 0000 0000 | = -29 = -512 |
| Largest (Positive) | 01 1111 1111 | = +(29-1) = +511 |