Name: KEY									Id#

COE 202, Term 102

Fundamentals of Computer Engineering

Quiz# 3

Date: Saturday, April 16

# Q1.

# Simplify the following Boolean functions F together with the don`t care conditions d, into minimal sum-of-products expressions. Identify all the prime implicants and the essential prime implicants.

## F(A, B, C, D)=m(0, 6, 7, 8, 9), d(A, B, C, D)=m(1, 2, 5, 10, 12, 13, 14, 15)

Prime Implicants:  C’D, CD’, BC, BD, B’C’, B’D’, AC’, AD’

There are no essential prime implicants.

F = B’C’ + BC

# Show an implementation of the function using minimal number of NAND gates.

# Show an implementation of the function using minimal number of NOR gates.

F’ = B’C + BC’  => F=F’’ = (B+C’)(B’+C)