## Slide 1: Introduction
COE 301 Computer Organization
Prof. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. M. Mudawar, COE 301, KFUPM]

## Slide 2: Next . . .
High-Level, Assembly-, and Machine-Languages
Components of a Computer System
Technology Improvements
Programmer’s View of a Computer System

## Slide 3: Some Important Questions to Ask
What is Assembly Language?
What is Machine Language?
How is Assembly related to a high-level language?
Why Learn Assembly Language?
What is an Assembler, Linker, and Debugger?

## Slide 4: A Hierarchy of Languages
Application Programs
High-Level Languages
Assembly Language
Machine Language
Hardware
High-Level Language
Low-Level Language
Machine independent
Machine specific

## Slide 5: Assembly and Machine Language
Machine language
  Native to a processor: executed directly by hardware
  Instructions consist of binary code: 1s and 0s
Assembly language
  Slightly higher-level language
  Readability of instructions is better than machine language
  One-to-one correspondence with machine language instructions
Assemblers translate assembly to machine code
Compilers translate high-level programs to machine code
  Either directly, or
  Indirectly via an assembler

## Slide 6: Compiler and Assembler

## Slide 7: Instructions and Machine Language
Each command of a program is called an instruction (it instructs the computer what to do).
Computers only deal with binary data, hence the instructions must be in binary format (0s and 1s) .
The set of all instructions (in binary form) makes up the computer's machine language. This is also referred to as the instruction set.

## Slide 8: Instruction Fields
Machine language instructions usually are made up of several fields. Each field specifies different information for the computer. The major two fields are:
Opcode field which stands for operation code and it specifies the particular operation that is to be performed.
  Each operation has its unique opcode.
Operands fields which specify where to get the source and destination operands for the operation specified by the opcode.
  The source/destination of operands can be a constant, the memory or one of the general-purpose registers.

## Slide 9: Translating Languages
MIPS Assembly Language:
sll $2,$5, 2
add $2,$4,$2
lw $15,0($2)
lw $16,4($2)
sw $16,0($2)
sw $15,4($2)
jr $31
Compiler
Program (C Language):
swap(int v[], int k) {
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
A statement in a high-level language is translated typically into several machine-level instructions
MIPS Machine Language:
00051080
00821020
8C620000
8CF20004
ACF20000
AC620004
03E00008
Assembler

## Slide 10: Advantages of High-Level Languages
Program development is faster
  High-level statements: fewer instructions to code
Program maintenance is easier
  For the same above reasons
Programs are portable
  Contain few machine-dependent details
    Can be used with little or no modifications on different machines
  Compiler translates to the target machine language
  However, Assembly language programs are not portable

## Slide 11: Why Learn Assembly Language?
Many reasons:
  Accessibility to system hardware
  Space and time efficiency
Accessibility to system hardware
  Assembly Language is useful for implementing system software
  Also useful for small embedded system applications
Space and Time efficiency
  Understanding sources of program inefficiency
  Tuning program performance
  Writing compact code

## Slide 12: Assembly Language Programming Tools
Editor
  Allows you to create and edit assembly language source files
Assembler
  Converts assembly language programs into object files
  Object files contain the machine instructions
Linker
  Combines object files created by the assembler with link libraries
  Produces a single executable program
Debugger
  Allows you to trace the execution of a program
  Allows you to view machine instructions, memory, and registers

## Slide 13: Assemble and Link Process
Source
File
Source
File
Source
File
Assembler
Object
File
Assembler
Object
File
Assembler
Object
File
Linker
Executable
File
Link
Libraries
A project may consist of multiple source files
Assembler translates each source file separately into an object file
Linker links all object files together with link libraries

## Slide 14: MARS Assembler and Simulator Tool

## Slide 15: MARS Assembler and Simulator Tool
Simulates the execution of a MIPS program
  No direct execution on the underlying Intel processor
Editor with color-coded assembly syntax
Assembler
  Converts MIPS assembly language programs into object files
Debugger
  Allows you to trace the execution of a program and set breakpoints
  Allows you to view machine instructions, edit registers and memory

## Slide 16: Next . . .
High-Level, Assembly-, and Machine-Languages
Components of a Computer System
Technology Improvements
Programmer’s View of a Computer System

## Slide 17: Components of a Computer System
Processor
  Datapath
  Control
Memory & Storage
  Main Memory
  Disk Storage
Input devices
Output devices
Bus: Interconnects processor to memory and I/O
Network: newly added component for communication
Computer
Memory
I/O Devices
Input
Output
BUS
Control
Datapath
Processor
Disk
Network

## Slide 18: Memory
Ordered sequence of bytes
  The sequence number is called the memory address
Byte addressable memory
  Each byte has a unique address
  Supported by almost all processors
Physical address space
  Determined by the address bus width
  Pentium has a 32-bit address bus
    Physical address space = 4GB = 232 bytes
  Itanium with a 64-bit address bus can support
    Up to 264 bytes of physical address space

## Slide 19: Address Space
Address Space is the set of memory locations (bytes) that can be addressed

## Slide 20: Address, Data, and Control Bus
Address Bus
  Memory address is put on address bus
  If memory address = a bits then 2a locations are addressed
Data Bus: bi-directional bus
  Data can be transferred in both directions on the data bus
Control Bus
  Signals control
  transfer of data
  Read request
  Write request
  Done transfer
Memory
0
1
2
3
2a – 1
. . .
read
write
done
data bus
address bus
Processor
d bits
a bits
Address Register
Data Register
Bus Control

## Slide 21: Memory Devices
Volatile Memory Devices
  Data is lost when device is powered off
  RAM = Random Access Memory
  DRAM = Dynamic RAM
    1-Transistor cell + trench capacitor
    Dense but slow, must be refreshed
    Typical choice for main memory
  SRAM: Static RAM
    6-Transistor cell, faster but less dense than DRAM
    Typical choice for cache memory
Non-Volatile Memory Devices
  Stores information permanently
  ROM = Read Only Memory
  Used to store the information required to startup the computer
  Many types: ROM, EPROM, EEPROM, and FLASH
  FLASH memory can be erased electrically in blocks

## Slide 22: Magnetic Disk Storage
Arm provides read/write heads for all surfaces
The disk heads are connected together and move in conjunction
Track 0
Track 1
Recording area
Spindle
Direction of rotation
Platter
Read/write head
Actuator
Arm
Track 2
A Magnetic disk consists of a collection of platters
Provides a number of recording surfaces

## Slide 23
Magnetic Disk Storage
Track 0
Track 1
Sector
Recording area
Spindle
Direction of rotation
Platter
Read/write head
Actuator
Arm
Track 2
Disk Access Time =
Seek Time +
Rotation Latency +
Transfer Time
Seek Time: head movement to the desired track (milliseconds)
Rotation Latency: disk rotation until desired sector arrives under the head
Transfer Time: to transfer data

## Slide 24
Example on Disk Access Time
Given a magnetic disk with the following properties
  Rotation speed = 7200 RPM (rotations per minute)
  Average seek = 8 ms, Sector = 512 bytes, Track = 200 sectors
Calculate
  Time of one rotation (in milliseconds)
  Average time to access a block of 32 consecutive sectors
Answer
  Rotations per second
  Rotation time in milliseconds
  Average rotational latency
  Time to transfer 32 sectors
  Average access time
  = 7200/60 = 120 RPS
= 1000/120 = 8.33 ms
= time of half rotation = 4.17 ms
= (32/200) * 8.33 = 1.33 ms
= 8 + 4.17 + 1.33 = 13.5 ms

## Slide 25
Processor-Memory Performance Gap
1980 – No cache in microprocessor
1995 – Two-level cache on microprocessor
CPU: 55% per year
DRAM: 7% per year
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-Memory
Performance Gap: (grows 50% per year)
Performance
“Moore’s Law”

## Slide 26
The Need for a Memory Hierarchy
Widening speed gap between CPU and main memory
  Processor operation takes less than 1 ns
  Main memory requires more than 50 ns to access
Each instruction involves at least one memory access
  One memory access to fetch the instruction
  A second memory access for load and store instructions
Memory bandwidth limits the instruction execution rate
Cache memory can help bridge the CPU-memory gap
Cache memory is small in size but fast

## Slide 27: Typical Memory Hierarchy
Registers are at the top of the hierarchy
  Typical size < 1 KB
  Access time < 0.5 ns
Level 1 Cache (8 – 64 KB)
  Access time: 0.5 – 1 ns
L2 Cache (64 KB – 8 MB)
  Access time: 2 – 10 ns
Main Memory (1 – 64 GB)
  Access time: 50 – 70 ns
Disk Storage (> 200 GB)
  Access time: milliseconds
Microprocessor
Registers
L1 Cache
L2 Cache
Memory
Disk, Tape, etc
Memory Bus
I/O Bus
Faster
Bigger

## Slide 28: Processor
Datapath: part of a processor that executes instructions
Control: generates control signals for each instruction
A
L
U
Registers
Instruction
Program Counter
Instruction
Cache
Next Program
Counter
Data
Cache
Control

## Slide 29: Datapath Components
Program Counter (PC)
  Contains address of instruction to be fetched
  Next Program Counter: computes address of next instruction
Instruction Register (IR)
  Stores the fetched instruction
Instruction and Data Caches
  Small and fast memory containing most recent instructions/data
Register File
  General-purpose registers used for intermediate computations
ALU = Arithmetic and Logic Unit
  Executes arithmetic and logic instructions
Buses
  Used to wire and interconnect the various components

## Slide 30: Fetch - Execute Cycle
Fetch instruction
Compute address of next instruction
Generate control signals for instruction
Read operands from registers
Compute result value
Writeback result in a register
Instruction Decode
Instruction Fetch
Execute
Writeback Result
Infinite Cycle implemented in Hardware
Memory Access
Read or write memory (load/store)

## Slide 31: Next . . .
Assembly-, Machine-, and High-Level Languages
Components of a Computer System
Technology Improvements
Programmer’s View of a Computer System

## Slide 32: Technology Improvements
Vacuum tube → transistor → IC → VLSI
Processor
  Transistor count: about 30% to 40% per year
Memory
  DRAM capacity: about 60% per year (4x every 3 yrs)
  Cost per bit: decreases about 25% per year
Disk
  Capacity: about 60% per year
Opportunities for new applications
Better organizations and designs

## Slide 33: Growth of Capacity per DRAM Chip
DRAM capacity quadrupled almost every 3 years
  60% increase per year, for 20 years

## Slide 34: Processor Performance
Almost 10000x improvement between 1978 and 2005
Slowed down by power and memory latency

## Slide 35: Next . . .
Assembly-, Machine-, and High-Level Languages
Components of a Computer System
Technology Improvements
Programmer’s View of a Computer System

## Slide 36: Programmer’s View of a Computer System
Application Programs
High-Level Language
Assembly Language
Operating System
Instruction Set
Architecture
Microarchitecture
Physical Design
Level 0
Level 1
Level 2
Level 3
Level 4
Level 5
Increased level of abstraction
Each level hides the details of the level below it
Software
Hardware
Interface SW & HW

## Slide 37: Programmer’s View of a Computer System
Application Programs (Level 5)
  Written in high-level programming languages
  Such as Java, C++, Pascal, Visual Basic . . .
  Programs compile into assembly language level (Level 4)
Assembly Language (Level 4)
  Instruction mnemonics (symbols) are used
  Have one-to-one correspondence to machine language
  Calls functions written at the operating system level (Level 3)
  Programs are translated into machine language (Level 2)

## Slide 38: Programmer’s View of a Computer System
Operating System (Level 3)
  Provides services to level 4 and 5 programs
  Translated to run at the machine instruction level (Level 2)
Instruction Set Architecture (Level 2)
  Interface between software and hardware
  Specifies how a processor functions
  Machine instructions, registers, and memory are exposed
  Machine language is executed by Level 1 (microarchitecture)

## Slide 39: Programmer’s View of a Computer System
Microarchitecture (Level 1)
  Controls the execution of machine instructions (Level 2)
  Implemented by digital logic
Physical Design (Level 0)
  Implements the microarchitecture at the transistor-level
  Physical layout of circuits on a chip