## Slide 1: Instruction Sets Chapter 2
COE 306: Introduction to Embedded Systems
Dr. Aiman El-Maleh
Computer Engineering Department
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Next . . .
Computer Architecture Taxonomy
ARM Instruction Set
PIC16F Instruction Set
TI CX55 DSP
TI C64X DSP

## Slide 3: Von Neumann Architecture
Memory holds data, instructions
Central processing unit (CPU) fetches instructions from memory
Allows self-modifying code

## Slide 4: Harvard Architecture
Has separate memories for data and program & allows two simultaneous memory fetches
Harvard architectures are widely used today
  the separation of program and data memories provides higher performance for digital signal processing (DSP); higher memory bandwidth

## Slide 5: Instruction Set Characteristics
The instruction set of the computer defines the interface between software modules and the underlying hardware.
Instruction set characteristics:
  Fixed vs. variable length
  Addressing modes
  Number of operands and type
  Types of operations supported
We often characterize architectures by their word length: 4-bit, 8-bit, 16-bit, 32-bit, 64-bit, etc.
Instruction set architecture: instruction set, memory, programmer accessible registers

## Slide 6: RISC vs. CISC
Complex instruction set computer (CISC):
  a variety of instructions that may perform very complex tasks;
  many addressing modes.
Reduced instruction set computer (RISC):
  fewer and simpler instructions;
  load/store;
  pipelined instructions.
Early RISC designs substantially outperformed CISC designs.
Performance gap between RISC and CISC has narrowed as CISC used RISC techniques to efficiently execute CISC instructions.

## Slide 7: Little-Endian vs. Big-Endian
Little-endian: least-significant byte first
Big-endian: most-significant byte first
Little-Endian
Big-Endian

## Slide 8: Instruction Execution
Single-issue: A single-issue processor executes one instruction at a time.
Multiple-issue
  A superscalar processor uses specialized logic to identify at run time instructions that can be executed simultaneously
  A VLIW processor relies on the compiler to determine what combinations of instructions can be legally executed together
VLIW is more energy-efficient than superscalar
VLIW is widely used in signal processing
  Multimedia processing
  Processing multiple channels of signals

## Slide 9: Development of the ARM Architecture

## Slide 10: ARM Architecture Version Summary

## Slide 11: ARM Architecture Version Summary

## Slide 12: ARM Instruction Set
RISC architecture: load/store
32-bit words and instructions
ARM7: Von Neumann architecture – our focus
ARM9: Harvard architecture
Cortex-M: either architecture based on model
ARM7: 32-bit addresses, byte-addressable
Configurable endianness on power-up
Most ARM’s implement two instruction sets
  32-bit ARM Instruction Set
  16-bit Thumb Instruction Set

## Slide 13: ARM Processor Modes
ARM has seven basic operating modes:
  User: unprivileged mode under which most tasks run
  FIQ: entered when a high priority (fast) interrupt is raised
  IRQ: is used for general-purpose interrupt handling
  Supervisor: is a protected mode for the operating system entered when the CPU is reset or a software interrupt instruction is executed
  Abort: used to handle memory access violations
  Undefined: entered when an undefined instruction is executed
  System: privileged mode for the operating system. It is not entered due to an exception

## Slide 14: The ARM Register Set
ARM has 37 registers
Note: System mode uses the User mode register set

## Slide 15: The ARM Register Set
ARM has 37 registers all of which are 32-bits long.
  1 dedicated program counter (pc)
  1 dedicated current program status register (cpsr)
  5 dedicated saved program status registers (spsr)
  30 general purpose registers
The current processor mode governs which of several banks is accessible. Each mode can access
  a particular set of r0-r12 registers
  a particular r13 (stack pointer, sp) and r14 (link register, lr)
  the program counter, r15 (pc)
  the current program status register, cpsr
Privileged modes (except System) can also access
  a particular spsr (saved program status register)

## Slide 16: Program Counter (r15)
When the processor is executing in ARM state:
  All instructions are 32 bits wide
  All instructions must be word-aligned
  Therefore the PC value is stored in bits [31:2] with bits [1:0] undefined (as instruction cannot be halfword)
When the processor is executing in Thumb state:
  All instructions are 16 bits wide
  All instructions must be halfword-aligned
  Therefore the PC value is stored in bits [31:1] with bits [0] undefined (as instruction cannot be byte-aligned)

## Slide 17: Program Status Registers
Condition code flags
  N = Negative result from ALU
  Z = Zero result from ALU
  C = ALU operation Carried out
  V = ALU operation oVerflowed
Sticky Overflow flag - Q flag
  Architecture 5TE/J only
  Indicates if saturation has occurred
J bit
  Architecture 5TEJ only
  J = 1: Processor in Jazelle state
Interrupt Disable bits.
  I = 1: Disables the IRQ.
  F = 1: Disables the FIQ.
T Bit
  Architecture xT only
  T = 0: Processor in ARM state
  T = 1: Processor in Thumb state
Mode bits
  Specify the processor mode

## Slide 18: ARM Instruction Set Format

## Slide 19: Conditional Execution
Most instruction sets only allow branches to be executed conditionally.
However by reusing the condition evaluation hardware, ARM effectively increases number of instructions.
All instructions contain a condition field which determines whether the CPU will execute them.
This removes the need for many branches, which stall the pipeline.
Allows very dense in-line code, without branches.

## Slide 20: The Condition Field

## Slide 21: Data Processing Instructions
Largest family of ARM instructions, all sharing the same instruction format.
Contains:
  Arithmetic operations
  Comparisons (no results - just set condition codes)
  Logical operations
  Data movement between registers
They each perform a specific operation on one or two operands.
  First operand always a register - Rn
  Second operand sent to the ALU via barrel shifter.

## Slide 22: Data Processing Instructions
cond
0 0
operand 2
#
opcode
S
Rn
Rd
31
28
27
26
25
24
21
20
19
16
15
12
1
1
0
destination register
first operand register
set condition codes
arithmetic/logic function
8-bit immediate
1
25
1
1
8
7
0
#rot
Rm
1
1
7
6
5
4
3
0
#shift
Rm
0
25
1
1
8
7
6
5
4
3
0
Rs
Sh
0
1
0
Sh
immediate alignment
immediate shift length
shift type
second operand register
register shift length

## Slide 23: Arithmetic Operations
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry - 1
  RSB operand2 - operand1
  RSC operand2 - operand1 + carry - 1
Syntax: <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5

## Slide 24: Logical Operations
Operations are:
  AND operand1 AND operand2
  EOR operand1 EOR operand2
  ORR operand1 OR operand2
  BIC operand1 AND NOT operand2 [i.e. bit clear]
Syntax: <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples:
  AND r0, r1, r2
  BICEQ r2, r3, #7
  EORS r1,r3,r0

## Slide 25: Comparisons
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS. Thus no need to set S bit.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax: <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 26: Data Movement
Operations are:
  MOV operand2
  MVN NOT operand2
Note that these make no use of operand1.
Syntax: <Operation>{<cond>}{S} Rd, Operand2
Examples:
  MOV r0, r1
  MOVS r2, #10
  MVNEQ r1,#0

## Slide 27: The Barrel Shifter
ARM doesn’t have actual shift instructions.
A barrel shifter provides a mechanism to carry out shifts as part of other instructions.

## Slide 28: Using the Barrel Shifter: The Second Operand

## Slide 29: Second Operand: Using a Shifted Register
Multiplication by constants can often be done by using some combination of MOVs, ADDs, SUBs and RSBs with shifts.
  Multiplications by a constant equal to a ((power of 2) ± 1) can be done in one cycle.
Example: r0 = r1 * 5 Example: r0 = r1 + (r1 * 4)
ï ADD r0, r1, r1, LSL #2
Example: r2 = r3 * 105 Example: r2 = r3 * 15 * 7 Example: r2 = r3 * (16 - 1) * (8 - 1)
ï RSB r2, r3, r3, LSL #4 ; r2 = r3 * 15 ï RSB r2, r2, r2, LSL #3 ; r2 = r2 * 7

## Slide 30: Second Operand: Immediate Value
No ARM instruction can contain a 32 bit immediate constant
  All ARM instructions are fixed as 32 bits long
The data processing instruction format has 12 bits available for operand2
4 bit rotate value (0-15) is multiplied by two to give range 0-30 in steps of 2
Values that cannot be generated in this way will cause an error.

## Slide 31: Second Operand: Immediate Value
This gives us:
  0 - 255 [0 - 0xff]
  256,260,264,..,1020 [0x100-0x3fc, step 4, 0x40-0xff ror 30]
  1024,1040,1056,..,4080 [0x400-0xff0, step 16, 0x40-0xff ror 28]
  4096,4160, 4224,..,16320 [0x1000-0x3fc0, step 64, 0x40-0xff ror 26]
These can be loaded using, for example:
  MOV r0, #0x40, 26 ; => MOV r0, #0x1000 (i.e. 4096)
To make this easier, the assembler will convert to this form for us if simply given the required constant:
  MOV r0, #4096 ; => MOV r0, #0x1000 (i.e. 0x40 ror 26)
The bitwise complements can also be formed using MVN: MOV r0, #0xFFFFFFFF; assembles to MVN r0, #0

## Slide 32: Loading 32-bit Constants
To allow larger constants to be loaded, the assembler offers a pseudo-instruction: LDR rd, =const
This will either:
  Produce a MOV or MVN instruction to generate the value (if possible).
  Generate a LDR instruction with a PC-relative address to read the constant from a literal pool (Constant data area embedded in the code).
For example
  LDR r0,=0xFF => MOV r0,#0xFF
  LDR r0,=0x55555555 => LDR r0,[PC,#Imm12] … … DCD 0x55555555

## Slide 33: Multiplication Instructions
The Basic ARM provides two multiplication instructions.
Multiply
  MUL{<cond>}{S} Rd, Rm, Rs ; Rd = Rm * Rs
Multiply Accumulate - does addition for free
  MLA{<cond>}{S} Rd, Rm, Rs, Rn ; Rd = (Rm * Rs) + Rn
Restrictions on use:
  Rd and Rm cannot be the same register
  Cannot use PC.
Operands can be considered signed or unsigned
  Up to user to interpret correctly.

## Slide 34: Load / Store Instructions
  LDR STR Word
  LDRB STRB Byte
  LDRH STRH Halfword
  LDRSB Signed byte load
  LDRSH Signed halfword load
Syntax:
  LDR{<size>} {<cond>} Rd, <address>
  STR{<size>} {<cond>} Rd, <address>
All of these instructions can be conditionally executed by inserting the appropriate condition code after STR / LDR.
  e.g. LDRBEQ

## Slide 35: Encoding Format of LDR & STR

## Slide 36: Address Accessed
Address accessed by LDR/STR is specified by a base register plus an offset
For word and unsigned byte accesses, offset can be
  An unsigned 12-bit immediate value (i.e. 0 - 4095 bytes). LDR r0,[r1,#8]
  A register, optionally shifted by an immediate value LDR r0,[r1,r2] LDR r0,[r1,r2,LSL#2]
Offset can be either added or subtracted from the base register: LDR r0,[r1,#-8] LDR r0,[r1,-r2] LDR r0,[r1,-r2,LSL#2]

## Slide 37: Address Accessed
For halfword and signed halfword / byte, offset can be:
  An unsigned 8 bit immediate value (i.e. 0-255 bytes).
  A register (unshifted).
For all accesses, offset can be applied
  before the transfer is made: Pre-indexed addressing
    optionally auto-incrementing the base register, by postfixing the instruction with an ‘!’.
  after the transfer is made: Post-indexed addressing
    causing the base register to be auto-incremented.

## Slide 38: Pre- or Post-Indexed Addressing

## Slide 39: ARM ADR Pseudo-Op
Cannot refer to an address directly in an instruction.
ADR pseudo-op generates instruction required to calculate address:
  ADR r1,FOO
Generates value by performing arithmetic on PC.

## Slide 40: Arithmetic Operations Example
C: x = (a + b) - c;
ARM Assembly:
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
ADR r4,b ; get address for b, reusing r4
LDR r1,[r4] ; get value of b
ADD r3,r0,r1 ; compute a+b
ADR r4,c ; get address for c
LDR r2,[r4] ; get value of c
SUB r3,r3,r2 ; complete computation of x
ADR r4,x ; get address for x
STR r3,[r4] ; store value of x

## Slide 41: Arithmetic Operations Example
C: y = a * (b + c);
ARM Assembly:
  ADR r4,b ; get address for b
  LDR r0,[r4] ; get value of b
  ADR r4,c ; get address for c
  LDR r1,[r4] ; get value of c
  ADD r2,r0,r1 ; compute partial result
  ADR r4,a ; get address for a
  LDR r0,[r4] ; get value of a
  MUL r2,r0,r2 ; compute final value for y
  ADR r4,y ; get address for y
  STR r2,[r4] ; store y

## Slide 42: Logical Operations Example
C: z = (a << 2) | (b & 15);
ARM Assembly:
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
MOV r0,r0,LSL 2 ; perform shift
ADR r4,b ; get address for b
LDR r1,[r4] ; get value of b
AND r1,r1,#15 ; perform AND
ORR r1,r0,r1 ; perform OR
ADR r4,z ; get address for z
STR r1,[r4] ; store value for z

## Slide 43: ARM Branches and Subroutines
Branch: B{<cond>} label
  PC relative: ±32 Mbyte range.
Branch with Link: BL{<cond>} sub_routine_label
  Stores return address in LR
  Returning implemented by restoring the PC from LR
  MOV pc, lr

## Slide 44: Control Flow: If Statement Example
C:
  if (a > b) { x = 5; y = c + d; } else x = c - d;
ARM Assembly:
; compute and test condition
ADR r4,a ; get address for a
LDR r0,[r4] ; get value of a
ADR r4,b ; get address for b
LDR r1,[r4] ; get value for b
CMP r0,r1 ; compare a > b
BLE fblock ; if a <= b, branch to false block

## Slide 45: Control Flow: If Statement Example
; true block
MOV r0,#5 ; generate value for x
ADR r4,x ; get address for x
STR r0,[r4] ; store x
ADR r4,c ; get address for c
LDR r0,[r4] ; get value of c
ADR r4,d ; get address for d
LDR r1,[r4] ; get value of d
ADD r0,r0,r1 ; compute y
ADR r4,y ; get address for y
STR r0,[r4] ; store y
B after ; branch around false block

## Slide 46: Control Flow: If Statement Example
; false block
Fblock ADR r4,c ; get address for c
LDR r0,[r4] ; get value of c
ADR r4,d ; get address for d
LDR r1,[r4] ; get value for d
SUB r0,r0,r1 ; compute c-d
ADR r4,x ; get address for x
STR r0,[r4] ; store value of x
after ...

## Slide 47: Control Flow: Switch Statement
C:
  switch (test) { case 0: … break; case 1: … }
ARM Assembly:
ADR r2,test ; get address for test
LDR r0,[r2] ; load value for test
ADR r1,switchtab ; load address for switch table
LDR r1,[r1,r0,LSL #2] ; index switch table
MOV pc, r1
switchtab DCD case0
DCD case1
...

## Slide 48: Control Flow: For Loop
C:
  for (i=0, f=0; i<N; i++)
  f = f + c[i]*x[i];
ARM Assembly:
; loop initiation code
MOV r0,#0 ; use r0 for i
MOV r8,#0 ; use separate index for arrays
ADR r2,N ; get address for N
LDR r1,[r2] ; get value of N
MOV r2,#0 ; use r2 for f
FIR FILTER

## Slide 49: Control Flow: For Loop
ADR r3,c ; load r3 with base of c
ADR r5,x ; load r5 with base of x
; loop body
loop LDR r4,[r3,r8] ; get c[i]
LDR r6,[r5,r8] ; get x[i]
MUL r4,r6,r4 ; compute c[i]*x[i]
ADD r2,r2,r4 ; add into running sum
ADD r8,r8,#4 ; add one word offset to array index
ADD r0,r0,#1 ; add 1 to i
CMP r0,r1 ; exit?
BLT loop ; if i < N, continue

## Slide 50: Examples of Conditional Execution
Use a sequence of several conditional instructions
  if (a==0) func(1);
    CMP r0,#0 MOVEQ r0,#1 BLEQ func
Set the flags, then use various condition codes
  if (a==0) x=0; if (a>0) x=1;
    CMP r0,#0 MOVEQ r1,#0 MOVGT r1,#1
Use conditional compare instructions
  if (a==4 || a==10) x=0;
    CMP r0,#4 CMPNE r0,#10 MOVEQ r1,#0

## Slide 51: Block Data Transfer
The Load and Store Multiple instructions (LDM / STM) allow between 1 and 16 registers to be transferred to or from memory.
Base register used to determine where memory access should occur.
  4 different addressing modes allow increment and decrement of the base register before or after the memory access.
  The base register can be incremented or decremented by one word for each register in the operation.
  Base register can be optionally updated following the transfer by appending it with an ‘!’.
  Lowest register number is always transferred to/from lowest memory location accessed.

## Slide 52: Block Data Transfer
These instructions are efficient for:
  Saving and restoring context (stack)
  Moving large blocks of data around memory

## Slide 53: Stack
A stack is an area of memory which grows as new data is “pushed” onto the “top” of it, and shrinks as data is “popped” off the top.
Two pointers define the current limits of the stack.
  A base pointer
    used to point to the “bottom” of the stack (the first location).
  A stack pointer
    used to point the current “top” of the stack.

## Slide 54: Stack Operation
Traditionally, a stack grows down in memory, with the last “pushed” value at the lowest address.
ARM also supports ascending stacks, where the stack structure grows up through memory.
The value of the stack pointer can either:
  Point to the last occupied address (Full Stack)
    and so needs pre-decrementing (i.e. before the push)
  Point to the next occupied address (Empty Stack)
    and so needs post-decrementing (i.e. after the push)

## Slide 55: Stack Operation
The stack type to be used is given by the postfix to the instruction:
  STMFD / LDMFD : Full Descending stack
  STMFA / LDMFA : Full Ascending stack.
  STMED / LDMED : Empty Descending stack
  STMEA / LDMEA : Empty Ascending stack

## Slide 56: Stack Examples

## Slide 57: Function Calls
Branch-and-link instruction: BL
  Uses r14 (lr) to store the current PC
Procedure call stack
  Allows nested function calls
  Allows passing of parameters and return values
  Structure is left to the programmer
Compilers use frames
  Also store local variables
  Stack pointer (sp) and frame pointer (fp)

## Slide 58: ARM Procedure Call Standard(APCS)
r0 – r3: first 4 parameters
Additional parameters use the stack frame
r0: return value
r4 – r7: register variables
r11: frame pointer (fp)
r12: intra procedure (ip) scratch register
r13: stack pointer (sp)
r10: stack size

## Slide 59: Stacks and Subroutines
Any registers needed can be pushed onto the stack at start of subroutine and popped off again at end so as to restore them before return to the caller:
STMFD sp!,{r0-r12, lr} ; stack all registers
........ ; and the return address
LDMFD sp!,{r0-r12, pc} ; load all the registers
; and return automatically

## Slide 60: PICmicro PIC16F Instruction Set
8-bit word size, 14-bit instructions
Harvard architecture
Instruction flash memory up to 8192 (i.e., 8K) words
13-bit PC
Data memory includes up to
  368 words SRAM
  256 bytes EEPROM
Low-power features:
  Sleep mode
  Support for multiple clocks

## Slide 61: Instruction Memory Organization
Program memory is divided into four 2k×14 pages
Interrupt vectors in bottom of memory
PC can be loaded from 8-level stack.
  Separate from program and data memory.
Stack operates as a circular buffer

## Slide 62: Register File Concept
All of data memory is part of the register file, so any location in data memory may be operated on directly
All peripherals are mapped into data memory as a series of registers
W is working register

## Slide 63: Architecture Block Diagram

## Slide 64: Data Memory Organization

## Slide 65: Data Memory Organization

## Slide 66: Status Register
IRP: Register Bank Select (used for Indirect addressing)
0 = Bank 0, 1 1 = Bank 2, 3
RP1:RP0: Register Bank Select Bits (used for direct addressing)
00 = Bank 0, 01 = Bank 1, 10 = Bank 2, 11 = Bank 3
TO: Time-out bit
0 = A WDT time-out occurred
PD: Power-down bit
0 = SLEEP instruction executed
Z: Zero bit
1 = Result of arithmetic operation is zero
DC: Digit cary / borrow bit
1 = Carry out of 4th low order bit occurred / No borrow occurred
C: Carry / borrow bit
1 = Carry out of MSb occurred / No borrow occurred

## Slide 67: Program Counter
13-bit PC can access up to 213 = 8192 words
Contains address of NEXT instruction
Lower byte accessible in data memory as PCL
Upper byte indirectly accessible via PCLATH
Runs freely across page boundaries
PCL register can be used as an operand in instructions

## Slide 68: PIC Instruction Set – Description Convention

## Slide 69: PIC16 Instruction Set

## Slide 70: Instruction Set Overview

## Slide 71: Instruction Set Overview

## Slide 72: Instruction Set Overview

## Slide 73: PIC16 Addressing Modes
Data Memory Access
  Direct addwf <data_address>, <d>
  Indirect addwf INDF, <d>
  Immediate (Literal) movlw <constant>
Indirect addressing controlled by INDF and FSR (File Select Register) registers
  Access to INDF causes indirect load through FSR
Program Memory Access
  Absolute goto <program_address>
  Relative addwf PCL,f

## Slide 74: Data Memory: Direct Addressing

## Slide 75: Data Memory: Indirect Addressing
8 bits from FSR + 1 bit from IRP = 9 bits
Effective 29 = 512 memory locations

## Slide 76: Register Indirect Addressing

## Slide 77: Control Flow Instructions
GOTO: Unconditional branch
INCFSZ: Increment f, skip if 0
DECFSZ: Decrement f, skip if 0
BTFSC: Bit test f, skip if clear
BTFSS: Bit test f, skip if set
CALL: Call subroutine
RETURN: Return from subroutine
RETLW: Return with literal in W
RETFIE: Return from interrupt
SLEEP: Go into standby mode

## Slide 78: PC Absolute Addressing
CALL and GOTO Instructions
PC Absolute Addressing (Program Memory)
  Jump to another program memory location out of PC sequence
  Call a subroutine
Used by the CALL and GOTO instructions
  11 bits of the required 13 address bits are encoded in the instruction
  2 additional bits will come from the PCLATH register
Used when performing Computed Goto operation
  Address to jump to is calculated by the program
  Computed address is written directly into the Program Counter

## Slide 79: PC Absolute Addressing

## Slide 80: PC Absolute Addressing

## Slide 81: PC Relative Addressing

## Slide 82: PC Relative Addressing: Lookup Table
Note: After fetching an instruction PCL gets incremented by 1.

## Slide 83: TI C55X Organization
Relatively high-performance digital signal processor
Accumulator architecture
Word: 16-bit, Longword: 32-bit
Some instructions are bit-addressable
Most registers are special-purpose
Most registers are memory-mapped
Can be accessed by name or address
Can execute two instructions in parallel
Has a variable length instruction set (8-16-24-32-40-64 bits)

## Slide 84: TI C55x Microarchitecture

## Slide 85: Instruction Buffer Unit (I Unit)
Receives program code into its instruction buffer queue and decodes instructions
Passes data to the P unit, the A unit, and the D unit for the execution of instructions
The CPU fetches 32 bits at a time from program memory
8 bytes are transferred from the queue to the instruction decoder

## Slide 86: Program Flow Unit (P Unit)
The program-address generation logic is responsible for generating 24-bit addresses for fetches from program memory
The program control logic performs the following actions:
  Tests whether a condition is true for a conditional instruction
  Initiates interrupt servicing
  Controls execution of repetition instructions
  Manages instructions that are executed in parallel.

## Slide 87: P-Unit Registers

## Slide 88: Address-Data Flow Unit (A Unit)
Data-Address Generation Unit (DAGEN)
  generates all addresses for reads from or writes to data space and I/O space
A-Unit Arithmetic Logic Unit (A-Unit ALU)
  Performs additions, subtractions, comparisons, Boolean logic operations, signed shifts, logical shifts, and absolute value calculations

## Slide 89: A-Unit Registers

## Slide 90: Data Computation Unit (D Unit)
40-bit shifter
40-bit ALU
Two Multiply-and-Accumulate Units (MACs)
  each MAC can perform a 17-bit ×17-bit multiplication (fractional or integer) and a 40-bit addition or subtraction with optional 32-/40-bit saturation
D-Unit Bit Manipulation Unit (D-Unit BIT)
  Extracts and expands bit fields, and performs bit counting

## Slide 91: D-Unit Registers
Accumulators
  AC0–AC3 40-bit Accumulators 0, 1, 2, and 3
  AC0L: low-order bits 0 – 15
  AC0H: high-order bits 16 – 31
  AC0G: guard bits 32-39
  Increase the range for intermediate calculations
Transition Registers
  TRN0, TRN1 16-bit Transition registers 0 and 1

## Slide 92: Memory Organization

## Slide 93: Memory Organization
24-bit address space
Data, program, and I/O spaces are mapped to the same physical memory
  Program space: byte-addressable, 24-bit addresses
  Data space: word-addressable
  I/O space: 64K words
Data space: 128 pages of 64K words each
Partial on-chip memory
First 96 words of data page 0 & First 192 words of program space
  Memory-mapped registers

## Slide 94: C55x Addressing Modes
Three addressing modes:
  Absolute addressing supplies an address in an instruction.
  Direct addressing supplies an offset.
  Indirect addressing uses a register as a pointer.
Absolute Addressing
  k16: 16-bit + DPH register = 23-bit absolute address
  k23: 23-bit unsigned value
  I/O absolute address: 16-bit unsigned value, e.g. port(#1234)

## Slide 95: Direct Addressing Modes
DP direct
  Uses an offset relative to data page register (DP) to access a memory location; ADP = DPH[22:15](DP+Doffset)
SP direct
  Uses an offset relative to data stack pointer (SP) to access stack values in data memory; ASP = SPH[22:15](SP+Soffset)
Register-bit direct
  Uses an offset from LSB to specify a bit address, used to access one register bit or two adjacent register bits
PDP direct
  Uses an offset relative to peripheral data page register (PDP) to specify an I/O address; APDP = PDP[15:6]PDPoffset

## Slide 96: Indirect Addressing Modes
AR indirect addressing: uses one of eight auxiliary registers (AR0–AR7) to point to data
Dual AR indirect addressing: similar to AR indirect mode; used with an instruction that accesses two or more data-memory locations at the same time
CDP indirect addressing: uses the coefficient data pointer (CDP) to point to coefficient data
Coefficient indirect addressing: similar to CDP indirect mode; used for instructions that can access a coefficient in data memory at the same time they access two other data-memory values using the dual AR indirect addressing mode

## Slide 97: C55x Data Instructions Examples
MOV src, dst register/memory register/memory
ADD src, dst dst = dst + src
ADD dual(Lmem),ACx,ACy
  LO(ACy) = LO(Lmem) + LO(ACx)
  HI(ACy) = HI(Lmem) + HI(ACx)
MPY src, dst Integer multiplication of 16-bit values
MAC ACx, Tx, ACy
  ACy = ACy + (ACx * Tx)
CMP src == dst, TC1
  Compare and set a test control flag TC1 in ST0_55 register

## Slide 98: Control Flow Instructions
Unconditional branch
  B ACx
  B label
Conditional branch
  BCC label, cond
Examples of cond
  ACx <= #0; content is less than or equal to 0
  !overflow(ACx) ACOVx bit is cleared to 0
  ARx != #0 content is not equal to 0
  CARRY; CARRY bit is set to 1
  TC1 ^ TC2; TC1 XOR TC2 is equal to 1

## Slide 99: Loops and Procedure Calls
Loops
  Single-instruction repeat registers: RPTC, CSR
  Block-repeat registers: BRC0, RSA0, REA0, BRC1, . . .
  2 levels of block-repeat
Procedures:
  CALL target: Unconditional procedure call. Uses the stack
  CALLCC addr, cond: Conditional procedure call
  Fast-return vs. slow-return

## Slide 100: TI 64X DSP
High-performance VLIW DSP.
  Up to eight instructions per cycle
  Divided into two data paths A and B
Floating-point and integer arithmetic
Harvard architecture
Load/store architecture
Separate data and program on-chip memories
Combined external memory
Instruction grouping: fetch packet and execute packet

## Slide 101: C64x Block Diagram
Execution divided between two data paths
Each data path has its own register file and 4 different functional units

## Slide 102: Function units
.L1 and .L2 perform 32/40-bit arithmetic, 32-bit logical, data packing/unpacking.
.S1 and .S2 perform 32-bit arithmetic, 32/40-bit shift and bit-field ops, 32-bit logical ops, branches, etc.
.M1 and .M2 perform multiplications, bit interleaving, rotation, Galois field multiplication, etc.
.D1 and .D2 perform address calculations, loads/stores, etc.

## Slide 103: TI C64X VLIW Organization
Fetch packet:
  A group of instructions fetched together
  8 words, aligned on 256-bit boundaries
  Up to 14 instructions per fetch packet
Execute packet:
  A group of instructions that execute together
  Up to 8 instructions, if they use different functional units
  A fetch packet may result in multiple execute packets

## Slide 104: Summary
Both the von Neumann and Harvard architectures are in common use today
ARM is a load-store architecture. It provides a few relatively complex instructions, such as saving and restoring multiple registers
The PIC16F is a very small, efficient microcontroller
The C55x provides a number of architectural features to support the arithmetic loops that are common on digital signal processing code
The C64x organizes instructions into execution packets to enable parallel execution