## Slide 1: Processes and Operating Systems Chapter 6
COE 306: Introduction to Embedded Systems
Dr. Aiman El-Maleh
Computer Engineering Department
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Next . . .
Processes and Operating Systems
Real Time Operating System (RTOS)
The Scheduling Problem
Rate Monotonic Scheduling (RMS)
Earliest-Deadline-First Scheduling (EDFS)
FreeRTOS

## Slide 3: Processes and Operating Systems
Processes and operating system are abstractions
  allow us to build complex applications on microprocessors
  provide much greater flexibility to satisfy timing requirements
Let us switch the state of the processor between multiple tasks
Process defines the state of an executing program
A process is a unique execution of a program
  Several copies of a program may run simultaneously or at different times
A process has its own state: registers and memory
  Threads share the same address space

## Slide 4: Processes and Operating Systems
The Operating System (OS) manages processes
OS provides the mechanism for switching execution between processes
Real-Time Operating System (RTOS) is OS that provides facilities for satisfying real-time requirements
  Allocates resources based on real-time requirements
  General-purpose OSs use other criteria, e.g. fairness
RTOS helps build more complex systems using several programs that run concurrently

## Slide 5: Tasks and Processes
A task is a functional description of a connected set of operations
Task can also mean a collection of processes
Multiple tasks means multiple processes
Multiple processes help with timing complexity:
  multiple rates
    multimedia
    automotive
  asynchronous input
    user interfaces
    communication systems

## Slide 6: Compression Unit Example
Variable data rates
  need to receive and send data at different rates
  program may emit two bits for first byte and then seven bits for second byte
  must ensure to process inputs and outputs at the proper rates
Asynchronous input
  a compression mode button that disables or enables compression
Keeping up with input and output data while checking on button can introduce complex control code into program

## Slide 7: Compression Unit Example
Sampling the button’s state too slowly can cause the machine to miss a button depression entirely
Sampling it too frequently can cause the machine to incorrectly compress data due to executing later than expected
Variable execution times of code causes other code to execute later than expected
We need to be able to keep track of these two different tasks separately, applying different timing requirements to each
Complex control is usually quite difficult to verify for either functional or timing properties

## Slide 8: Multi-Rate Systems
Multirate embedded computing systems are very common, including automobile engines, printers, and cell phones
Certain operations must be executed periodically, and each operation is executed at its own rate
Tasks may be synchronous or asynchronous
Synchronous tasks may recur at different rates
Processes run at different rates based on computational needs of the tasks

## Slide 9: Example: Engine Control
Tasks:
  spark control
    Firing the spark plug periodically
    Spark timing varies with engine speed
  regulate exhaust emissions
  crankshaft sensing
  fuel/air mixture
  oxygen sensor
  multimode control scheme
    engine warm-up , cruise, climbing steep hills
Rates at which engine inputs and outputs must be handled range between 2ms and 1s

## Slide 10: Typical Rates in Engine Controllers
Variable | Update period (ms)
Engine spark timing | 2
Throttle | 2
Air flow | 4
Battery voltage | 4
Fuel flow | 10
Recycled exhaust gas | 25
Status switches | 20
Air temperature | 400
Barometric pressure | 1000
Spark (dwell) | 1
Fuel adjustment | 8
Carburetor | 25
Mode actuators | 100

## Slide 11: Real-Time Systems
Perform a computation to conform to external timing constraints
Deadline frequency:
  Periodic
  Aperiodic
Deadline type:
  Hard: failure to meet deadline causes system failure
    Car Airbag system, car brakes
  Soft: failure to meet deadline causes degraded response
    Room temperature control, car multimedia system
  Firm: late response is useless; Infrequent deadline misses are tolerable, but may degrade the system's quality of service
    A digital cable set-top box frame decoder

## Slide 12: Types of Process Timing Requirements
Release time: time at which process becomes ready to execute
Deadline: time at which process must finish execution
Periodic process: a process executes every period
  e.g. Firing the spark plugs
Aperiodic process: executes on demand
  Processing a button press
Period : interval between process activations
  Initiation Interval or Rate = 1/period

## Slide 13: Types of Process Timing Requirements
Jitter: Allowable variation in task completion time
  Example: multimedia synchronization
What happens when a process misses a deadline?
  Can be catastrophic such as in an automotive control system
  a missed deadline in a telephone system may cause a temporary silence on the line
Example: Space Shuttle software error
  Space Shuttle’s first launch was delayed by a software timing error
  Change to one routine added delay that threw off start time calculation

## Slide 14: Task Graphs
Tasks may have data dependencies---must execute in certain order
Task graph shows data/control dependencies between processes
Task: connected set of processes
Task set: One or more tasks
Task graph assumes that all processes in each task run at the same rate, tasks do not communicate
In reality, some amount of inter-task communication is necessary

## Slide 15: Process Execution Characteristics
Process execution time Ti
  Execution time in absence of preemption
  Possible time units: seconds, clock cycles
  Worst-case, best-case execution time may be useful in some cases
Sources of variation:
  Data dependencies
  Memory system
  CPU pipeline

## Slide 16: CPU Utilization
CPU utilization
  Fraction of the CPU that is doing useful work
  Often calculated assuming no scheduling overhead
Utilization:
  U = (CPU time for useful work) / (total available CPU time)
  Utilization over a time interval [t1, t2]
    =
    = T/t

## Slide 17: Running Periodic Processes
Need code to control execution of processes
Simplest implementation: process = subroutine
While loop implementation
  Simplest implementation has one loop
  No control over execution timing
  Pad the loop with NOP instructions
  Used by some video games in the 1970s
  Broken: hard to determine execution time, conditionals, re-evaluation upon code change
while (TRUE) {
p1();
p2();
}

## Slide 18: Running Periodic Processes
Timed loop implementation
  Encapsulate set of all processes in a single function that implements the task set
  Use timer to control execution of the task
  No control over timing of individual processes
Multiple timers implementation
  Each task has its own function
  Each task has its own timer
    May not have enough timers to implement all the rates
void A(){ /* rate A */
p1(); p3();
}
void B(){ /* rate B */
p2(); p4(); p5();
}
void pall() {
p1();
p2();
}

## Slide 19: Running Periodic Processes
Timer + counter implementation
  Use a software count to divide the timer
  Only works for clean multiples of the timer period
Implementing processes
  All of these implementations are inadequate.
  Need better control over timing
  Need a better mechanism than subroutines
  Real-time operating systems (RTOS)
int p2count = 0;
void pall(){
p1();
if (p2count >= 2) {
p2();
p2count = 0;
}
else p2count++;
p3();
}

## Slide 20: Operating Systems
The operating system controls resources
  who gets the CPU
  when I/O takes place
  how much memory is allocated
The most important resource is the CPU itself
  CPU access controlled by the scheduler

## Slide 21: Real-Time Operating Systems
Solves the main problems of a cooperative multitasking system
Executes processes based on timing requirements provided by system designer
Based on two basic concepts:
  Preemption: the ability to interrupt a process to switch to another
  Context switching: switching execution and CPU state between processes

## Slide 22: State of a Process
A process can be in one of three states:
  executing on the CPU
  ready to run
  waiting for I/O, another process, timer, next period
The operating system selects the next executing process
At most one executing process

## Slide 23: Preemptive Execution
Kernel: part of the OS. Determines which process runs
The kernel is activated periodically by the timer
The timer period is known as the time quantum
  The smallest time unit in which CPU activity can be controlled

## Slide 24: Context Switching
Context: The set of registers that define a process
Context Switching: Switching the registers from one process to another
  Timer interrupt: transfer control from a process to kernel
  Kernel saves current process context
  Kernel selects next process (scheduling)
  Kernel restores next process context
Context switching code is usually assembly code
Task priorities make selecting processes flexible and fast

## Slide 25: Context Switching in FREERTOS

## Slide 26: The Scheduling Problem
Choosing the order of running processes is known as scheduling
Workstations try to avoid starving processes of CPU access
  Fairness = access to CPU
Embedded systems must meet deadlines
  Low-priority processes may not run for a long time
Scheduling feasibility
  Resource constraints make schedulability analysis NP-hard
  Must show that the deadlines are met for all timings of resource requests

## Slide 27: Scheduling Feasibility
Assume:
  No resource conflicts
  Constant process execution times
Require:
  T (period) ≥ Si Ti
  Can’t use more than 100% of the CPU.
Hyperperiod: least common multiple (LCM) of the task periods
  Must look at the hyperperiod schedule to find all task interactions
  Hyperperiod can be very long if task periods are not chosen carefully

## Slide 28: Hyperperiod Example
Long hyperperiod:
  P1 7 ms
  P2 11 ms
  P3 15 ms
  LCM = 1155 ms
Example:
  P1 period 1 ms, CPU time 0.1 ms
  P2 period 1 ms, CPU time 0.2 ms
  P3 period 5 ms, CPU time 0.3 ms
Shorter hyperperiod:
  P1 8 ms
  P2 12 ms
  P3 16 ms
  LCM = 96 ms

## Slide 29: Round-Robin Scheduling
All the processes are kept on a list and scheduled one after the other
Time slices are assigned to each process in equal portions and in circular order
Common in general-purpose Oses
Schedule process only if ready
  Always test processes in the same order
Start round-robin again after finishing a round

## Slide 30: Priority-Based Scheduling
Each process has a priority
CPU goes to highest-priority process that is ready
Priorities determine scheduling policy:
  fixed priority
  time-varying priorities
Example:
  each process has a fixed priority (1 highest)
  highest-priority ready process gets CPU
  process continues until done

## Slide 31: Priority-Based Scheduling Example
time
P2 ready t=0
P1 ready t=15
P3 ready t=18
0
30
10
20
60
40
50
P2
P2
P1
P3

## Slide 32: Scheduling Metrics
How do we evaluate a scheduling policy:
  Ability to satisfy all deadlines
  CPU utilization---percentage of time devoted to useful work
  Scheduling overhead---time required to make scheduling decision

## Slide 33: Rate Monotonic Scheduling (RMS)
RMS is widely-used, analyzable scheduling policy
A static scheduling policy: processes have fixed priorities
RMS Model
  All processes run on single CPU
  Context switching time is ignored
  No data dependencies between processes
  Process execution time is constant
  All deadlines are at the end of the period
  Highest-priority ready process runs first
Priority assignment: The process with the shortest period is assigned the highest priority

## Slide 34: Rate Monotonic Scheduling (RMS)
RMS always provides a feasible schedule if such a schedule exists with fixed priority
Optimal static assignment
  No fixed-priority scheme does better
  Highest CPU utilization while ensuring that all processes meet their deadlines
Ti is computation time of process i
ti is period of process i
Released
Absolute deadline
ti
Execution time Ti

## Slide 35: Rate Monotonic Scheduling Example
What if execution times become 2, 3, 3?

## Slide 36: Rate Monotonic Analysis (RMA)
If P1 has higher priority, required constraint on CPU time:
If P2 has higher priority, required constraint on CPU time:
There are cases where first
relationship can be satisfied
and second cannot.
There are no cases where
second relationship can be
satisfied and first cannot
Consider T1=2 and T2=2,
1=3, 2=6.

## Slide 37: RMS CPU utilization
Utilization for n processes is:
Given n processes and ratio between any two periods less than 2, RMS CPU utilization upper bound:
  n = 2; U ≤ 0.83
  n = 3; U ≤ 0.78
  n ; U ≤ ln2 ≈ 0.69, 31% idle time
RMS may not be able to use 100% of CPU, even with zero context switch overhead

## Slide 38: RMS CPU Utilization Example
Utilization = 1/4 + 2/6 + 3/12 = 0.83

## Slide 39: Response Time
Response time
  Duration from released time to finish time
(1,4)
(2,5)
(2,10)
Response Time
5
5
10
10
15
15
P1
P2
P3

## Slide 40: Response Time
Response Time (ri) [Audsley et al., 1993]
  HP(Pi) : a set of higher-priority tasks than Pi
Real-time system is schedulable under RMS
if and only if ri ≤ i for all processes Pi(Ti,  i)

## Slide 41: Response Time
Response time computation for P3
  r3 = 2 + 0 = 2
  r3 = 2 + 2 + 1 = 5
  r3 = 2 + 2 + 2 = 6
  r3 = 2 + 4 + 2 = 8
  r3 = 2 + 4 + 2 = 8

## Slide 42: RMS- Schedulability Check
A set of n processes is schedulable on a uniprocessor by the RMS algorithm if the processor utilization (utilization test):
This condition is sufficient, but not necessary
  If U is less than or equal to the given bound, a schedule exists
  If there is a schedule, U could be greater than the bound
Example:
  P1: (T1=1, 1=2), P2: (T2=2, 2=4)
  There is a schedule with U=100%

## Slide 43: Another RMS Example
P1: T1=1, 1=4
P2: T2=2, 2=5
P3: T3=2, 3=7
(1,4)
(2,5)
(2,7)
5
5
10
10
15
15
P1
P2
P3
  n = 3; U ≤ 0.78
  U =0.936

## Slide 44: Another RMS Example
(1,4)
(2,5)
(2,7)
5
5
10
10
15
15
P1
P2
P3
  n = 3; U ≤ 0.78
  U =0.936

## Slide 45: Another RMS Example
(1,4)
(2,5)
(2,7)
Deadline Miss !
5
5
10
10
15
15
P1
P2
P3
  n = 3; U ≤ 0.78
  U =0.936

## Slide 46: Earliest-Deadline-First Scheduling
EDFS: dynamic priority scheduling scheme
Process closest to its deadline has highest priority
Requires recalculating processes priorities at every timer interrupt
Can achieve 100% utilization;higher utilization than RMS
On each timer interrupt
  compute time to deadline; choose process closest to deadline
Optimal scheduling algorithm
  if there is a schedule for a set of real-time tasks, EDF can schedule it
  Real-time system is schedulable under EDFS iff ∑Ui ≤ 1

## Slide 47: EDFS Example
(1,4)
(2,5)
(2,7)
5
5
10
10
15
15
P1
P2
P3
P1: T1=1, 1=4
P2: T2=2, 2=5
P3: T3=2, 2=7

## Slide 48: EDFS Example
(1,4)
(2,5)
(2,7)
5
5
10
10
15
15
P1
P2
P3

## Slide 49: EDFS Example
(1,4)
(2,5)
(2,7)
5
5
10
10
15
15
P1
P2
P3

## Slide 50: EDFS Example
(1,4)
(2,5)
(2,7)
5
5
10
10
15
15
P1
P2
P3

## Slide 51: EDFS – Overload Conditions
Domino effect during overload conditions
  Example: P1(3,4), P2(3,5), P3(3,6), P4(3,7)
P1
5
0
7
P2
P3
P4
3
6
Deadline Miss !
P1
5
0
7
P3
3
6
Better schedules :
P1
5
0
7
P4
3
6

## Slide 52: FreeRTOS
FreeRTOS is a real-time kernel/scheduler on top of which MCU applications can be built to meet their hard real-time requirements.
  Allows MCU applications be organized as a collection of independent threads of execution.
  Decides which thread should be executed by examining the priority assigned to each thread.
    Assume a single core MCU, where only a single thread can be executing at one time.
In FreeRTOS, each thread of execution is called a ‘task’.

## Slide 53: Task States in FreeRTOS
A task can exist in one of the following states:
  Running
  Ready
  Blocked
    A task is said to be in the Blocked state if it is currently waiting for either a temporal or external event.
  Susepended
    tasks only enter or exit the Suspended state when explicitly commanded to do so through the vTaskSuspend() and xTaskResume() API calls

## Slide 54: FreeRTOS Task Functions
Tasks are implemented as C functions.
  Its prototype must return void and take a void pointer parameter as the following
  void ATaskFunction (void *pvParameters);
Each task is a small program in its own right.
  Has an entry point
  Normally runs forever within an infinite loop
  Does not exit
  Must not contain a ‘return’ statement
  Must not be allowed to execute past the end of the function
  If a task is no longer required, it should be explicitly deleted.

## Slide 55: FreeRTOS Task Functions

## Slide 56: Creating Tasks
xTaskCreate() API function
  the most fundamental component in a multitasking system
    Probably the most complex of all API functions
  portBASE_TYPE xTaskCreate(
    pdTASK_CODE pvTaskCode,
    const signed char * const pcName,
    unsigned short usStackDepth,
    void *pvParameters,
    unsigned portBASE_TYPE uxPriority,
    xTaskHandle *pxCreatedTask
  );

## Slide 57: Task Parameters
pvTaskCode
  a pointer to the function (just the function name) that implements the task.
pcName
  A descriptive name for the task. It is not used by FreeRTOS, but a debugging aid.
usStackDepth
  Each task has its own unique stack that is allocated by the kernel to the task when the task is created.
  The value specifies the number of words the task stack can hold.

## Slide 58: Task Parameters
pvParameters
  The value assigned to pvParameters will be the values passed into the task
uxPriority
  defines the priority at which the task will execute.
  Priorities can be assigned from 0, which is the lowest priority, to (configMAX_PRIOIRTIES-1), which is the highest priority.
pxCreatedTask
  pass out a handle to the created task; to be used to refer the created task in API calls.
    E.g., change the task priority or delete the task
  Set to NULL if no use for the task handle

## Slide 59: Tasks Creation Examples
void vTaskFunction1(void *pvParameters);
void vTaskFunction2(void *pvParameters);
const char *pcTextForTask1 = "Task 1 is running\n";
const char *pcTextForTask2 = "Task 2 is running\n";
xTaskCreate(vTaskFunction1, "Task 1", 240, (void*) pcTextForTask1, 1, NULL);
xTaskCreate(vTaskFunction2, "Task 2", 240, (void*) pcTextForTask2, 2, NULL);
vTaskStartScheduler();

## Slide 60: Running a Periodic Task
vTaskDelayUntil() API Function
void vTaskDelayUntil(
portTickType *pxPreviousWakeTime,
portTickType xTimeIncrement);)
Parameters to vTaskDelayUntil()
  specify the exact tick count value at which the calling task should be moved from the Blocked state into the Ready state.
  to be used when a fixed execution period is required.
Example
  vTaskDelayUntil(&xLastWakeTime, (50 / portTICK_RATE_MS));

## Slide 61: vTaskDelayUntil() prototype
pxPreviousWakeTime
  Holds the time at which the task left the Blocked state.
  Be used as a reference point to compute the time at which the task next leaves the Blocked state.
  The variable pointed by pxPreviousWakeTime is updated automatically, not to be modified by application code, other than when the variable is first initialized.
xTimeIncrement
  Assume that vTaskDelayUtil() is being used to implement a task that executes periodically and with a fixed frequency – set by xTimeIncrement.
  Be specified in ‘ticks’. The constant portTICK_RATE_MS can be used to convert ms to ticks.

## Slide 62: Task Example
void vTaskFunction1(void *pvParameters) {
char *pcTaskName;
portTickType xLastWakeTime;
pcTaskName = (char *) pvParameters;
xLastWakeTime = xTaskGetTickCount();
for (;;) {
vPrintString(pcTaskName);
vPrintStringAndNumber("Task 1 Run @", xLastWakeTime);
vTaskDelayUntil(&xLastWakeTime, (50 / portTICK_RATE_MS));
}
}

## Slide 63: FreeRTOS
An open-source RTOS available at http://www.freertos.org
  Supports 34 architectures
  107,000 downloads a year
  Professionally developed, strictly quality controlled
  Free to use in commercial products
  Used in market sectors from toys to aircraft navigation
  Browsing the source code
    http://sourceforge.net/projects/freertos/
    Files, pick version
    FreeRTOS/Source/
    portable/GCC/ARM7_LPC23xx (compiler / architecture)