COE 405, Term 162

Design & Modeling of Digital Systems

Assignment# 2

Due date: Saturday, March 11

# Consider the given FSM that has 6 states, two inputs X and Y, and one output Z, represented by the following state table:

| Present State | Next State | Output |
| --- | --- | --- |
|  | XY=00 | XY=01 | XY=10 | XY=11 | Z |
| S0 | S1 | S3 | S0 | S4 | 0 |
| S1 | S0 | S4 | S1 | S5 | 0 |
| S2 | S2 | S5 | S0 | S5 | 0 |
| S3 | S1 | S3 | S0 | S4 | 1 |
| S4 | S0 | S4 | S2 | S5 | 1 |
| S5 | S1 | S3 | S1 | S3 | 1 |

## Determine the equivalent states.

## Reduce the state table into the minimum number of states and show the reduced state table.

# Consider the given FSM that has 4 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S0, 1 | S2, 0 |
| S1 | S0, 0 | S2, 0 |
| S2 | S1, 0 | S3, 0 |
| S3 | S1, 0 | S3, 1 |

## Implement the FSM using the following state assignment: S0=00, S1=10, S2=01, S3=11.

## Implement the FSM using the following state assignment: S0=10, S1=01, S2=11, S3=00.

## Compare the area of the two resulting circuits.

# It is required to design a sequential circuit using Mealy model that computes the equation Z=3*X-3, where X is an unsigned number that will be fed serially.  Assume that the circuit has an asynchronous Reset input that resets the machine to the reset state.

## Draw the state diagram for your sequential circuit. Make sure that your state machine is minimal and that it does not have any redundant state.

## Derive minimized equations for the output Z and next state variables.

## Write a Verilog model for modeling your sequential circuit.

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=1}, {X=3}, {X=5} and {X=4}.

## This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a PDF file that contains the following items:

## i.      Your name and ID

## ii.     Assignment number

## iii.    Problem statement

## iv.    Your solution

## v. Include snapshots of simulation output to illustrate the correctness of your models.