COE 405, Term 162

Design & Modeling of Digital Systems

Assignment# 4

Due date: Saturday, April 23

## It is required to design an n-bit signed multiplier circuit. The architecture and the algorithm for performing signed multiplication are given below:

## The example below illustrates the signed multiplication of two 4-bit numbers:

## Write a parametrizable Verilog module to model the signed multiplication circuit as a combinational circuit using for loop.

## Write a test bench to test the correct functionality of your combinational signed multiplication circuit by instantiating a 4-bit multiplier and applying the following sets of inputs: -6*-1, -4*-3, -8*+7,+7*+7.

## Implement your combinational signed multiplication circuit in FPGA and demonstrate its correct functionality. Include a video link that demonstrates the correct functionality of your implemented combinational signed multiplication circuit.

## Next, consider implemting the signed multiplication algorithm as a sequential circuit. Show the design of the datapath components and their control signals.

## Derive the ASMD chart of the control unit that will control the operation of the signed multiplication circuit.

## Model the data path of the sequential signed multiplication circuit in Verilog using a parametrizable module.

## Model the control unit of the sequential signed multiplication circuit in Verilog based on your derived ASM chart in (v).

## Write a test bench to test the correct functionality of your sequential signed multiplication circuit by instantiating a 4-bit multiplier and applying the following sets of inputs: -6*-1, -4*-3, -8*+7,+7*+7.

## Implement your sequential signed multiplication circuit in FPGA and demonstrate its correct functionality. Include a video link that demonstrates the correct functionality of your implemented sequential signed multiplication circuit.

## This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a PDF file that contains the following items:

## i.      Your name and ID

## ii.     Assignment number

## iii.    Problem statement

## iv.    Your solution

## v. Include snapshots of simulation output to illustrate the correctness of your models.