COE 405, Term 162

Design & Modeling of Digital Systems

Assignment# 4 Solution

Due date: Saturday, April 23

## It is required to design an n-bit signed multiplier circuit. The architecture and the algorithm for performing signed multiplication are given below:

## The example below illustrates the signed multiplication of two 4-bit numbers:

## Write a parametrizable Verilog module to model the signed multiplication circuit as a combinational circuit using for loop.

module MULC #(parameter N=4) (output reg [N-1:0] HI, LO, input [N-1:0] A, B);

integer i;

reg [N-1:0] C;

reg OVF, Sign;

always @(A, B) begin

HI = 0;  LO = B;

for (i=0; i<N; i=i+1) begin

if( LO[0] ) begin

if ( i==N-1 ) begin

C = HI - A;

OVF = (HI[N-1] ^ A[N-1]) & (HI[N-1]^C[N-1]);

end

else begin

C = HI + A;

OVF = (HI[N-1] ~^ A[N-1]) & (HI[N-1]^C[N-1]);

end

Sign = OVF ^ C[N-1];

HI = C;

end

else Sign = HI[N-1];

{HI, LO} = {Sign, HI,  LO[N-1:1]};

end

end

endmodule

## Write a test bench to test the correct functionality of your combinational signed multiplication circuit by instantiating a 4-bit multiplier and applying the following sets of inputs: -6*-1, -4*-3, -8*+7,+7*+7.

module MULC_Test();

reg [3:0] A, B;

wire [3:0] HI, LO;

wire [7:0] T;

assign T = {HI, LO};

MULC M1 (HI, LO, A, B);

initial begin

A=-6; B=-1;

#100 A=-4; B=-3;

#100 A=-8; B=+7;

#100 A=+7;

end

endmodule

As can be seen from the simulation results below, the multiplier module is producing the correct results:

## Implement your combinational signed multiplication circuit in FPGA and demonstrate its correct functionality. Include a video link that demonstrates the correct functionality of your implemented combinational signed multiplication circuit.

## Next, consider implemting the signed multiplication algorithm as a sequential circuit. Show the design of the datapath components and their control signals.

## Derive the ASMD chart of the control unit that will control the operation of the signed multiplication circuit.

## Model the data path of the sequential signed multiplication circuit in Verilog using a parametrizable module.

module SMUL_DP #(parameter n=4)(output reg [n-1:0] HI, LO, output EZ, input [n-1:0] A, B, input Init, Dec, Sel, EN, CLK);

// Down Counter

reg [log2(n-1):0] DCNT;

assign EZ = ~|DCNT;

always @(posedge CLK)

if (Init) DCNT = n-1;

else if (Dec) DCNT = DCNT - 1;

// Multiplicand Register

reg [n-1:0] Multiplicand;

always @(posedge CLK)

if (Init) Multiplicand= B;

// MUX for ADDition/ Subtraction

wire [n-1:0] X;

assign X = EZ? ~Multiplicand: Multiplicand;

// Adder/Subtracter

wire [n-1:0] Y;

assign Y = HI + X + EZ;

// MUX for Selection between HI and result of ADDition/ Subtraction

wire [n-1:0] Z;

assign Z = Sel? Y : HI;

// Overflow and Sign Computation

wire OVF, Sign;

assign OVF = (HI[n-1] ~^ X[n-1]) & (HI[n-1] ^ Z[n-1]);

assign Sign = Z[n-1] ^ OVF;

// HI & LO Registres

always @(posedge CLK)

if (Init) begin

HI = 0;

LO = A;

end

else if (EN)  {HI, LO} = {Sign, Z, LO[n-1:1]};

function integer log2 (input integer n);

integer i;

begin

log2 = 1;

for (i=0; 2**i<n; i=i+1)

log2 = i+1;

end

endfunction

endmodule

## Model the control unit of the sequential signed multiplication circuit in Verilog based on your derived ASM chart in (v).

module SMUL_CU (output reg Init, Dec, Sel, EN, Done, input Start, EZ, LOZ, CLK, Reset);

parameter S0 = 2'b00, S1=2'b01, S2=2'b10;

reg [1:0] state, next_state;

always @(posedge CLK, posedge Reset)

if (Reset) state <= S0;

else state <= next_state;

always @(state, Start, EZ, LOZ) begin

Init=0; Dec=0; Sel=0; Dec=0; EN=0; Done=0;

case (state)

S0:

if (Start)begin

Init = 1;

next_state=S1;

end

else next_state=S0;

S1: begin EN=1;

if (LOZ) Sel=1;

if (EZ) next_state=S2;

else begin Dec=1; next_state=S1; end

end

S2: begin Done=1;

if (Start)begin

Init = 1;

next_state=S1;

end

else next_state=S2;

end

default: begin

Init=1'bx; Dec=1'bx; Sel=1'bx; Dec=1'bx; 				      EN=1'bx; Done=1'bx;

next_state=2'bx;

end

endcase

end

endmodule

## Write a test bench to test the correct functionality of your sequential signed multiplication circuit by instantiating a 4-bit multiplier and applying the following sets of inputs: -6*-1, -4*-3, -8*+7,+7*+7.

module SMUL #(parameter n=4) (output [2*n-1:0] Result, output Done, input [n-1:0] A, B, input Start, CLK, Reset);

SMUL_DP #(4) M1 (Result[2*n-1:n], Result[n-1:0], EZ, A, B, Init, Dec, Sel, EN, CLK);

SMUL_CU M2 (Init, Dec, Sel, EN, Done, Start, EZ, Result[0], CLK, Reset);

endmodule

module SMUL_Test();

wire [7:0] Result;

wire Done;

reg [3:0] A, B;

reg Start, CLK, Reset;

SMUL #(4) M1 (Result, Done, A, B, Start, CLK, Reset);

initial begin

CLK=0;

forever

#100 CLK = ~ CLK;

end

initial begin

// Resetting the machine

@(negedge CLK) Reset=1;

// A=-6 B=-1

@(negedge CLK) Reset=0; Start=1; A=-6; B=-1;

@(negedge CLK) Start=0;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

// A=-4 B=-3

@(negedge CLK) Start=1; A=-4; B=-3;

@(negedge CLK) Start=0;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

// A=-8 B=+7

@(negedge CLK) Start=1; A=-8; B=+7;

@(negedge CLK) Start=0;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

// A=+7 B=+7

@(negedge CLK) Start=1; A=+7;

@(negedge CLK) Start=0;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

@(negedge CLK) ;

end

endmodule

As can be seen from the simulation results below, the sequential multiplier is working correctly and is producing the correct results as expected.

## Implement your sequential signed multiplication circuit in FPGA and demonstrate its correct functionality. Include a video link that demonstrates the correct functionality of your implemented sequential signed multiplication circuit.