May 20, 2013

COMPUTER ENGINEERING DEPARTMENT

COE 405

DESIGN & MODELING OF DIGITAL SYSTEMS

Final Exam

Second Semester  (122)

Time: 7:00-10:00 PM

OPEN BOOK EXAM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 28 |  |
| Q2 | 20 |  |
| Q3 | 36 |  |
| Q4 | 16 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

[28 Points]

# (Q1) Determine possible circuits that will be synthesize by each of the following modules:

- module FinalQ1_1 (output reg E, input A, B, C, D);

always @(posedge A)

if (B==C) E <= D;

elseE <= ~ D;

endmodule

- module FinalQ1_2 (output reg E, input A, B, C, D);

always @(A, B, C, D)

case ({A,B})

2'b00:  E = C & D;

2'b01:  E = C | D;

2'b10:  E = C ^ D;

endcase

endmodule

- module FinalQ1_3 (output reg E, input A, B, C, D);

always @(A, B, C, D) begin

E = 0;

case ({A,B})

2'b00:  E = C & D;

2'b01:  E = C | D;

2'b10:  E = C ^ D;

endcase

end

endmodule

- module FinalQ1_4 (output E, input A, B, C, D);

reg t;

always @(posedge A)

t <= B;

assign E = D?C:1'bz;

assign E = ~D?t:1'bz;

endmodule

- module FinalQ1_5 (output reg [3:0] Data_out, input DIN, clock, reset);

always @ (posedge clock,  posedge reset) begin

if (reset) Data_out = 0;

else begin

Data_out[0]=DIN;

Data_out[1]=Data_out[0];

Data_out[2]=Data_out[1];

Data_out[3]=Data_out[2];

end

end

endmodule

- module FinalQ1_6 (output reg Y, input D, S, R, X);

always @(posedge X, posedge S, posedge R )

if (R) Y <= 0;

else if (S) Y <=1;

else Y <= D;

endmodule

- module FinalQ1_7 (output reg Y, input D, S, R, X);

always @(posedge X)	begin

if (R) Y <= D;

if (S) Y <=~D;

end

endmodule

[20 Points]

# (Q2) The three n-bit registers R1, R2, and R3, are connected through  a tri-state bus (Cbus) to allow the transfer of the content of any register to any other register as shown below:

- Write a Verilog model  Datapath to model the given datapath showing the inetrface signals assuming R1, R2, R3 as output signals, CLK, Reset,  R1in, R2in, R3in, R1out, R2out, R3out, Dout and Data as input signals. Assume that RST is Asynchronous reset that resets the machine when set to 1. Use parametr n for determining  the width of registers with a default value of 8.

- Write a test bench to do the following assuming that the period of the clock is 100 ns and that the duty cycle is 50%:

  - Initialize all the registers to 0  using the RST signal at time = 200 ns.

  - Assign RST and all other  control signals to 0 at time 300 ns.

  - Assign Data=5 and Dout=1 at time 400 ns.

  - Copy the value 5 from the bus into register R1 in the next cycle.

  - Move the value of R1 into R2 in the following cycle.

  - All registers keep their value in the subsequent clock cycles

[36 Points]

# (Q3) It is required to design a module to perform unsigned division of an n-bit dividend number, A,  by an n-bit  divisor  number, B. The divider produces an n-bit quotient and an n-bit remainder. Assume that the divider will be a sequential divider and it will set the signal Ready to 1 when the quotient and remainder results are ready. The divider has an Asynchronous Reset after which in the next clock cycle it starts the division process if the Start signal is 1. The quotient and remainder willl maintain their values unless the divider is reset again. The module of the divider is given below where A is the dividend, B is the divider, Q is the quotient and R is the reminder:

module UDIV # (parameter n= 4)

(output [n-1:0] Q, R, output Ready,

input [n-1:0] A, B,

input Start, Reset, CLK);

DPath_DIV #(n) DPU(Q, R, CEN, DGEZ, LDR, ClearR, LDQ, SetQ0, LDB, Shift, INC, CLRC, CLK, A, B);

CU_DIV CU (LDR, ClearR, LDQ, SetQ0, LDB, Shift, INC, CLRC, Ready, Start, CLK, Reset, DGEZ, CEN);

endmodule

Part of the Datapath of the divider is given below:

The algorithm for performing sequential division is as follows:

- Set Quotient=Dividened, Set Remainder=0.

- Shift(Remainder,Quotient) Left by 1 bit

- Difference=Remainder-Divisor

- If (Difference( 0) Then

Remainder=Difference

Set Least Significant bit of Quotient to 1.

End If;

- If (#iterations<N) Then Goto Step 2.

An example of applying the algorithm for a 4-bit divider with dividened=1110 and divisor=0011 is given below. Note that the Quotient=0100 and the Remainder=0010.

The description of various signals is illustrated in the table below:

| Signal | Role |
| --- | --- |
| LDR | Load the remainder register |
| ClearR | Clear the remainder register |
| LDQ | Load the quotient register |
| SetQ0 | Set quotion register bit 0 to 1 |
| LDB | Load the B register with the divisor |
| Shift | Shift the quotient and remainder register one bit to the left |
| INC | Increment counter |
| CLRC | Clear counter |
| DGEZ | Set when difference is ≥ 0 |
| CEN | Set when counter is equal to n |

## Complete the Verilog model given below for modeling the Datapath of the divider.

module DPath_DIV #(parameter n=4)

(output reg [n-1:0] Q, R, output CEN, DGEZ,

input LDR, ClearR, LDQ, SetQ0, LDB, Shift, INC, CLRC, CLK,

input [n-1:0] A, B);

endmodule

## Write an ASMD chart for the control unit of the divider.

## Complete the Verilog model given below for modeling the Control Unit of the divider.

# module  CU_DIV (output reg LDR, ClearR, LDQ, SetQ0, LDB, Shift, INC, CLRC, Ready, input Start, CLK, Reset, DGEZ, CEN);

endmodule

[16 Points]

(Q4) It is required to model an Asynchronous FIFO (First-In-First-Out) memory queue. The FIFO has a parametrizable memory depth of upto K loctions with a parametrizable data width of N bits. The FIFO interface is given below:

The Reset signal is an Asynchronous reset and when set to 1 it will consider the content of FIFO empty and set the EMPTY flag to one and all other flags to 0. A handshaking mechanism is used for both writing and reading from the FIFO using the signal WR_EN, WR_ACK, RD_EN and RD_ACK. When WR_EN=1, the data in DIN input will be written to the available location in the FIFO as long as the FULL signal is not set to 1. If the FIFO is FULL the request is ignored and not acknolwdged. It is assumed that the WR_EN signal will remain 1 until a WR_ACK is set to 1 by the FIFO. After that, the WR_EN signal will go to 0. A similar handshaking mechanism is used for reading from the FIFO. When RD_EN=1, the data in the proper location will be output to DOUT  as long as the EMPTY signal is not set to 1. Then, the RD_ACK signal is set to 1. If the FIFO is EMPTY the request is ignored and not acknolwdged. It is very important to note that the FIFO should be able to read and write simultaneously if needed.

A read pointer is used to point at the location to be read from and a write pointer is used to point at the location to be written to. A counter is used to keep track of when the FIFO is full or empty.

Part of the FIFO mdoule is given below and you need to complete the following missing parts:

## Declare all the required variables for modeling the FIFO.

## The Read and Counter processes are given to you. Describe the write process for writing to the FIFO.

module FIFO #(parameter N=8, K=4, KS=2)

(output reg [N-1:0] DOUT,

output reg WR_ACK, RD_ACK, FULL, EMPTY,

input [N-1:0] DIN,

input Reset, WR_EN, RD_EN);

// Define required variables here

// Read Process

always @ (Reset, RD_EN, Count) begin

if (Reset) begin

RD_ACK = 0;

ReadP = 0;

EMPTY = 1;

DEC = 0;

end

else begin

if (RD_EN)

if (Count > 0) begin

DOUT = FIFO[ReadP];

if (ReadP < K-1)

ReadP = ReadP + 1;

else

ReadP = 0;

RD_ACK = 1;

DEC = 1;

@ (posedge DECA)	DEC = 0;

@ (negedge RD_EN)	RD_ACK = 0;							end

if (Count==0)

EMPTY = 1;

else

EMPTY = 0;

end

end // Read Process

// Write Process

// Counter Process

always @ (Reset, INC, DEC) begin

if (Reset==1) begin

Count = 0;

INCA = 0;

DECA = 0;

end

else begin

if (INC) begin

Count = Count + 1;

INCA = 1;

@ (negedge INC) INCA = 0;

end

if (DEC) begin

Count = Count - 1;

DECA = 1;

@ (negedge DEC) DECA = 0;

end

end

end // Counter Process

endmodule

# Text boxes

Reset

FIFO

K x N

EMPTY

RD_ACK

RD_EN

Dout[N-1:0]

FULL

WR_ACK

WR_EN

Din[N-1:0]

Difference

Shift Left

n-bit

n-bit

n-bit

Quotient

Remainder

Divisor

n-bit

SUB