Jan. 1, 2014

COMPUTER ENGINEERING DEPARTMENT

COE 405

DESIGN & MODELING OF DIGITAL SYSTEMS

Final Exam

First Semester  (131)

Time: 7:00-10:00 PM

OPEN BOOK EXAM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 14 |  |
| Q3 | 13 |  |
| Q4 | 13 |  |
| Q5 | 40 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

[20 Points]

# (Q1) Determine possible circuits that will be synthesized by each of the following modules:

- module FinalQ1_1 (output reg Dout1, Dout2, input A, B, C, D, sel, clk);

always @ (posedge clk) begin

Dout1 <= A & B; Dout2 <= Dout1 ^ C;

if (sel) Dout1 <= Dout2 | D;

end

endmodule

- module FinalQ1_2 (output reg [3:0] DOUT, input DIN, clock, reset);

always @ (posedge clock,  posedge reset) begin

if (reset) DOUT <= 0;

else begin

DOUT[0]<=DIN;

DOUT[1]<=DOUT[0];

DOUT[2]<=DOUT[1];

DOUT[3]<=DOUT[2];

end

end

endmodule

- module FinalQ1_3 (output reg E, input A, B, C, D);

always @(A,B, C, D) begin

case ({A,B})

2'b10:  E = C & D;

2'b01:  E = C | D;

endcase

end

endmodule

- module FinalQ1_4 #(parameter n=3)(output  reg C, D, output E, input [n-1:0] A, B);

integer k;

assign E = ~(C | D);

always @ (A, B) begin

C = 0; D = 0;

for (k=n-1; k>=0; k=k-1) begin

C = C | A[k] & ~B[k] & ~D;

D = D | ~A[k] & B[k] & ~C;

end

end

endmodule

- module FinalQ1_5 #(parameter n=4) (output reg [n-1:0] R1, R2, R3,  input CLK, RST, R1in, R2in, R3in, R1out, R2out, R3out, Dout, input [n-1:0] Data);

wire [n-1:0] Cbus;

always @ (posedge CLK, posedge RST) begin

if (RST) begin R1 <= 0; R2 <= 0; R3 <= 0;	end

else begin

if (R1in) R1 <= Cbus;

if (R2in) R2 <= Cbus;

if (R3in) R3 <= Cbus;

end

end

assign Cbus = R1out? R1:{n{1'bz}};

assign Cbus = R2out? R2:{n{1'bz}};

assign Cbus = R3out? R3:{n{1'bz}};

assign Cbus = Dout? Data:{n{1'bz}};

endmodule

[14 Points]

# (Q2) It is required to design a circuit to compute the equation Y=(A+B)-(C+D) using only a single adder. Assume that the 4-bit  inputs  will hold their values until the end of the operation. Also, assume that the inputs will be ready when a Start input is asserted. Assume that a Done signal will be set when the result is ready and the result will remain held until the next Start operation.

## Show a schedule of the operations with minimum latency (i.e., clock cycles) satisfying the area constraints.

## Show the DataPath design of your circuit indicating all the control signals and the adder size.

## Show the ASMD diagram of your control unit.

[13 Points]

# (Q3) It is required to design a Vending Machine Controller. The machine takes one Riyal only. For each one Riyal inserted, the input signal Ri is asserted. The machine can dispense: Water: 2 Riyals (input W), Cola: 2 Riyals (input C), Juice: 3 Riyals (input J).  A product is dispensed in one clock cycle after an input selection. The machine has a money return button (input R). When this button is pressed, all the inserted money is returned. It is assumed that only one input may be active at a time. If more than 3 Riyals are inserted, the extra money is automatically returned. If 3 Riyals are inserted and the user selects Water or Cola, the requested product is dispensed along with the return of one Riyal. Outputs are as follows: MRo: Money Return Out (all inserted money in the machine), Wo: Water Out, Co: Cola Out, Jo: Juice Out, Ro: One Riyal Out. Show a state diagram for modeling the Vending Machine Controller.

[13 Points]

# (Q4) The functional unit UART_Clock_Generator given below can be used to generate a set of baud rate signal pairs for use in UART.

The table below shows the clock frequency pairs that are generated if Sys_Clock is 8 MHZ.

| Sel_Baud_Rate | Sample_Clk (HZ) | Clock (HZ) |
| --- | --- | --- |
| 000 | 307,692 | 38,462 |
| 001 | 153,846 | 19,231 |
| 010 | 76,923 | 9,615 |
| 011 | 38,463 | 4,808 |
| 100 | 19,231 | 2,404 |
| 101 | 9,615 | 1,202 |
| 110 | 4,808 | 601 |
| 111 | 2,404 | 301 |

Write a synthesizble Verilog model for the UART_Clock_Generator. The signal reset_ is  an asynchronous active low reset.

[40 Points]

# (Q5) Bubble Sort is a well known sorting algorithm. The psuedo code for the sorting algorithm is given below:

for i=2 to N

for j=N downto i

if [A[j-1] > A[j] then

begin

Temp = A[j-1];

A[j-1] = A[j];

A[j] = Temp;

end

It is required to write a synthesizable Verilog model for implementing the Bubble Sort algorithm. The ASMD chart and block diagram of a machine that executes the Bubble Sort algorithm is given below.

The machine is parametrizable with the number of words to be sorted as N and the word size as word_size. It is assumed that once the user sets the Load signal to 1, a set of N words will be sent through Data_in input serially in the next N clock cycles and loaded into an internal memory. Then when the signal Sort is asserted, the algorithm starts sorting. Once sorting is finished and the user asserts Send signal, the sorted data will be sent serially through Data_out in the next N clock cycles.

The bubble sort module is given below:

module Bubble_Sort # ( parameter N = 8, word_size = 4)(

output [word_size -1: 0] Data_out,

output Ready, Busy, Waiting,

input [word_size -1: 0] Data_in,

input Load, Sort, Send, clk, rst);

Controller M0 (Ready, Busy, Waiting, ld, set_i, incr_i, set_j, decr_j, clr_k, incr_k,

swap, snd, Load, Sort, Send, gt, i_lte_N, j_gte_i, done, clk, rst);

Datapath M1 (Data_out, gt, i_lte_N, j_gte_i, done, Data_in,

ld, set_i, incr_i, set_j, decr_j, clr_k, incr_k, swap, snd, clk);

endmodule

- Write a parametrizable Verilog model BSDatapath to model the datapath of the Bubble_Sort module. The parameters are the number of words to be sorted N and the word size word_size.

- Write a Verilog model BSController to model the control unit of the Bubble_Sort module.

- Write a Verilog test bench for the Bubble_Sort module to sort 8 words of test data sent serially as 1 followed by 2, 3, 4, 5, 6, 7 and 8. Assume a CLK of 10 ns period with 50% duty cycle. Your test bench should generate the CLK.