COE 405, Term 152

Design & Modeling of Digital Systems

HW# 1   Solution

Due date: Thursday, Feb. 11

# Consider the two functions f=a ( b ( c and g=a b + a c + b c.

## Implement the function g using only 2x1 MUXs.

g = a' [ b c] + a [b + c] = a' [ b' [0] + b [c] ] + a [ b'[c] + b[1] ]

## Compute the function f(g based on orthonormal basis expansion.

f = a'b' [c] + a'b [c'] + ab' [c'] + ab [c]

g = a'b' [0] + a'b [c] + ab' [c] + ab [1]

f(g = a'b' [c] + a'b [1] + ab' [1] + ab [c'] = a'b'c + a'b + ab' + abc' = a'c + a'b + ab' + ac'

# It is required to design a combinational circuit that computes the equation Y=3*X-1, where X is an n-bit signed 2's complement number.

## Design the circuit as a modular circuit where each module receives a single bit of the input, Xi.

This circuit can be designed by assuming that we have a borrow feeding the first cell or by representing -1 in 2's complement as 11…111 and adding this 1 ion each cell. I will follow the second approach. We need to represent carry-out values in the range 0 to 3. Thus, we need to signals to represent Carry out values.

## Derive the truth table of your 1-bit module in (i).

| C1i-1 | C0i-1 | Xi | C1i | C0i | Zi |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 |
| 1 | 0 | 0 | 0 | 1 | 1 |
| 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 1 | 1 |

## Derive minimized two-level sum-of-product equations for your 1-bit module circuit.

Z= (C0i-1 ( Xi)'

C0i = C1i-1  C0i-1' + C1i-1  Xi + C1i-1'  C0i-1 Xi' = C1i-1  (C0i-1' + Xi) + C1i-1'  C0i-1 Xi' = C1i-1 ((C0i-1 Xi')

C1i = Xi + C1i-1  C0i-1

## Verify the correctness of your design by modeling and simulating a circuit to compute the required equation assuming X is a 4-bit number using logicworks.

Note that for values whose correct result will not fit in 4-bits such as values ≥ 6 will not produce correct results. We need to use larger number of cells to ensure that the correct output will fit.