COE 405, Term 062

Design & Modeling of Digital Systems

HW# 2

Due date: Monday, March 26, 2007

# It is required to design an 8-bit shift register. The shift register should be able to shift or rotate either left or right based on the following table:

| S1 S0 | Operation |
| --- | --- |
| 00 | Shift left |
| 01 | Shift right |
| 10 | Rotate left |
| 11 | Rotate right |

# The reset is a synchronous reset and the shift register is rising-edge triggered. Assume that the shifted bit is based on the input SI. The interface description of the 8-bit shifter is shown below.

## Describe an Entity Shifter8 for the 8-bit shift register.

## Model a behavioral Architecture Behave for this 8-bit shift register. Verify its correctness by simulation.

## Model a structural Architecture Struct for this 8-bit shift register. Make your model generic using GENERATE statement to instantiate the required components such that your design can be extended into a shift register of any size by changing just a size parameter. Use configuration statement to configure the bounding of used components to entities. Verify the correctness of your model by simulation.

# Problem 4.15.

# Text boxes

8-bit Shift Register

S7-S0

SI

reset

clk

S1

S0