COE 405, Term 131

Design & Modeling of Digital Systems

HW# 2

Due date: Wednesday, October 9

# It is required to design a sequential circuit that has a single input X and a single output Y. The circuit receives an unsigned number serially through the input X from the least significant bit (LSB) to the most significant bit (MSB), and computes the equation 5*X and generates the output serially from the least significant bit to the most significant bit. The circuit has an additional reset input R which resets the circuit into an initial state. The following are examples of input and output data:

Examples:

| Input | X | 0 | 1 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 0 | 1 | 1 | 1 | 1 |

| Input | X | 1 | 1 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 1 | 1 | 1 | 1 | 0 |

## Draw the state diagram of the circuit assuming a Mealy model.

## Implement the circuit using D-FFs.

## Verify the correctness of your circuit by simulation.

# Consider the given FSM that has 5 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S1 | S3, 1 | S5, 0 |
| S2 | S3, 0 | S5, 1 |
| S3 | S2, 0 | S1, 1 |
| S4 | S4, 0 | S5, 1 |
| S5 | S4, 1 | S1, 0 |

## Determine the equivalent states.

## Reduce the state table into the minimum number of states and show the reduced state table.

# Consider the given FSM that has 4 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S0, 0 | S1, 0 |
| S1 | S2, 0 | S3, 0 |
| S2 | S0, 0 | S1, 1 |
| S3 | S2, 0 | S3, 0 |

## Implement the FSM using the following state assignment: S0=00, S1=10, S2=01, S3=11.

## Implement the FSM using the following state assignment: S0=11, S1=01, S2=00, S3=10.

## Verify that the two circuits are equivalent by simulation by applying the following input sequence: {0,1,0,1,1,0,1,0,1,0,0}.

# Text boxes

Output=15

Input=3

LSB

MSB

Output=30

Input=6

LSB

MSB