COE 405, Term 062

Design & Modeling of Digital Systems

HW# 3   Solution

Due date: Monday, April 16, 2007

# You are required to model an ALU that has the following entity description:

# Entity ALU is

# Generic (N: Natural :=4);

# Port (A, B: IN Bit_Vector(N-1 Downto 0);

# Cin: IN Bit;

# Sel: IN Bit_Vector(2 Downto 0);

# C: OUT Bit_Vector(N-1 Downto 0);

# Cout, SignF, OverflowF, ZeroF: OUT BIT

# );

# End;

# The ALU performs one of eight different functions according to selection line inputs as shown in the table given below:

| Sel | Function |
| --- | --- |
| 000 | C=A+B |
| 001 | C=A+B+Cin |
| 010 | C=A-B |
| 011 | C=A-B-Cin |
| 100 | C=B+1 |
| 101 | C=B-1 |
| 110 | C=B |
| 111 | C=2*B |

# The four flags Cout, SignF, OverflowF and ZeroF are computed according to the result. Note that the Cout flag is considered a borrow when a subtraction operation is performed.

## Model the following two functions, “+” and “-“, to support addition and subtraction on Bit_Vector. Model the functions by converting Bit_Vector type to Integer, perform the required operation in integer and then convert the result back to Bit_Vector type. Assume that the returned result has length one extra bit more than the inputs to return the carry out.

## Function 	"+" ( l, r : Bit_Vector ) RETURN Bit_vector IS

## Function 	"-" ( l, r : Bit_Vector ) RETURN Bit_vector IS

Subtype SInteger is Integer Range -2**(N+1)to 2**(N+1)-1;

Function Bin2Int(Bin: Bit_Vector) return SInteger is

variable SUM: SInteger:=0;

begin

-- convert to integer as unsigned

For I IN 0 To (Bin'Length - 1) Loop

if Bin(I)='1' then

SUM := SUM + (2**I);

end if;

End Loop;

return SUM;

end Bin2Int;

Procedure Int2Bin (Int: IN SInteger; Bin : OUT BIT_VECTOR)  IS

Variable Tmp: SInteger;

Constant size: Natural := Bin'length;

Begin

Tmp := Int;

if (Tmp < 0) Then

Tmp :=2**size+Tmp;

End If;

For I IN 0 To (Bin'Length - 1) Loop

If ( Tmp MOD 2 = 1) Then

Bin(I) := '1';

Else Bin(I) := '0';

End If;

Tmp := Tmp / 2;

End Loop;

End Int2Bin;

Function 	"+" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable IRes: SInteger;

Variable Result: Bit_Vector(l'length downto 0);

Begin

IRes := Bin2Int(l) + Bin2Int(r);

Int2Bin(IRes, Result);

Return Result;

End "+";

Function 	"-" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable IRes: SInteger;

Variable Result: Bit_Vector(l'length downto 0);

Begin

IRes := Bin2Int(l) - Bin2Int(r);

Int2Bin(IRes, Result);

Return Result;

End "-";

## Write a behavioral model for modeling the ALU using the developed functions in (i).

Architecture BM of ALU is

Begin

Process(A, B, Cin, Sel)

Variable Tmp: Bit_Vector (A'length Downto 0);

Variable Tmp2: Bit_Vector (A'length-1 Downto 0);

Variable Tmp3 : Bit_Vector (A'length Downto 0);

Variable Zero: Bit_Vector (A'length-1 Downto 0) := (N-1 Downto 0=>'0');

Begin

Case Sel is

When "000" =>   Tmp := A + B;

Cout <= Tmp(N); C <= Tmp(N-1 Downto 0);

if (Tmp(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) = B(N-1)) AND (Tmp(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp(N-1);

When "001" =>   Tmp  := A + B;

Tmp2 := ((N-1 Downto 1=>'0')&Cin);

Tmp3 := Tmp(N-1 Downto 0) + Tmp2;

C <= Tmp3(N-1 Downto 0);

If (Tmp(N)='1' OR Tmp3(N)='1') Then

Cout <= '1';

else

Cout <= '0';

end if;

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) = B(N-1)) AND (Tmp3(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "010" =>   Tmp := A - B;

Cout <= Tmp(N); C <= Tmp(N-1 Downto 0);

if (Tmp(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) /= B(N-1)) AND (Tmp(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp(N-1);

When "011" =>   Tmp := A - B;

Tmp2 := ((N-1 Downto 1=>'0')&Cin);

Tmp3 := Tmp(N-1 Downto 0) - Tmp2;

C <= Tmp3(N-1 Downto 0);

If (Tmp(N)='1' OR Tmp3(N)='1') Then

Cout <= '1';

else

Cout <= '0';

end if;

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) /= B(N-1)) AND (Tmp3(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "100" =>

Tmp2 := ((N-1 Downto 1=>'0')&'1');

Tmp3 := B + Tmp2;

C <= Tmp3(N-1 Downto 0);

Cout <= Tmp3(N);

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (B(N-1) = Tmp2(N-1)) AND (Tmp3(N-1) /= B(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "101" =>

Tmp2 := ((N-1 Downto 1=>'0')&'1');

Tmp3 := B - Tmp2;

C <= Tmp3(N-1 Downto 0);

Cout <= Tmp3(N);

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (B(N-1) /= Tmp2(N-1)) AND (Tmp3(N-1) /= B(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "110" =>

Cout <= '0'; C <= B;

if (B(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

OverflowF <= '0';

Signf <= B(N-1);

When "111" =>   Tmp := B + B;

Cout <= Tmp(N); C <= Tmp(N-1 Downto 0);

if (Tmp(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) = B(N-1)) AND (Tmp(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp(N-1);

End Case;

End Process;

End;

## Write a test bench for testing the n-bit ALU assuming that the input arguments are read from an input file and that the output will be stored in an output file. Use TEXTIO package for this purpose. Apply the following values for testing the correct operation of a 4-bit ALU:

| ALU Select | Input A | Input B | Cin |
| --- | --- | --- | --- |
| 000 | 5 | 2 |  |
| 000 | -8 | 7 |  |
| 000 | 7 | 7 |  |
| 000 | -7 | -2 |  |
| 000 | -1 | 1 |  |
| 000 | -1 | -1 |  |
| 001 | -1 | 1 | 1 |
| 001 | -1 | -1 | 0 |
| 001 | -1 | -1 | 1 |
| 001 | -1 | 0 | 1 |
| 010 | 3 | 4 |  |
| 010 | -8 | 7 |  |
| 010 | -7 | -1 |  |
| 010 | -7 | 2 |  |
| 011 | -7 | 1 | 1 |
| 011 | 3 | 2 | 1 |
| 011 | -8 | 1 | 1 |
| 100 |  | -1 |  |
| 100 |  | 1 |  |
| 100 |  | 7 |  |
| 101 |  | 0 |  |
| 101 |  | -1 |  |
| 101 |  | -8 |  |
| 101 |  | 7 |  |
| 110 |  | -1 |  |
| 110 |  | 7 |  |
| 111 |  | -1 |  |
| 111 |  | 3 |  |
| 111 |  | 7 |  |

The output should be stored in the output file using the following format:

ALU Operation	Input A     Input B     Result	 Cout   Signf   OverflowF    ZeroF

C=A+B		    5	         2		  7	    0         0             0	           0

USE STD.TEXTIO.ALL;

Entity ALU_test is

End;

Architecture Test of ALU_test is

Component ALU

Generic (N: Natural :=4);

Port (A, B: IN Bit_Vector(N-1 Downto 0);

Cin: IN Bit;

Sel: IN Bit_Vector(2 Downto 0);

C: OUT Bit_Vector(N-1 Downto 0);

Cout, SignF, OverflowF, ZeroF: OUT BIT

);

End Component;

For ALL: ALU Use Entity work.alu(BM);

Constant N: Positive :=4;

Constant K: Positive :=30;

Constant Period: Time := 100 ns;

TYPE Integers IS ARRAY (NATURAL RANGE <>) of INTEGER;

TYPE Vectors IS ARRAY (NATURAL RANGE <>) of Bit_Vector(2 downto 0);

TYPE Bits IS ARRAY (NATURAL RANGE <>) of Bit;

Procedure Int2Bin (Int: IN Integer; Bin : OUT BIT_VECTOR)  IS

Variable Tmp: Integer;

Constant size: Natural := Bin'length;

Begin

Tmp := Int;

if (Tmp < 0) Then

Tmp :=2**size+Tmp;

End If;

For I IN 0 To (Bin'Length - 1) Loop

If ( Tmp MOD 2 = 1) Then

Bin(I) := '1';

Else Bin(I) := '0';

End If;

Tmp := Tmp / 2;

End Loop;

End Int2Bin;

Procedure Apply_Data (

Signal Target: OUT Bit_Vector;

Constant Values: IN Integers;

Constant Period: IN Time) IS

Variable Buf: Bit_Vector(Target'range);

Begin

For I IN 0 To Values'length-1 Loop

Int2Bin (Values(I), Buf);

Target <= Transport Buf After I * Period;

End Loop;

End Apply_Data;

Procedure Apply_Data (

Signal Target: OUT Bit_Vector;

Constant Values: IN Vectors;

Constant Period: IN Time) IS

Begin

For I IN 0 To Values'length-1 Loop

Target <= Transport Values(I) After I * Period;

End Loop;

End Apply_Data;

Procedure Apply_Data (

Signal Target: OUT Bit;

Constant Values: IN Bits;

Constant Period: IN Time) IS

Begin

For I IN 0 To Values'length-1 Loop

Target <= Transport Values(I) After I * Period;

End Loop;

End Apply_Data;

function Bin2Int(Bin: Bit_Vector) return integer is

variable SUM: INTEGER:=0;

begin

-- convert to integer as unsigned

For I IN 0 To (Bin'Length - 1) Loop

if Bin(I)='1' then

SUM := SUM + (2**I);

end if;

End Loop;

-- if negative

if (Bin(Bin'Length -1)='1') then

-- 2's complement

SUM := 2**(Bin'Length)-SUM;

-- set the negaive sign

SUM := -SUM;

end if;

return SUM;

end Bin2Int;

Signal A, B, C: Bit_Vector(N-1 Downto 0);

Signal Cin, Cout, SignF, OverflowF, ZeroF: Bit;

Signal Sel: Bit_Vector(2 Downto 0);

Signal First, Second: Integers(0 to K-1);

Signal SelA: Vectors(0 to k-1);

Signal Carryin: Bits(0 to k-1);

Begin

Process

File Infile : Text IS IN "alu_input.txt";

Variable My_Line : Line;

Variable val: Integer;

Variable sval: Bit_Vector(2 downto 0);

Variable cval : Bit;

File outFile: Text IS OUT "alu_output.txt";

Variable write_line: Line;

Variable Str: String(1 to 67);

Variable Str2: String(1 to 13);

Variable Str3: String(1 to 85);

Variable i,j: integer :=0;

Begin

While Not ( Endfile(Infile) )  Loop

Readline( Infile, My_Line);           -- read a line from the input file

Read( My_Line, sval);	       -- read select value

SelA(i) <= sval;

Case sval is

When "000" | "010" =>

Read( My_Line, val);	         -- read A value from the line

First(i)<= val;

Read( My_Line, val);	         -- read B value from the line

Second(i)<= val;

Carryin(i) <= '0';

When "001" | "011" =>

Read( My_Line, val);	         -- read A value from the line

First(i)<= val;

Read( My_Line, val);	         -- read B value from the line

Second(i)<= val;

Read( My_Line, cval);      -- read Cin value from the line

Carryin(i) <= cval;

When Others =>

First(i)<= 0;

Read( My_Line, val);	         -- read B value from the line

Second(i)<= val;

Carryin(i) <= '0';

End Case;

i := i + 1;

End Loop;

-- added code to write sum's into a file ---

wait for 10 ns;

Str :="ALU Operation"&ht&"Input A"&ht&"Input B"&ht&"Cin"&ht&"Result"&ht&"Cout"&ht&"Signf"&ht&"OverflowF"&ht&"ZeroF";

Write(write_line,Str);

Writeline(outFile, write_line);

Str3 :="-------------------------------------------------------------------------------------";

Write(write_line,Str3);

Writeline(outFile, write_line);

j:=0;

while (j < i) loop

sval := SelA(j);

Case Sval is

When "000" =>

str2 := "C=A+B        ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line, First(j));

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "001" =>

str2 := "C=A+B+Cin    ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line, First(j));

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line, Carryin(j));

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "010" =>

str2 := "C=A-B        ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line, First(j));

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "011" =>

str2 := "C=A-B-Cin    ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line, First(j));

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line, Carryin(j));

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "100" =>

str2 := "C=B+1        ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "101" =>

str2 := "C=B-1        ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "110" =>

str2 := "C=B          ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

When "111" =>

str2 := "C=2*B        ";

Write(write_line,str2);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Bin2Int(C));

Write(write_line,ht);

Write(write_line, Cout);

Write(write_line,ht);

Write(write_line, Signf);

Write(write_line,ht);

Write(write_line, OverflowF);

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, ZeroF);

Writeline(outFile, write_line);

End Case;

j := j + 1;

wait for Period;

End loop;

wait;

End Process;

Apply_data(A, First, Period);

Apply_data(B, Second, Period);

Apply_data(Cin, Carryin, Period);

Apply_data(Sel, SelA, Period);

CUT: ALU Generic Map (N) Port Map (A, B, Cin, Sel, C, Cout, SignF, OverflowF, ZeroF);

End;

Resulting output file from running the test bench:

ALU Operation	Input A	Input B	Cin	Result	Cout	Signf	OverflowF	ZeroF

---------------------------------------------------------------------------------------------------------------------------

C=A+B        	5	2		7	0	0	0		0

C=A+B        	-8	7		-1	0	1	0		0

C=A+B        	7	7		-2	0	1	1		0

C=A+B        	-7	-2		7	1	0	1		0

C=A+B        	-1	1		0	1	0	0		1

C=A+B        	-1	-1		-2	1	1	0		0

C=A+B+Cin    	-1	1	1	1	1	0	0		0

C=A+B+Cin    	-1	-1	0	-2	1	1	0		0

C=A+B+Cin    	-1	-1	1	-1	1	1	0		0

C=A+B+Cin    	-1	0	1	0	1	0	0		1

C=A-B      	  	3	4		-1	1	1	0		0

C=A-B      	  	-8	7		1	0	0	1		0

C=A-B        		-7	-1		-6	1	1	0		0

C=A-B      	  	-7	2		7	0	0	1		0

C=A-B-Cin    	-7	1	1	7	0	0	1		0

C=A-B-Cin    	3	2	1	0	0	0	0		1

C=A-B-Cin    	-8	1	1	6	0	0	1		0

C=B+1        			-1		0	1	0	0		1

C=B+1        			1		2	0	0	0		0

C=B+1        			7		-8	0	1	1		0

C=B-1        			0		-1	1	1	0		0

C=B-1        			-1		-2	0	1	0		0

C=B-1        			-8		7	0	0	1		0

C=B-1        			7		6	0	0	0		0

C=B          			-1		-1	0	1	0		0

C=B          			7		7	0	0	0		0

C=2*B        			-1		-2	1	1	0		0

C=2*B        			3		6	0	0	0		0

C=2*B        			7		-2	0	1	1		0

## Define a package called HW3 where you store all used types, subtypes, functions and procedures inside the package and use the package when needed.

Package HW3 is

Constant N: Positive :=4;

Subtype SInteger is Integer Range -2**(N+1)to 2**(N+1)-1;

TYPE Integers IS ARRAY (NATURAL RANGE <>) of INTEGER;

TYPE Vectors IS ARRAY (NATURAL RANGE <>) of Bit_Vector(2 downto 0);

TYPE Bits IS ARRAY (NATURAL RANGE <>) of Bit;

Function Bin2Int(Bin: Bit_Vector) return SInteger;

Procedure Int2Bin (Int: IN SInteger; Bin : OUT BIT_VECTOR);

Function 	"+" ( l,r : Bit_Vector ) RETURN Bit_vector;

Function 	"-" ( l,r : Bit_Vector ) RETURN Bit_vector;

Procedure Apply_Data (

Signal Target: OUT Bit_Vector;

Constant Values: IN Integers;

Constant Period: IN Time);

Procedure Apply_Data (

Signal Target: OUT Bit_Vector;

Constant Values: IN Vectors;

Constant Period: IN Time);

Procedure Apply_Data (

Signal Target: OUT Bit;

Constant Values: IN Bits;

Constant Period: IN Time);

Function Bin2Ints(Bin: Bit_Vector) return integer;

End;

Package Body HW3 is

Function Bin2Int(Bin: Bit_Vector) return SInteger is

variable SUM: SInteger:=0;

begin

-- convert to integer as unsigned

For I IN 0 To (Bin'Length - 1) Loop

if Bin(I)='1' then

SUM := SUM + (2**I);

end if;

End Loop;

return SUM;

end Bin2Int;

Procedure Int2Bin (Int: IN SInteger; Bin : OUT BIT_VECTOR)  IS

Variable Tmp: SInteger;

Constant size: Natural := Bin'length;

Begin

Tmp := Int;

if (Tmp < 0) Then

Tmp :=2**size+Tmp;

End If;

For I IN 0 To (Bin'Length - 1) Loop

If ( Tmp MOD 2 = 1) Then

Bin(I) := '1';

Else Bin(I) := '0';

End If;

Tmp := Tmp / 2;

End Loop;

End Int2Bin;

Function 	"+" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable IRes: SInteger;

Variable Result: Bit_Vector(l'length downto 0);

Begin

IRes := Bin2Int(l) + Bin2Int(r);

Int2Bin(IRes, Result);

Return Result;

End "+";

Function 	"-" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable IRes: SInteger;

Variable Result: Bit_Vector(l'length downto 0);

Begin

IRes := Bin2Int(l) - Bin2Int(r);

Int2Bin(IRes, Result);

Return Result;

End "-";

Procedure Apply_Data (

Signal Target: OUT Bit_Vector;

Constant Values: IN Integers;

Constant Period: IN Time) IS

Variable Buf: Bit_Vector(Target'range);

Begin

For I IN 0 To Values'length-1 Loop

Int2Bin (Values(I), Buf);

Target <= Transport Buf After I * Period;

End Loop;

End Apply_Data;

Procedure Apply_Data (

Signal Target: OUT Bit_Vector;

Constant Values: IN Vectors;

Constant Period: IN Time) IS

Begin

For I IN 0 To Values'length-1 Loop

Target <= Transport Values(I) After I * Period;

End Loop;

End Apply_Data;

Procedure Apply_Data (

Signal Target: OUT Bit;

Constant Values: IN Bits;

Constant Period: IN Time) IS

Begin

For I IN 0 To Values'length-1 Loop

Target <= Transport Values(I) After I * Period;

End Loop;

End Apply_Data;

Function Bin2Ints(Bin: Bit_Vector) return integer is

variable SUM: INTEGER:=0;

begin

-- convert to integer as unsigned

For I IN 0 To (Bin'Length - 1) Loop

if Bin(I)='1' then

SUM := SUM + (2**I);

end if;

End Loop;

-- if negative

if (Bin(Bin'Length -1)='1') then

-- 2's complement

SUM := 2**(Bin'Length)-SUM;

-- set the negaive sign

SUM := -SUM;

end if;

return SUM;

end Bin2Ints;

End;

## Synthesize the modeled ALU in (ii) using Xilinx Project Navigator and report on the total equivalent gate count for design after mapping and the longest delay in the design based on Post-Map static timing report.

Total equivalent gate=609

Longest delay in the design= 11.787ns.

## Remodel the functions in (i), “+” and “-“, based on performing the operation using a ripple carry add like functionality. Change the ALU model based on the use of these two newly modeled functions and reapply the same test bench modeled in (iii) to verify the correct functionality of the ALU.

Architecture BM2 of ALU is

Function 	"+" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable Sum: Bit_Vector(l'length downto 0);

Variable P, G: Bit_Vector(l'length-1 downto 0);

Variable C: Bit_Vector(l'length downto 0);

Begin

C(0) := '0';

For i in 0 to N-1 Loop

P(i) := l(i) XOR r(i);

G(i) := l(i) AND r(i);

Sum(i) := P(i) XOR C(i);

C(i+1)  := G(i) OR (P(i) AND C(i));

End Loop;

Sum(l'length) := C(l'length);

Return Sum;

End "+";

Function 	"-" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable Sum: Bit_Vector(l'length downto 0);

Variable P, G: Bit_Vector(l'length-1 downto 0);

Variable C: Bit_Vector(l'length downto 0);

Begin

C(0) := '1';

For i in 0 to N-1 Loop

P(i) := l(i) XOR Not r(i);

G(i) := l(i) AND Not r(i);

Sum(i) := P(i) XOR C(i);

C(i+1)  := G(i) OR (P(i) AND C(i));

End Loop;

Sum(l'length) := C(l'length);

Return Sum;

End "-";

Begin

Process(A, B, Cin, Sel)

Variable Tmp: Bit_Vector (A'length Downto 0);

Variable Tmp2: Bit_Vector (A'length-1 Downto 0);

Variable Tmp3 : Bit_Vector (A'length Downto 0);

Variable Zero: Bit_Vector (A'length-1 Downto 0) := (N-1 Downto 0=>'0');

Begin

Case Sel is

When "000" =>   Tmp := A + B;

Cout <= Tmp(N); C <= Tmp(N-1 Downto 0);

if (Tmp(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) = B(N-1)) AND (Tmp(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp(N-1);

When "001" =>   Tmp  := A + B;

Tmp2 := ((N-1 Downto 1=>'0')&Cin);

Tmp3 := Tmp(N-1 Downto 0) + Tmp2;

C <= Tmp3(N-1 Downto 0);

If (Tmp(N)='1' OR Tmp3(N)='1') Then

Cout <= '1';

else

Cout <= '0';

end if;

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) = B(N-1)) AND (Tmp3(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "010" =>   Tmp := A - B;

Cout <= Not Tmp(N); C <= Tmp(N-1 Downto 0);

if (Tmp(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) /= B(N-1)) AND (Tmp(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp(N-1);

When "011" =>   Tmp := A - B;

Tmp2 := ((N-1 Downto 1=>'0')&Cin);

Tmp3 := Tmp(N-1 Downto 0) - Tmp2;

C <= Tmp3(N-1 Downto 0);

If (Tmp(N)='1' OR Tmp3(N)='1') Then

Cout <= '0';

else

Cout <= '0';

end if;

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) /= B(N-1)) AND (Tmp3(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "100" =>

Tmp2 := ((N-1 Downto 1=>'0')&'1');

Tmp3 := B + Tmp2;

C <= Tmp3(N-1 Downto 0);

Cout <= Tmp3(N);

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (B(N-1) = Tmp2(N-1)) AND (Tmp3(N-1) /= B(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "101" =>

Tmp2 := ((N-1 Downto 1=>'0')&'1');

Tmp3 := B - Tmp2;

C <= Tmp3(N-1 Downto 0);

Cout <= Not Tmp3(N);

if (Tmp3(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (B(N-1) /= Tmp2(N-1)) AND (Tmp3(N-1) /= B(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp3(N-1);

When "110" =>

Cout <= '0'; C <= B;

if (B(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

OverflowF <= '0';

Signf <= B(N-1);

When "111" =>   Tmp := B + B;

Cout <= Tmp(N); C <= Tmp(N-1 Downto 0);

if (Tmp(N-1 Downto 0) = Zero) Then

ZeroF <= '1';

else

ZeroF <= '0';

end if;

if ( (A(N-1) = B(N-1)) AND (Tmp(N-1) /= A(N-1)) ) 	Then

OverflowF <= '1';

else

OverflowF <= '0';

End if;

Signf <= Tmp(N-1);

End Case;

End Process;

End;

Running the test bench on thos model of the ALU produced the results shown below which are identical to the first model:

ALU Operation	Input A	Input B	Cin	Result	Cout	Signf	OverflowF	ZeroF

---------------------------------------------------------------------------------------------------------------------------

C=A+B        	5	2		7	0	0	0		0

C=A+B        	-8	7		-1	0	1	0		0

C=A+B        	7	7		-2	0	1	1		0

C=A+B        	-7	-2		7	1	0	1		0

C=A+B        	-1	1		0	1	0	0		1

C=A+B        	-1	-1		-2	1	1	0		0

C=A+B+Cin    	-1	1	1	1	1	0	0		0

C=A+B+Cin    	-1	-1	0	-2	1	1	0		0

C=A+B+Cin    	-1	-1	1	-1	1	1	0		0

C=A+B+Cin    	-1	0	1	0	1	0	0		1

C=A-B      	  	3	4		-1	1	1	0		0

C=A-B      	  	-8	7		1	0	0	1		0

C=A-B      	  	-7	-1		-6	1	1	0		0

C=A-B      	  	-7	2		7	0	0	1		0

C=A-B-Cin    	-7	1	1	7	0	0	1		0

C=A-B-Cin    	3	2	1	0	0	0	0		1

C=A-B-Cin    	-8	1	1	6	0	0	1		0

C=B+1        			-1		0	1	0	0		1

C=B+1        			1		2	0	0	0		0

C=B+1        			7		-8	0	1	1		0

C=B-1        			0		-1	1	1	0		0

C=B-1        			-1		-2	0	1	0		0

C=B-1        			-8		7	0	0	1		0

C=B-1        			7		6	0	0	0		0

C=B          			-1		-1	0	1	0		0

C=B          			7		7	0	0	0		0

C=2*B        			-1		-2	1	1	0		0

C=2*B        			3		6	0	0	0		0

C=2*B        			7		-2	0	1	1		0

## Synthesize the modeled ALU in (vi) using Xilinx Project Navigator and report on the total equivalent gate count for design after mapping and the longest delay in the design based on Post-Map static timing report. Compare the gate count and maximum delay obtained with that obtained in (v). What are your observations and conclusions?

Total equivalent gate= 504.

Longest delay in the design= 10.768ns.

We noticed that this implementation has resulted in less area and less delay. This is because the conversion function from binary to integer in the first ALU has been implemented in hardware which is a costly solution.

## Remodel the functions in (i), “+” and “-“, based on performing the operation using a cascaded 4-bit carry-look-ahead like functionality. Change the ALU model based on the use of these two newly modeled functions and reapply the same test bench modeled in (iii) to verify the correct functionality of the ALU.

The two remodeled functions are shown below and the ALU architecture is exactly the same as the one given in (vi).

Function 	"+" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable Sum: Bit_Vector(l'length downto 0);

Variable P, G: Bit_Vector(l'length-1 downto 0);

Variable C: Bit_Vector(l'length downto 0);

Begin

C(0) := '0';

For i in 0 to N-1 Loop

P(i) := l(i) XOR r(i);

G(i) := l(i) AND r(i);

End Loop;

For i in 0 to (N/4)-1 Loop

C(i*4+1)  := G(i*4+0) OR (P(i*4+0) AND C(i*4+0));

C(i*4+2)  := G(i*4+1) OR (P(i*4+1) AND G(i*4+0)) OR (P(i*4+1) AND P(i*4+0) AND C(i*4+0));

C(i*4+3)  := G(i*4+2) OR (P(i*4+2) AND G(i*4+1)) OR (P(i*4+2) AND P(i*4+1) AND G(i*4+0)) OR (P(i*4+2) AND P(i*4+1) AND P(i*4+0) AND C(i*4+0));

C(i*4+4)  := G(i*4+3) OR (P(i*4+3) AND G(i*4+2)) OR (P(i*4+3) AND P(i*4+2) AND G(i*4+1)) OR (P(i*4+3) AND P(i*4+2) AND P(i*4+1) AND G(i*4+0)) OR (P(i*4+3) AND P(i*4+2) AND P(i*4+1) AND P(i*4+0) AND C(i*4+0));

End Loop;

For i in 0 to N-1 Loop

Sum(i) := P(i) XOR C(i);

End Loop;

Sum(l'length) := C(l'length);

Return Sum;

End "+";

Function 	"-" ( l,r : Bit_Vector ) RETURN Bit_vector IS

Variable Sum: Bit_Vector(l'length downto 0);

Variable P, G: Bit_Vector(l'length-1 downto 0);

Variable C: Bit_Vector(l'length downto 0);

Begin

C(0) := '1';

For i in 0 to N-1 Loop

P(i) := l(i) XOR NOT r(i);

G(i) := l(i) AND NOT r(i);

End Loop;

For i in 0 to (N/4)-1 Loop

C(i*4+1)  := G(i*4+0) OR (P(i*4+0) AND C(i*4+0));

C(i*4+2)  := G(i*4+1) OR (P(i*4+1) AND G(i*4+0)) OR (P(i*4+1) AND P(i*4+0) AND C(i*4+0));

C(i*4+3)  := G(i*4+2) OR (P(i*4+2) AND G(i*4+1)) OR (P(i*4+2) AND P(i*4+1) AND G(i*4+0)) OR (P(i*4+2) AND P(i*4+1) AND P(i*4+0) AND C(i*4+0));

C(i*4+4)  := G(i*4+3) OR (P(i*4+3) AND G(i*4+2)) OR (P(i*4+3) AND P(i*4+2) AND G(i*4+1)) OR (P(i*4+3) AND P(i*4+2) AND P(i*4+1) AND G(i*4+0)) OR (P(i*4+3) AND P(i*4+2) AND P(i*4+1) AND P(i*4+0) AND C(i*4+0));

End Loop;

For i in 0 to N-1 Loop

Sum(i) := P(i) XOR C(i);

End Loop;

Sum(l'length) := C(l'length);

Return Sum;

End "-";

## Synthesize the modeled ALU in (viii) using Xilinx Project Navigator and report on the total equivalent gate count for design after mapping and the longest delay in the design based on Post-Map static timing report. Compare the gate count and maximum delay obtained with that obtained in (vii). What are your observations and conclusions?

Total equivalent gate= 528.

Longest delay in the design= 12.970ns.

The obtained area is slightly more than the ripple carry adder and less than the first ALU implementation. However, the delay obtained is the largest while it should be less than the RCA ALU. This is due to the mapping process in FPGAs.