COE 405, Term 122

Design & Modeling of Digital Systems

HW# 3   Solution

Due date: Saturday, March 16

# The block diagram below shows the datapath and controller for a machine that transfers two 4-bit signed numbers in 2’s complement representation into registers AR and BR, divides the number in AR by 2 and transfers the result to register CR if the number in AR is negative, multiplies the number in BR by 2 and transfers the result to register CR if the number in AR is positive but non-zero, and if the number in AR is zero, clears register CR to 0.

## Develop an ASMD chart for the machine.

## Show the design of the data-path and control unit of the machine.

Data Path:

Control Unit:

| C.S. | Input | N.S. | Output |
| --- | --- | --- | --- |
|  | start | AR_gt_0 | AR_lt_0 |  | Done | LD_AR_BR | Div_AR_x2 | Mul_AR_x2 | Clr_CR |
| S0 | 0 | x | x | S0 | 1 | 0 | 0 | 0 | 0 |
| S0 | 1 | x | x | S1 | 1 | 1 | 0 | 0 | 0 |
| S1 | x | 0 | 1 | S0 | 0 | 0 | 1 | 0 | 0 |
| S1 | x | 1 | 0 | S0 | 0 | 0 | 0 | 1 | 0 |
| S1 | x | 0 | 0 | S0 | 0 | 0 | 0 | 0 | 1 |

We assume the state assignment S0=0 and S1=1.

## Implement the machine and verify its correct functionality by simulation.

Silmulation Results:

Simulation results above test the three cases and demonstrate correct operation of the circuit.

# It is required to design an unsigned 4-bit sequential multiplier. The multiplier is assumed to have an 8-bit register to hold the result, a 4-bit register to hold the multiplicand and a 3-bit counter. When reset is 1, the multiplicand, the product and counter registers are reset. When operation is started, the multiplicand register is loaded with word1 while the least significant 4-bits of the product are loaded with word2.  The block diagram and the ASMD chart of the sequential multiplier are given below. Ready signals that the unit is ready to accept a command to multiply. If word1 or word2 are 0, Empty is set to 1. Flush loads the product with 0. C_is_mx is set when the counter is equal to 3. P0 is the least significant bit of the product i.e. product[0].

## Show the design of the data-path and control unit of the 4-bit sequential multiplier.

Data Path:

Control Unit:

| C.S. | Input | N.S. | Output |
| --- | --- | --- | --- |
|  | Start | Empty | P0 | c_is_max |  | Ready | Flush | Load_words | Shift | Add_shift |
| S_idle | 0 | x | x | X | S_idle | 1 | 0 | 0 | 0 | 0 |
| S_idle | 1 | 1 | x | X | S_idle | 1 | 1 | 0 | 0 | 0 |
| S_idle | 1 | 0 | x | x | S_running | 1 | 0 | 1 | 0 | 0 |
| S_running | x | x | 0 | 0 | S_running | 0 | 0 | 0 | 1 | 0 |
| S_running | x | x | 0 | 1 | S_idle | 0 | 0 | 0 | 1 | 0 |
| S_running | x | x | 1 | 0 | S_running | 0 | 0 | 0 | 0 | 1 |
| S_running | x | x | 1 | 1 | S_idle | 0 | 0 | 0 | 0 | 1 |

We assume the state assignment S_idle =0 and S_running =1.

## Implement the machine and verify its correct functionality by simulation.

As shown above multiplying 4x5 produces the correct result of 20=’h14.

Also, multiplying 10*6=60=’h3C.