COE 405, Term 131

Design & Modeling of Digital Systems

HW# 3 Solution

Due date: Tuesday, Nov. 5

# It is required to design a circuit that computes the results of election and determines the winner. It is assumed that there are four members competing in the election with the following codes: Member 1: 00, Member 2: 01, Member 3: 10, and Member 4: 11.Assume that the number of votes to be counted will be given to the circuit when a Start input is set. Assume for simplicity that the maximum number of votes to be counted is 63. Assume that votes will be given to the circuit one vote at a time before the rising edge of each clock cycle. Once the circuit finishes computation, it will assert a Done signal and will generate a 2-bit output indicating the code of the winner. In case there is a tie, a Tie signal is set to 1.

## Develop an ASMD chart for the circuit.

## Show the design of the data-path and control unit of the circuit.

Block Diagram:

Data Path Unit:

Control Unit:

| C.S. | Input | N.S. | Output |
| --- | --- | --- | --- |
|  | Start | Data[1] | Data[0] | VCEZ |  | Load | INC1 | INC2 | INC3 | INC4 | Done |
| S0 | 0 | x | x | X | S0 | 0 | 0 | 0 | 0 | 0 | 0 |
| S0 | 1 | x | x | X | S1 | 1 | 0 | 0 | 0 | 0 | 0 |
| S1 | x | 0 | 0 | 0 | S1 | 0 | 1 | 0 | 0 | 0 | 0 |
| S1 | x | 0 | 1 | 0 | S1 | 0 | 0 | 1 | 0 | 0 | 0 |
| S1 | x | 1 | 0 | 0 | S1 | 0 | 0 | 0 | 1 | 0 | 0 |
| S1 | x | 1 | 1 | 0 | S1 | 0 | 0 | 0 | 0 | 1 | 0 |
| S1 | x | x | x | 1 | S0 | 0 | 0 | 0 | 0 | 0 | 1 |

State Assignment: S0=0, S1=1.

## Implement the circuit and verify its correct functionality by simulation.

The simulation waveforms given below show clearly that the circuit works correctly:

In the first simulation run, the number of votes is 7 and the votes applied are: 0, 1, 2, 3, 3, 1, 1. The winner is member 1.

In the second simulation run, the number of votes is 6 and the votes applied are: 2, 1, 2, 1, 3, 0. There is a tie between member 1 and member 2.