COE 405							Dr. Aiman El-Maleh

HW#4 Solution

Q 5.15

Package HW4 is

COMPONENT p1 PORT (in1: IN BIT; out1: BUFFER BIT); END COMPONENT ;

COMPONENT p2 PORT (in1,in2: IN BIT;out1: BUFFER BIT);END COMPONENT;

component counter port (en, clk: in bit; q: buffer bit; co: buffer bit); end component;

component MSJK port (j,k, c: in bit; q : buffer bit ; q_bar: buffer bit); end component;

component myand2 port(in1,in2: in bit; out1: buffer bit); end component;

END HW4;

==========

package mygates is

component mynand2 	port (in1, in2 : In BIT; out1 : BUFFER BIT); end component;

component myand2 	port (in1, in2 : In BIT; out1 : BUFFER BIT); end component;

component myinv 	port (in1  : In BIT; out1 : BUFFER BIT); end component;

END mygates;

==========

Entity mynand2 is

port ( in1, in2 : In Bit; out1 : BUFFER bit);

End mynand2;

Entity myand2 is

port ( in1, in2 : In Bit; out1 : BUFFER bit);

End myand2;

Entity myinv is

port ( in1 : In BIT; out1 : BUFFER BIT);

END myinv;

Architecture fast_single_delay OF mynand2 is

begin

out1 <= in1 NAND in2 AFTER 3 NS;

END fast_single_delay;

Architecture single_delay OF myinv is

begin

out1 <= NOT in1 AFTER 5 ns;

END single_delay;

Architecture single_delay OF myand2 is

begin

out1 <= in1 AND in2 AFTER 5 NS;

END single_delay;

Architecture single_delay OF mynand2 is

begin

out1 <= in1 NAND in2 AFTER 5 NS;

END single_delay;

entity MSJK is

port (J    : in BIT;

K    : in BIT;

C  : in BIT;

Q  : BUFFER BIT;

Q_BAR : BUFFER BIT);

end MSJK;

Use work.mygates.all;

Use work.HW4.all;

Architecture Struct of MSJK is

FOR ALL : p1 USE ENTITY WORK.myinv;

FOR a1,a2 : p2 USE ENTITY WORK.myand2(single_delay);

FOR n1,n2,n3,n5,n6,n7 : p2 USE ENTITY WORK.mynand2(fast_single_delay);

FOR n4,n8 : p2 USE ENTITY WORK.mynand2(single_delay);

signal a1out, a2out, i1out, n1out, n2out, n3out, n4out, n5out, n6out : BIT;

begin

a1 : p2 port map ( Q_BAR, J, a1out);

a2 : p2 port map ( K, Q, a2out);

i1 : P1 port map ( C, i1out);

n1 : p2 port map (a1out, C, n1out);

n2 : p2 port map (C, a2out, n2out);

n3 : p2 port map (n1out, n4out, n3out);

n4 : p2 port map (n3out, n2out, n4out);

n5 : p2 port map (n3out, i1out, n5out);

n6 : p2 port map (n4out, i1out, n6out);

n7 : p2 port map (n5out, Q_BAR, Q);

n8 : p2 port map (Q, n6out, Q_BAR);

end struct;

Q 5.17

entity function_f is port (a, b, c, d, e: in bit ; f:out bit);

end function_f;

architecture configurable of function_f is

component n1 port (w: in bit; z: out bit); end component;

component n2 port (w, x: in bit; z: out bit); end component;

component n3 port (w, x, y: in bit; z: out bit); end component;

for all: n1 use entity work.nand3(single_delay) port map

(w,w,w,z);

for all: n2 use entity work.nand3(single_delay) port map

(w,w,x,z);

for all: n3 use entity work.nand3(single_delay) port map

(w,x,y,z);

signal i1, i2, i3, i4: bit;

begin

g0: n1 port map (d, i1);

g1: n1 port map (e, i2);

g2: n2 port map (i1, c, i3);

g3: n2 port map (a, b, i4);

g4: n3 port map (i2, i3, i4, f);

end configurable;

Q 5.20

Package HW4 is

COMPONENT p1 PORT (in1: IN BIT; out1: BUFFER BIT); END COMPONENT ;

COMPONENT p2 PORT (in1,in2: IN BIT;out1: BUFFER BIT);END COMPONENT;

component counter port (en, clk: in bit; q: buffer bit; co: buffer bit); end component;

component MSJK port (j,k, c: in bit; q : buffer bit ; q_bar: buffer bit); end component;

component myand2 port(in1,in2: in bit; out1: buffer bit); end component;

END HW4;

===========

entity counter is

port (en, clk: in bit; q: buffer bit; co: buffer bit);

end counter;

USE WORK.HW4.all;

architecture struct of counter is

FOR ALL : MSJK USE ENTITY WORK.MSJK;

FOR ALL : Myand2 USE ENTITY WORK.myand2(single_delay);

signal q_bar: bit;

begin

jk: MSJK port map (en, en, clk, q, q_bar);

anding: myand2 port map (q, en, co);

end struct;

entity counter8 is

port (en, clk: in bit; q : buffer bit_vector(7 downto 0); cout: buffer bit);

end counter8;

USE WORK.HW4.all;

architecture struct of counter8 is

For all : counter USE ENTITY WORK.counter;

signal middle : bit_vector(6 downto 0);

constant n: INTEGER := 8;

begin

ccount: for i in 0 to 7 generate

one: if i = 0 generate

first: counter port map (en, clk, q(i), middle(i));

end generate;

last: if i = n-1 generate

most: counter port map(middle(i-1), clk, q(i), cout);

end generate;

mid: if i<n-1 and i>0 generate

midl: counter port map(middle(i-1), clk, q(i), middle(i));

end generate;

end generate;

end struct;