COE 405, Term 062

Design & Modeling of Digital Systems

HW# 4   Solution

Due date: Saturday, May12, 2007

# It is required to model an N-bit Serial Multiplier. The VHDL Entity description of the n-bit multiplier is given below:

Entity multiplier is

Generic (n: Positive := 4);

Port(clk: IN std_logic; dataready: IN std_logic; A : IN 	std_logic_vector (n-1 downto 0); B : IN 	std_logic_vector (n-1 downto 0);

busy, done: OUT std_logic; result: OUT 	std_logic_vector ( 2*n-1 downto 0));

End multiplier;

# The circuit receives two n-bit operands when the input dataready becomes 1. This causes the multiplication process to begin and the busy flag to become active. Using the add-shift method, the multiplier takes one or two clock cycles for each bit of the multiplicand.  When the process is completed, done becomes 1 for one clock cycle and busy returns to 0. The circuit receives two operands from its X and Y inputs and produces the result on its 2n-bit result output.

## Develop a behavioral model of the n-bit Serial Multiplier.  Divide your multiplier into a data-path and control unit and model each one separately using behavioral modeling style.

It is possible to model serial multiplier behaviorally without splitting the control unit and data path as shown below:

library ieee;

use ieee.std_logic_1164.all;

use ieee.std_logic_unsigned.all;

Entity multiplier is

Generic (n: Positive := 4);

Port(clk: IN std_logic; dataready: IN std_logic; A : IN 	std_logic_vector (n-1 downto 0); B : IN 	std_logic_vector (n-1 downto 0);

busy, done: OUT std_logic; result: OUT 	std_logic_vector ( 2*n-1 downto 0));

End multiplier;

architecture Behavioral of multiplier is

signal ac1, ac2 : std_logic_vector (n-1 downto 0);

signal extra : std_logic_vector (n downto 0);

begin

process(clk)

variable state : integer range 1 to 5 := 1;

variable count : integer range 0 to n := 0;

begin

if (clk'event and clk = '1') then

case state is

when 1 =>

count := 0;

extra <= (others => '0');

ac1 <= A; ac2 <= B;

done <= '0';

if dataready = '1' then

state := state + 1;

end if;

when 2 =>

busy <= '1';

if ac1(0) = '1' then

state := 3;

else state := 4;

end if;

when 3 =>

extra <= extra + ('0'&ac2);

state := 4;

when 4 =>

extra <= '0' & extra(n downto 1);

ac1 <= extra(0) & ac1(n-1 downto 1);

count := count + 1;

if count = n then state := 5;

else state := 2;

end if;

when 5 =>

done <= '1';

busy <= '0';

state := 1;

end case;

end if;

end process;

result <= extra(n-1 downto 0)&ac1;

end Behavioral;

Next, we will show separate modeling of the control unit and data path using behavioral modeling as required by the question.

Library IEEE;

use ieee.std_logic_1164.all;

Entity multiplier is

Generic (n: Positive := 8);

Port(clk: IN std_logic; dataready: IN std_logic; A : IN 	std_logic_vector (n-1 downto 0); B : IN 	std_logic_vector (n-1 downto 0);

busy, done: OUT std_logic; result: OUT 	std_logic_vector ( 2*n-1 downto 0));

End multiplier;

Architecture DF of multiplier is

Component DPath_Multiplier

Generic(n: Positive:= 8);

Port(LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Clk: IN std_logic;

CEN, AC1RB: OUT std_logic;

A, B: in std_logic_vector(N-1 DownTo 0);

result: out std_logic_vector(2*n-1 DownTo 0));

End Component;

Component CU_Multiplier

Port(clk, dataready, AC1RB, CEN: IN std_logic ;

LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Busy, Done: OUT std_logic);

End Component;

Signal LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, CEN, AC1RB: std_logic;

Begin

dpu: DPath_Multiplier Generic Map(N) PORT MAP (LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Clk, CEN, AC1RB, A, B, result);

cu: CU_Multiplier  PORT MAP (clk, dataready, AC1RB, CEN, LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Busy, Done);

End;

Library IEEE;

use ieee.std_logic_1164.all;

use ieee.std_logic_unsigned.all;

Entity DPath_Multiplier is

Generic(N: Positive:= 8);

Port(LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Clk: IN std_logic;

CEN, AC1RB: OUT std_logic;

A, B: in std_logic_vector(N-1 DownTo 0);

result: out std_logic_vector(2*N-1 DownTo 0));

End;

Architecture BV of DPath_Multiplier is

Constant LN: Positive:=N;

Signal AC1R, AC2R	: std_logic_vector(N-1 DownTo 0);

Signal ExtraR: std_logic_vector(N DownTo 0);

Signal CounterR, t2: std_logic_vector(LN-1 DownTo 0);

Begin

AC1Reg: Process(clk)

Begin

if (clk'event and clk='0') Then

if (LD_AC1R='1') Then

AC1R <= A;

Elsif (Shift='1') Then

AC1R <= ExtraR(0) & AC1R(N-1 Downto 1);

End if;

end if;

AC1RB <= AC1R(0);

end process;

AC2Reg: Process(clk)

Begin

if (clk'event and clk='0') Then

if (LD_AC2R='1') Then

AC2R <=  B;

end if;

end if;

end process;

ExtraReg: Process(clk)

Begin

if (clk'event and clk='0') Then

if (LD_ExtraR='1') Then

ExtraR <= ExtraR + ('0'&AC2R);

Elsif  (ClearExtraR='1') Then

ExtraR <=(N Downto 0 => '0');

Elsif (Shift='1') Then

ExtraR <= ('0' & ExtraR(N Downto 1));

End if;

end if;

end process;

CounterReg: Process(clk)

Begin

if (clk'event and clk='0') Then

t2 <= (LN-2 Downto 0 =>'0')&'1';

if (INC='1') Then

CounterR <=  CounterR + t2;

elsif (CLRC='1' ) Then

CounterR <= (LN-1 Downto 0 => '0');

end if;

end if;

if (CounterR=N-1) Then

CEN <= '1' ;

else

CEN <= '0';

end if;

end process;

result <= ExtraR(N-1 downto 0) & AC1R;

End  BV;

Library IEEE;

use ieee.std_logic_1164.all;

Entity CU_Multiplier is

Port(clk, dataready, AC1RB, CEN: IN std_logic ;

LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Busy, Done: OUT std_logic :='0');

End;

Architecture BV of CU_Multiplier is

Type States is (s1, s2, s3, s4, s5);

Signal PS, NS : States;

Begin

reg: Process(Clk)

Begin

IF (Clk'EVENT and Clk = '1')  Then

PS <= NS;

End IF;

End Process;

Transitions: Process(PS, dataready, AC1RB, CEN)

Begin

CASE PS is

when  s1  =>

IF dataready = '1' Then NS <= s2;

else NS <= s1; End IF;

when  s2  =>

IF AC1RB = '1' Then NS <= s3;

else NS <= s4; End IF;

when  s3  =>

NS <= s4;

when  s4  =>

IF CEN = '1' Then NS <= s5;

else NS <= s2; End IF;

when  s5  =>

NS <= s1;

End CASE;

End Process;

LD_AC1R  <= '1' when PS= s1 else '0';

LD_AC2R  <= '1' when PS= s1 else '0';

ClearExtraR <= '1' when PS= s1 else '0';

CLRC <= '1' when PS= s1 else '0';

LD_ExtraR  <= '1' when PS= s3 else '0';

Shift  <= '1' when PS= s4 else '0';

INC  <= '1' when PS= s4 else '0';

Busy <= '1' when PS=s2 or PS=s3 or PS=s4 else '0';

Done <= '1' when PS=s5 else '0';

End  BV;

## Write a test bench for testing the 4-bit Serial Multiplier assuming that the input arguments are read from an input file and that the output will be stored in an output file. Use TEXTIO package for this purpose. Apply the following values for testing the correct operation of a 4-bit Serial Multiplier:

| Input A | Input B |
| --- | --- |
| 5 | 2 |
| 2 | 2 |
| 7 | 0 |
| 0 | 7 |
| 15 | 10 |
| 10 | 15 |
| 15 | 15 |
| 15 | 1 |
| 1 | 15 |
| 15 | 2 |
| 15 | 4 |
| 15 | 8 |

The output should be stored in the output file using the following format:

Input A     Input B     	Result

5	     2		5*2=10

The following test bench was developed and used to verify the correct functionality of the behavioral multiplier which produced the output given below:

Library IEEE;

use ieee.std_logic_1164.all;

USE STD.TEXTIO.ALL;

Entity multiplier_test is

End;

Architecture Test of multiplier_test is

Component multiplier

Generic (n: Positive := 4);

Port(clk: IN std_logic; dataready: IN std_logic; A : IN std_logic_vector (n-1 downto 0);

B : IN 	std_logic_vector (n-1 downto 0);

busy, done: OUT std_logic; result: OUT 	std_logic_vector ( 2*n-1 downto 0));

End Component;

Constant N: Positive :=4;

Constant K: Positive :=30;

Constant Period: Time := 100 ns;

TYPE Integers IS ARRAY (NATURAL RANGE <>) of INTEGER;

Procedure Int2Bin (Int: IN Integer; Bin : OUT std_logic_vector)  IS

Variable Tmp: Integer;

Constant size: Natural := Bin'length;

Begin

Tmp := Int;

if (Tmp < 0) Then

Tmp :=2**size+Tmp;

End If;

For I IN 0 To (Bin'Length - 1) Loop

If ( Tmp MOD 2 = 1) Then

Bin(I) := '1';

Else Bin(I) := '0';

End If;

Tmp := Tmp / 2;

End Loop;

End Int2Bin;

function Bin2Int(Bin: std_logic_vector) return integer is

variable SUM: INTEGER:=0;

begin

For I IN 0 To (Bin'Length - 1) Loop

if Bin(I)='1' then

SUM := SUM + (2**I);

end if;

End Loop;

return SUM;

end Bin2Int;

Signal clk, dataready, done, busy: std_logic :='0';

Signal A, B: std_logic_vector(N-1 Downto 0);

Signal Result: std_logic_vector(2*N-1 Downto 0);

Signal First, Second: Integers(0 to K-1);

Begin

Process

File Infile : Text IS IN "mul_input.txt";

Variable My_Line : Line;

Variable val: Integer;

File outFile: Text IS OUT "mul_output.txt";

Variable write_line: Line;

Variable Str: String(1 to 24);

Variable Str2: String(1 to 42);

Variable i,j: integer :=0;

Variable Buf: std_logic_vector(N-1 Downto 0);

Begin

While Not ( Endfile(Infile) )  Loop

Readline( Infile, My_Line);  -- read a line from the input file

Read( My_Line, val);	         -- read A value from the line

First(i)<= val;

Read( My_Line, val);	         -- read B value from the line

Second(i)<= val;

i := i + 1;

End Loop;

wait for 0 ns;

j:=0;

Str :="Input A"&ht&ht&"Input B"&ht&ht&"Result";

Write(write_line,Str);

Writeline(outFile, write_line);

Str2 :="------------------------------------------";

Write(write_line,Str2);

Writeline(outFile, write_line);

while (j < i) loop

wait for period;

if busy='1' Then wait until busy='0'; end if;

dataready <= '1';

Int2Bin (First(j), Buf);

A<=Transport Buf ;

Int2Bin (Second(j), Buf);

B<=Transport Buf ;

wait for 2*period;

dataready <= '0';

if done='0' Then wait until done='1';	end if;

Write(write_line, First(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, Second(j));

Write(write_line,ht);

Write(write_line,ht);

Write(write_line, First(j));

Write(write_line, '*');

Write(write_line, Second(j));

Write(write_line, '=');

Write(write_line, Bin2Int(result));

Writeline(outFile, write_line);

j := j + 1;

wait for 3*period;

End loop;

wait;

End Process;

clk <= not clk after period;

CUT: multiplier Generic Map (N) Port Map (clk, dataready, A, B, busy, done, result);

End;

Input A		Input B		Result

---------------------------------------------------------

5		2		5*2=10

2		2		2*2=4

7		0		7*0=0

0		7		0*7=0

15		10		15*10=150

10		15		10*15=150

15		15		15*15=225

15		1		15*1=15

1		15		1*15=15

15		2		15*2=30

15		4		15*4=60

15		8		15*8=120

## Synthesize the modeled Serial Multiplier in (i) using Xilinx Project Navigator and report on the total equivalent gate count for design after mapping and the longest delay in the design based on Post-Map static timing report.

Both models given in part (i) are synthesizable. The results of the synthesis of the required model are shown below:

Total equivalent gate count for design:  358

Longest delay is 8.165 ns.

## Develop a dataflow model of the n-bit Serial Multiplier.  Divide your multiplier into a data-path and control unit and model each one separately using dataflow modeling style.

Library IEEE;

use ieee.std_logic_1164.all;

Entity multiplier is

Generic (n: Positive := 8);

Port(clk: IN std_logic; dataready: IN std_logic; A : IN 	std_logic_vector (n-1 downto 0); B : IN 	std_logic_vector (n-1 downto 0);

busy, done: OUT std_logic; result: OUT 	std_logic_vector ( 2*n-1 downto 0));

End multiplier;

Architecture DF of multiplier is

Component DPath_Multiplier

Generic(n: Positive:= 8);

Port(LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Clk: IN std_logic;

CEN, AC1RB: OUT std_logic;

A, B: in std_logic_vector(N-1 DownTo 0);

result: out std_logic_vector(2*n-1 DownTo 0));

End Component;

Component CU_Multiplier

Port(clk, dataready, AC1RB, CEN: IN std_logic ;

LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Busy, Done: OUT std_logic);

End Component;

Signal LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, CEN, AC1RB: std_logic;

Begin

dpu: DPath_Multiplier Generic Map(N) PORT MAP (LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Clk, CEN, AC1RB, A, B, result);

cu: CU_Multiplier  PORT MAP (clk, dataready, AC1RB, CEN, LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Busy, Done);

End;

Library IEEE;

use ieee.std_logic_1164.all;

use ieee.std_logic_unsigned.all;

Entity DPath_Multiplier is

Generic(N: Positive:= 8);

Port(LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Clk: IN std_logic;

CEN, AC1RB: OUT std_logic;

A, B: in std_logic_vector(N-1 DownTo 0);

result: out std_logic_vector(2*N-1 DownTo 0));

End;

Architecture DF of DPath_Multiplier is

Constant LN: Positive:=N;

Signal AC1R, AC2R	: std_logic_vector(N-1 DownTo 0);

Signal ExtraR, t1	: std_logic_vector(N DownTo 0);

Signal CounterR, t2: std_logic_vector(LN-1 DownTo 0);

Signal AC1RE,AC2RE,ExtraRE, CounterRE : Boolean:=False ;

Begin

AC1RE <= LD_AC1R='1' or Shift='1' ;

AC2RE <= LD_AC2R='1';

ExtraRE <= LD_ExtraR='1' or ClearExtraR='1' or Shift='1' ;

CounterRE <= INC='1' or CLRC='1';

edge: Block(Clk='0' and not Clk'Stable)

Begin

AC1Reg: Block(AC1RE and Guard)

Begin

AC1R <= Guarded A when LD_AC1R='1' Else ExtraR(0) & AC1R(N-1 Downto 1);

AC1RB <= AC1R(0);

end Block AC1Reg;

AC2Reg: Block(AC2RE and Guard)

Begin

AC2R <= Guarded B;

end Block AC2Reg;

ExtraReg: Block(ExtraRE and Guard)

Begin

t1 <= '0' & ExtraR(N Downto 1);

ExtraR <= Guarded ExtraR+ ('0'&AC2R) when LD_ExtraR='1' Else (N Downto 0 => '0')when ClearExtraR='1' Else t1;

end Block ExtraReg;

CounterReg: Block(CounterRE and Guard)

Begin

t2 <= (LN-2 Downto 0 =>'0')&'1';

CounterR <= Guarded CounterR + t2 when INC='1' else (LN-1 Downto 0 => '0');

CEN <= '1' when CounterR=N else '0';

end Block CounterReg;

End Block edge;

result <= ExtraR(N-1 downto 0) & AC1R;

End  DF;

Library IEEE;

use ieee.std_logic_1164.all;

Entity CU_Multiplier is

Port(clk, dataready, AC1RB, CEN: IN std_logic ;

LD_AC1R, LD_AC2R, ClearExtraR, LD_ExtraR, Shift, INC, CLRC, Busy, Done: OUT std_logic :='0');

End;

Architecture DF of CU_Multiplier is

Type States is (s1, s2, s3, s4, s5);

Type State_Vector is Array (Natural Range <>) of States;

Function RF(V:State_Vector) Return States is

Begin

Return V(V'Left);

end RF;

Signal PS:  RF States Register := s1;

Begin

edge: Block(Clk='1'  and  not Clk'Stable)

Begin

S1B: Block(PS= s1 and Guard)

Begin

PS <= Guarded s2 when dataready='1' Else  s1;

end Block S1B;

S2B: Block(PS= s2 and Guard)

Begin

PS <= Guarded s3 when AC1RB='1' Else  s4;

end Block S2B;

S3B: Block(PS= s3 and Guard)

Begin

PS <= Guarded s4;

end Block S3B;

S4B: Block(PS= s4 and Guard)

Begin

PS <= Guarded s5 when CEN='1' Else  s2;

end Block S4B;

S5B: Block(PS= s5 and Guard)

Begin

PS <= Guarded s1;

end Block S5b;

End Block edge;

LD_AC1R  <= '1' when PS= s1 else '0';

LD_AC2R  <= '1' when PS= s1 else '0';

ClearExtraR <= '1' when PS= s1 else '0';

CLRC <= '1' when PS= s1 else '0';

LD_ExtraR  <= '1' when PS= s3 else '0';

Shift  <= '1' when PS= s4 else '0';

INC  <= '1' when PS= s4 else '0';

Busy <= '1' when PS=s2 or PS=s3 or PS=s4 else '0';

Done <= '1' when PS=s5 else '0';

End  DF;

## Verify the correct functionality of your dataflow model using the test bench developed in (ii).

Using the same test bench developed in (ii) the correct functionality of the dataflow multiplier is verified and the following output is obtained:

Input A		Input B		Result

-------------------------------------------------------------

5		2		5*2=10

2		2		2*2=4

7		0		7*0=0

0		7		0*7=0

15		10		15*10=150

10		15		10*15=150

15		15		15*15=225

15		1		15*1=15

1		15		1*15=15

15		2		15*2=30

15		4		15*4=60

15		8		15*8=120