COE 405, Term 021

Design & Modeling of Digital Systems

HW# 5

Due date: Monday, Dec. 16, 2002

## Write a function for the carry output of a full-adder.

## Write a function for the sum output of a full adder.

## Using the carry and sum functions, write a functional description of a full-adder. Use an entity declaration with a, b, and ci inputs and s and co outputs. In the functional architecture of this entity, include the necessary functions. Use 21- and 18-ns delays for the sum and carry outputs, respectively.

# 6.5

# Using bin2int and int2bin in the basic_utilities package write a function, inc_bin, that uses a binary input parameter and returns a binary value. The return value is the increment of the input parameter. Define the basic_utitlities package to include bin2int and int2bin and use it.

## Write an entity declaration and an average_delay architecture for an exclusive-OR gate with a tplh of 9 ns and a tphl of 7 ns. The entity declaration should contain generics for the timing parameters with the specified default values.

## Using an XOR gate and 2-input NAND gate, write a gate-level description for a full-adder. Use a configuration specification to use the XOR and 2-input gate with average_delay architecture with generic map aspects to override the default values of the timing parameters of all gates with 11 ns.

## Using an XOR gate and 2-input NAND gate, write a gate-level description for a full-adder. Write a configuration declaration on top of the full-adder to use the XOR and 2-input gate with average_delay architecture with generic map aspects to override the default values of the timing parameters of all gates with 11 ns.

## Use generate statements to describe an 8-bit adder using the full-adder described in (iii). Write a configuration declaration on top of this adder to use the XOR and 2-input NAND gate with average_delay architecture. Using this configuration declaration, specify tplh and tphl of 10 ns and 11 ns for NAND2 and 11 ns and 13 ns for XOR.