COE 405, Term 152

Design & Modeling of Digital Systems

HW# 5   Solution

Due date: Thursday, April 7

# It is required to design a circuit that receives two 4-bit signed numbers in 2's complement representation A=A3A2A1A0, B=B3B2B1B0 and produces 5-bit output C= C4C3C2C1C0. The circuit implements the following functions based on the values of the three selection inputs: S1, S1 and S0.

| S2 S1 S0 | Function |
| --- | --- |
| 0 0 0 | C = A + B |
| 0 0 1 | C = A - B |
| 0 1 0 | C = A + 1 |
| 0 1 1 | C = A + 2 |
| 1 0 0 | C = A - 1 |
| 1 0 1 | C = A - 2 |
| 1 1 0 | C = 2A |
| 1 1 1 | C = 2B |

# Show the block diagram design of your circuit using MSI components like Adder, Multiplexor, as needed. Use only one adder in your solution.

# Model your design in Verilog by modeling each component separately i.e. adder, MUX, etc. and then instantiating these components to model your circuit.

module Ass3 (input [3:0] A, B, input s2, s1, s0, output [4:0]C);

wire sel;

wire [3:0] T1, T2, T3;

assign sel = s2 & s1 & s0;

mux2x1 #(4) M1 (A, B, sel, T1);

mux2x1 #(4) M2 (B, ~B, s0, T2);

mux4x1 #(4) M3 (T2, 4'b0001, 4'b1110, T1, s2, s1, T3);

assign Cin = s0 & ~s2 | s2 & ~s1 & ~s0;

adder  #(5) M4 (Cout, C, {T1[3], T1}, {T3[3], T3}, Cin);

endmodule

module mux4x1 #(parameter n = 1)(input  [n-1:0] a, b, c, d, input s1, s0,  output reg [n-1:0] y);

always@(s1, s0, a, b, c, d) begin

case ({s1, s0})

2'b00: y=a;

2'b01: y=b;

2'b10: y=c;

2'b11: y=d;

endcase

end

endmodule

module mux2x1 #(parameter n = 1)(input  [n-1:0] a, b, input select,  output [n-1:0] c);

assign c = (select ? b : a);

endmodule

module adder #(parameter n = 4)

(output cout, output [n-1:0] sum, input [n-1:0] a, b, input cin);

assign {cout, sum} = a + b + cin;

endmodule

# Write a Verilog test bench to test your design and verify its correctness by simulation. For each function, test at least 2 input combinations of your choice to demonstrate correct functionality. Show snapshots of your simulation to demonstrate its correctness.

module Ass3_Test();

wire [4:0] C;

reg [3:0] A, B;

reg [2:0]  S;

Ass3 M1 (A, B, S[2], S[1], S[0], C);

initial begin

A = 7; B = 3; S = 0;

#10 S = 1;

#10 S = 2;

#10 S = 3;

#10 S = 4;

#10 S = 5;

#10 S = 6;

#10 S = 7;

#10 A = -8; B = -7; S = 0;

#10 S = 1;

#10 S = 2;

#10 S = 3;

#10 S = 4;

#10 S = 5;

#10 S = 6;

#10 S = 7;

end

endmodule

Simulation Results:

# Write another Verilog model that models the circuit behaviorally. Make your model parametrizable where n is the inputs width in bits.

module Ass3Behav  #(parameter n=4)(input [n-1:0] A, B, input s2, s1, s0, output reg[n:0]C);

wire [n:0] A5, B5;

assign A5={A[n-1], A};

assign B5={B[n-1], B};

always @(s2, s1, s0, A, B) begin

case ({s2,s1,s0})

3'b000:    C = A5 + B5;

3'b001:    C = A5 - B5;

3'b010:    C = A5 + 1;

3'b011:    C = A5 + 2;

3'b100:    C = A5 - 1;

3'b101:    C = A5 - 2;

3'b110:    C = A5 + A5;  // or 2*A5

3'b111:    C = B5 + B5;  // or 2*B5

endcase

end

endmodule

# Use the test bench you developed in (iii) to test the correctness of your behavioral model. Show snapshots of your simulation to demonstrate its correctness.

module Ass3_Testb();

wire [4:0] C;

reg [3:0] A, B;

reg [2:0]  S;

Ass3Behav M1 (A, B, S[2], S[1], S[0], C);

initial begin

A = 7; B = 3; S = 0;

#10 S = 1;

#10 S = 2;

#10 S = 3;

#10 S = 4;

#10 S = 5;

#10 S = 6;

#10 S = 7;

#10 A = -8; B = -7; S = 0;

#10 S = 1;

#10 S = 2;

#10 S = 3;

#10 S = 4;

#10 S = 5;

#10 S = 6;

#10 S = 7;

end

endmodule

Simulation Results:

# Implement your behavioral model on FPGA and demonstrate its correct functionality for n=2. Include a link for a video snapshot to demonstrate correct functionality of your circuit on FPGA.