COE 405, Term 152

Design & Modeling of Digital Systems

HW# 7

Due date: Sunday, May 1

# Consider the logic network below with inputs {a, b, c, d, e} and output {k}:

# Assume that the delay of the inverter gate is 1 and that the delay of the 2-input NAND gate is 2.  Also, assume that the input data-ready times are zero except for input a, which is equal to 2.

## Compute the data ready times and slacks for all vertices in the network.

## Determine the topological critical path.

## Suggest an implementation of the function k using only inverters and 2-input NAND gates to reduce the delay of the circuit to the minimum possible and determine the maximum propagation delay in the optimized circuit. Has the area been affected?

# It is required to design a circuit to compute the equation Y=A+B-C-D, where A, B, C and D are N-bit inputs. Assume that inputs are available only during the first cycle when a START input is asserted.  Assume that a DONE signal will be set when the result is ready and the result will remain held until the next Start operation.

## Show a schedule of the operations with minimum latency (i.e., clock cycles) assuming that the clock cycle is limited by the time for performing one addition/subtraction operation. Store the output Y in a register.

## Show the Data Path design of your circuit indicating all the control signals and the used adder/subtractor sizes.

## Show the ASMD diagram of your control unit.

## Write the necessary Verilog modules to module the data path unit, control unit and the overall circuit.

## Write a test bench to test the correct operation of your circuit. Include simulation snapshots.

## Implement your circuit on FPGA assuming N=2 bits. Include a link for a video snapshot to demonstrate correct functionality of your circuit.

This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a word file that contains the following items:

#### Your name and ID

#### Assignment number

#### Problem statement

#### Your solution

#### Include snapshots of simulation output to illustrate the correctness of your models.