Name:									Id#

COE 405, Term 122

Design & Modeling of Digital Systems

Quiz# 1

Date: Monday, Feb. 18, 2013

# Consider the two functions:   and

# Compute the expansion of  and  using the Orthonormal Basis {(1=, (2=, (3=, (4=}.

# Compute the function.

# It is required to model a 4-bit comparator that compares two 4-bit numbers A=A3A2A1A0 and B=B3B2B1B0, and produces two outputs GT and LT. If A>B, then the output signal GT is set to 1 and LT is set to 0. If A<B, then the output signal LT is set to 1, and GT is set to 0. Otherwise both signals will be set to 0, which indicates that the two numbers are equal (i.e. A=B). The 4-bit comparator circuit can be designed in a modular way as shown below:

## Derive the truth table for a 1-bit magnitude comparator.

## Find the simplified equations for the outputs of a 1-bit magnitude comparator.

# Text boxes

LT0

GT0

LT1

GT1

LT

GT

B0

A0

LT1

GT1

LT2

GT2

LT2

GT2

LT3

GT3

LT3

GT3

LT4

GT4

0

0

B1

A1

B2

A2

B3

A3