Name: KEY									Id#

COE 405, Term 131

Design & Modeling of Digital Systems

Quiz# 1

Date: Tuesday, Oct. 1, 2013

# Consider the two functions:   and

# Compute the expansion of  and  using the Orthonormal Basis {(1=, (2=, (3=, (4=}.

# Compute the function.

# It is required to design a combinational circuit that computes the equation Y=3*X+2, where X is an n-bit unsigned number.

## Design the circuit as a modular circuit where each module receives a single bit of the input, Xi.

## Derive the truth table of your 1-bit module in (i).

## Derive minimized two-level sum-of-product equations for your 1-bit module circuit.