Name:									Id#

COE 405, Term 131

Design & Modeling of Digital Systems

Quiz# 2

Date: Thursday, October 24, 2013

# It is required to design a sequential circuit that has a single input X and a single output Y. The circuit receives an unsigned number serially through the input X from the least significant bit (LSB) to the most significant bit (MSB), and computes the equation Y=3*X+2 and generates the output serially from the least significant bit to the most significant bit. The circuit has an additional reset input R which resets the circuit into an initial state. The following are examples of input and output data:

Examples:

| Input | X | 0 | 1 | 1 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 0 | 0 | 1 | 0 | 1 |

| Input | X | 1 | 1 | 0 | 0 | 0 |
| --- | --- | --- | --- | --- | --- | --- |
| Output | Y | 1 | 1 | 0 | 1 | 0 |

## Draw the state diagram of the circuit assuming a Mealy model.

# Consider the following state table for an FSM which has a single input X, a single output Z:

| QA | QB | X | QA+ | QB+ | Z |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 1 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 |
| 1 | 0 | 1 | 0 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 0 | 1 | 0 |

Implement the circuit for the FSM using D-FFs with minimal area.

# Consider the given FSM that has 5 states, one input (X) and one output (Z), represented by the following state table:

| Present State | Next State, Z |
| --- | --- |
|  | X=0 | X=1 |
| S0 | S3, 0 | S0, 0 |
| S1 | S4, 0 | S0, 0 |
| S2 | S3, 0 | S1, 0 |
| S3 | S2, 1 | S2, 0 |
| S4 | S2, 1 | S1, 0 |

## Determine the equivalent states.

## Reduce the state table into the minimum number of states and show the reduced state table.

# Text boxes

Output=11

Input=3

LSB

MSB

Output=20

Input=6

MSB

LSB