Name: Key									Id#

COE 405, Term 021

Design & Modeling of Digital Systems

Quiz# 2

Date: Monday, October 21, 2002

# It is required to design a 3-bit register that has the capability to count up, count down, shift left logically, or shift right logically based on a 2-input select. The interface description of the 3-bit register is shown below, where sel determines the operation. When sel=00, the register will count up, when sel=01, it will count down, when sel=10, it will shift left logically, and when sel =11, it will shift right logically. The reset is a synchronous reset and the register is rising-edge triggered.

## Describe an Entity CS3 for the 3-bit register using type BIT and BIT_VECTOR for the interface signals.

Entity CS3 IS

PORT (reset, clk: IN BIT; sel: IN BIT_VECTOR(1 downto 0); C: OUT Bit_Vector(2 Downto 0));

Constant limit: INTEGER :=7;

END CS3 ;

## Model a behavioral Architecture Behave for this 3-bit register.

Architecture Behave OF CS3 IS

Begin

Process(clk)

Variable count: INTEGER := 0;

Begin

IF (clk = '1' AND clk'Event ) THEN

IF reset = '1' THEN 	count := 0;

ELSE

CASE sel is

when "00" => count := count+1;

when "01" => count := count-1;

when "10" => count := count*2;

when "11" => count := count/2;

END case;

END IF;

IF (count > limit) Then count := count-limit-1;

ELSE IF count= -1 Then count := limit; END IF;

END IF;

END IF;

Case count is

when 0 => c <= "000";

when 1 => c <= "001";

when 2 => c <= "010";

when 3 => c <= "011";

when 4 => c <= "100";

when 5 => c <= "101";

when 6 => c <= "110";

when 7 => c <= "111";

when others => c <= "000";

End Case;

END process;

END Behave ;

# Text boxes

clk

Sel1Sel0

reset

C2-C0

3-bit Special Register